## Slide 1: Overview of FIP Issues in the RUC, Verifiable Cost, and other Nodal Market Processes
January 28, 2009
WMS Meeting

## Slide 2: Outline
Review the issues with current language in nodal protocols regarding the gas price index (“FIP”)
Review, section by section, the use of FIP
Discuss whether FIP is appropriate, or should it be modified.
If FIP should be modified, discuss recommended changes.
Discuss next steps.

## Slide 3: What is the Issue?
This presentation was developed after one specific issue regarding FIP came to light. That issue is:
  Current FIP language only recovers a fuel index price. Does not recover other costs of fuel; such as intra-day premiums, transport, swing, imbalance.
    This is especially troublesome for RUC committed units since the gas will typically be purchased at Spot Gas Prices after the market closes.
    Language in the nodal protocols would result in an under-recovery of costs for RUC deployed units in a vast majority of instances.
    Problem is not isolated to RUC units, but more pronounced since the units are forced on for reliability. FIP language also is used prospectively in nodal and that is also an issue.

## Slide 4: Where is FIP Used?
Section 4.4.9.2.3 - Startup Offer and Minimum-Energy Offer Generic Caps
Section 4.4.9.3.3 - Energy Offer Curve Caps for Make-Whole Calculation Purposes
Section 4.4.9.4 - Mitigated Offer Cap and Mitigated Offer Floor
Sections 4.4.11 - System-Wide Offer Caps and Section 4.4.11.1 - Scarcity Pricing Mechanism
Section 5.6.1.1 - Verifiable Startup Costs*
Section 5.6.1.2 - Verifiable Minimum-Energy Costs*
Section 6.6.6.2 - RMR Payment for Energy
Section 7.9.1.3 - Minimum and Maximum Resource Prices

## Slide 5: 4.4.9.2.3 - Startup Offer and Minimum-Energy Offer Generic Caps
Description: This Section sets the startup and minimum-energy offer caps until resources submit verifiable costs.
Protocol excerpt:
  The Resource Category Minimum-Energy Generic Cap is the cost per MWh of energy for a Resource in producing energy up to and including the Resource’s LSL after breaker close, as indicated by a telemetered Resource status of On-Line, according to the following:
    (c) Combined cycle greater than 90 MW = 10 MMBtu/MWh * ((Percentage of FIP * FIP) + (Percentage of FOP * FOP))/100, as specified in Minimum-Energy Offer;…..
Recommendation: No change to FIP language.
Reason: The generic caps were set low to provide incentives for resource owners to submit verifiable costs.

## Slide 6: 4.4.9.3.3 - Energy Offer Curve Caps for Make-Whole Calculation Purposes
Description: FIP is used in 4.4.9.3.3 to calculate the make-whole caps when reimbursing a QSE for allowable energy costs not recovered in energy revenue when the Resource is committed by the DAM or by a RUC.
Protocol excerpt:
  (1) The following Energy Offer Curve Caps must be used for the purpose of Make-Whole Settlements:
    (c) Combined Cycle greater than 90 MW = 9 MMBtu/MWh * ((Percentage of FIP * FIP) + (Percentage of FOP * FOP))/100, as specified in the Energy Offer Curve;
    (d) Combined Cycle less than or equal to 90 MW = 10 MMBtu/MWh * ((Percentage of FIP * FIP) + (Percentage of FOP * FOP))/100, as specified in the Energy Offer Curve Offer;
Recommendation: No change to FIP language.
Reason: 100% fuel price accuracy is not necessary when using the generic heat rates.

## Slide 7: 4.4.9.4 - Mitigated Offer Cap and Mitigated Offer Floor
Description: FIP is used in 4.4.9.4 to calculate the offer caps and floors for resources that are subject to real-time mitigation.
Protocol excerpt:
  (a) For a Generation Resource that commences commercial operation after January 1, 2004, ERCOT shall construct an incremental mitigated offer cap curve (Section 6.5.7.3) such that each point on the Mitigated Offer Cap curve (Cap vs. output level) is the greater of:
    (i)14.5 MMBtu/MWh times the minimum of Fuel Index Price (FIP) or Fuel Oil Price (FOP); or
    (ii) the Resource’s verifiable incremental heat rate (MMBtu/MWh) for the output level multiplied by ((Percentage of FIP * FIP) + (Percentage of FOP * FOP))/100, as specified in the Energy Offer Curve, plus verifiable variable O&M cost ($/MWh) times a multiplier described in (c);
Recommendation: No change to FIP language.
Reason: 100% fuel price accuracy is not necessary when calculating offer caps and floors.

## Slide 8: 4.4.11 - System-Wide Offer Caps and 4.4.11.1 - Scarcity Pricing Mechanism
Description: FIP is used in 4.4.11 and 4.4.11.1 to calculate the low system-wide offer cap (LCAP) and the peaker operating cost (POC) in order to reset the system-wide offer caps if and when the peaker net margin is reached.
Protocol excerpt:
  (a) The LCAP is set on a daily basis at the higher of:
    (i) $500 per MWh for energy and $500 per MW per hour for Ancillary Services; or
    (ii) Fifty times the FIP of the previous Operating Day, expressed in dollars per MWh for energy and dollars per MW per hour for Ancillary Services….;
Recommendation: No change to FIP language.
Reason: 100% fuel price accuracy is not necessary when estimating POC and/or resetting offer caps and floors.

## Slide 9: 5.6.1.1 - Verifiable Startup Costs*
Description: FIP is used in 5.6.1.1 as the fuel price when submitting verifiable startup costs. These costs serve as startup caps for all offers prospectively.
Protocol excerpt:
  The unit-specific verifiable costs for starting a Resource for each cold, intermediate, and hot start condition, as determined using the data submitted under Section 5.6.1, Verifiable Costs, above and the Resource Parameters for the Resource are:
    (a) Actual fuel consumption rate per start (MMBtu/start) multiplied by a resource category generic fuel price (FIP, FOP, or $1.50 per MMBtu, as applicable); and
    (b) Unit-specific verifiable operation and maintenance expenses.
Recommendation: Modify the language to be FIP * 1.X (recommend 1.10).
Reason: FIP does not cover all costs of fuel: Transport, Swing, Imbalance. In addition, fuel Purchased for RUC committed units will be purchased at Spot Gas Prices, normally much higher than day-ahead.

## Slide 10: 5.6.1.2 - Verifiable Minimum-Energy Costs*
Description: FIP is used in 5.6.1.2 as the fuel price when submitting verifiable minimum-energy costs. These costs serve as minimum energy caps for all offers prospectively.
Protocol excerpt:
  The unit-specific verifiable minimum-energy costs for a Resource are:
    (a) Actual fuel cost to operate the unit at LSL; plus
    (b) Variable operation and maintenance expenses; plus
    (c) Nodal implementation surcharges to operate the unit at LSL.
  …For gas-fired units, the actual fuel costs must be calculated using the actual seasonal heat rate (which must be supplied to ERCOT with seasonal heat-rate test data) multiplied by FIP...
Recommendation: Modify the language to be FIP * 1.X (recommend 1.10).
Reason: FIP does not cover all costs of fuel: Transport, Swing, Imbalance. In addition: fuel Purchased for RUC committed units will be purchased at Spot Gas Prices, normally much higher than day-ahead.

## Slide 11: 6.6.6.2 - RMR Payment for Energy
Description: FIP is used in 6.6.6.2 as an approximation of the fuel costs paid for energy produced from RMR units on the initial settlement and settlements prior to True-up. Actual submitted costs are ultimately paid for RMR-produced energy.
Protocol excerpt:
  Payment for energy on the Initial Settlement and settlements executed before True-up and before actual cost data is submitted must be calculated using the estimated input/output curve and startup fuel as specified in the RMR Agreement, the actual energy produced and the Fuel Index Price (FIP). The payment for energy for all other settlements must be based on actual fuel costs for the RMR Unit.
Recommendation: No change to FIP language.
Reason: FIP is only used as an initial estimate. RMR payments are ultimately based on actual submitted fuel costs.

## Slide 12: 7.9.1.3 - Minimum and Maximum Resource Prices
Description: FIP is used in 7.9.1.3 to determine the hedge value of CRRs that source or sink at resources.
Protocol excerpt:
  Minimum Resource Prices for Resources located at source Settlement Points are:
    (d) Combined Cycle greater than 90 MW = FIP * 5 MMBtu/MWh;
    (e) Combined Cycle less than or equal to 90 MW = FIP * 6 MMBtu/MWh;
    (f) Gas -Steam Supercritical Boiler = FIP * 6.5 MMBtu/MWh;
Recommendation: No change to FIP language.
Reason: 100% fuel price accuracy is not necessary when estimating the hedge value of CRRS.

## Slide 13: Summary
Recommendations herein only suggests modifying FIP in two sections of the nodal protocols:
  Section 5.6.1.1 - Verifiable Startup Costs*
  Section 5.6.1.2 - Verifiable Minimum-Energy Costs*
FIP + 10% will better align cost recovery to actual gas prices. FIP alone does not cover costs.
VCWG still reviewing the possibility of utilizing this concept for a simplification of Exceptional Events related to high spot gas during RUC events. To be discussed in next VCWG presentation.
FIP + 10% was chosen because 1) it is similar to wording in current zonal protocols: Section “6.8.1.11(3)(b) - For gas fired Resources, such documentation will not be required if the requested incremental fuel cost is less than one hundred ten percent (110%) of the Fuel Index Price; and 2) similar to other markets (ex: From PJM operating agreement, section 6.4, Offer Price Caps, for reliability services: “The offer price cap shall be one of the amounts specified below… (ii) The incremental operating cost of the generation resource…plus 10% of such costs…
FIP + adder similar to RMR language. RMR is a reliability service (just like RUC but with longer terms), and RMR language provides complete recovery of actual fuel costs.
Language in nodal protocol Section 5.6.1.2 is not technically correct. Actual fuel costs are not recovered if only FIP is allowed.

## Slide 14: Questions???

## Slide 15: Appendix: Section 3 of the Nodal Protocols
RMR units:
Examples of Eligible Costs include the following to the extent they each meet the standard for eligibility: “Reservation and transportation costs associated with firm fuel supplies not recovered under Section 6.6.6.2, RMR Payment for Energy;
Subject to the reductions described in items (2) and (3), the Incentive Factor for RMR Agreements is equal to 10% of the actual Eligible Costs excluding fuel costs incurred by the RMR Unit.
The RMR Unit owner shall provide ERCOT with actual fuel costs on a monthly basis for the RMR Unit in a level of detail sufficient for ERCOT to verify that all fuel costs are actual and appropriate. The estimated fuel payments may include a fuel adder to better approximate expected actual fuel costs. ERCOT shall perform a true-up of the estimated fuel costs using the submitted and verified actual fuel costs for the RMR Unit. Actual cost data must be submitted on time by the Generation Entity for the RMR Unit and then verified by ERCOT so the actual cost data can be reflected in the True-Up Settlement Statement.
Actual fuel costs must be appropriate actual costs attributable to ERCOT’s scheduling and/or deployment of the RMR Unit. Actual fuel costs may include cost of fuel (including the cost of exceeding swing gas contract limits, additional gas demand costs set by fuel supply, or transportation contracts); demand fees, imbalance penalties, transportation charges, and cash out premiums.