## Slide 1
Texas Regional Entity
ROS Presentation
February 12, 2009
TEXAS RE ROS PRESENTATION FEBRUARY 2009
Notes: Texas RE Board Report
<number>

## Slide 2: Topics
Metrics Report
Operations Training Seminar
CIPS Self Certification
Nodal Plan
Load Serving Entity Update
Texas RE ROS Presentation February 2009

## Slide 3: December 2008 ERCOT’s CPS1 Monthly Performance
TRE Compliance Report
February 2009

## Slide 4: Analysis of CPS1 Monthly Performance
Purpose: To maintain Interconnection steady-state frequency within defined limits by balancing real power demand and supply in real-time
CPS1 is one reliability measure of how well the ERCOT region managed the BPS
The measure is based on a rolling 12 month average
ERCOT region’s frequency performance is determined by NERC Control Performance Standard 1 (CPS1)
TRE Compliance Report
February 2009

## Slide 5: Analysis of CPS1 Monthly Performance (cont.)
Seasonal fluctuation is expected
Scores for individual months can be adversely affected by events (such as hurricanes)
A detailed formula can be found in NERC Reliability Standard BAL-001-0a
There was a sharp decrease in September 2008 due to Hurricane Ike and a recovery in October 2008
Recent improvements have been tied to the economic downturn and a reduction in non-conforming loads per ERCOT ISO
TRE Compliance Report
February 2009

## Slide 6: December 2008 SCPS2 Scores for Non-Wind Only QSEs
TRE Compliance Report
February 2009

## Slide 7: December 2008 SCPS2 Scores for Wind Only QSEs
TRE Compliance Report
February 2009
Notes: <number>

## Slide 8: Analysis of December 2008 SCPS2 Scores
This is a schedule focused metric
Calculations are Portfolio Based by QSE
Because of variations in the wind, it is more difficult for wind generators to match their scheduled generation to their actual output
A detailed formula can be found in Protocol 6.10.5.3
4th Straight month that all non-wind only QSEs passed
The wide variation on SCPS2 wind scores for wind only QSEs should be analyzed to determine what is driving the wide variation between QSEs’ performance
  Identify useful wind only metrics
TRE Compliance Report
February 2009

## Slide 9: November 2008 Resource Plan Performance Metrics for Non-Wind Only QSEs
TRE Compliance Report
February 2009
Resource Plan Performance Metric | ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | FW | DK | DE | IP | AP | AO | HA | BY | BC | JA | AY | AM | AR | BR | DF | CI | AD | BJ | BH | JD
Resource Status | - | 100 | 100 | 100 | 99 | 100 | 100 | 100 | 100 | 100 | 98 | 99 | 100 | 100 | 100 | 100 | 100 | 99 | - | 100
LSL as % of HSL | - | 99 | 96 | 100 | 96 | 94 | 93 | 99 | 100 | 100 | 100 | 100 | 99 | 98 | 99 | 84 | - | 99 | - | 99
DA Zonal Schedule | 100 | 99 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 93 | 99 | 100 | 100 | 100 | 100 | - | 100 | 100 | 99
AP Zonal Schedule | - | 99 | 100 | 100 | 100 | 99 | 98 | 100 | 99 | 100 | 95 | 100 | 100 | 99 | 100 | 98 | - | 98 | 98 | 100
Down Bid & Obligation | - | 99 | 97 | 100 | 99 | 99 | 99 | 98 | 99 | 100 | 96 | 90 | 97 | 93 | 94 | 92 | - | 94 | 100 | 96
Total Up AS Scheduled | - | - | 99 | - | 99 | 99 | 100 | 98 | 99 | 100 | 99 | 99 | 100 | 97 | 85 | - | - | 100 | - | 99
Resource Plan Performance Metric | ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | CF | ET | JO | DA | DP | BG | CX | FK | HW | IN | IZ | BX | CC | CD | AC | IE | CQ | EO | IO | FY
Resource Status | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 99 | 100 | 100 | 100 | 100 | 96 | 100 | 99 | 100 | - | 100 | -
LSL as % of HSL | 100 | 100 | 100 | 100 | 100 | 99 | 99 | 100 | 97 | 100 | - | 99 | 100 | 98 | 100 | 100 | 96 | - | 100 | -
DA Zonal Schedule | 100 | - | 100 | 100 | 100 | 100 | 100 | 98 | 100 | 100 | - | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 95 | -
AP Zonal Schedule | 99 | - | 100 | 98 | 100 | 99 | 99 | 99 | 98 | 99 | - | 100 | 100 | 100 | 100 | 98 | 100 | - | 85 | -
Down Bid & Obligation | 98 | - | 98 | 97 | 96 | 99 | 95 | 100 | 95 | 98 | - | 98 | 98 | 98 | 91 | 100 | 90 | - | 90 | -
Total Up AS Scheduled | 100 | - | 100 | 94 | 100 | 100 | 96 | 93 | 96 | 100 | - | 93 | 99 | 92 | - | 98 | 100 | - | - | 100
 |  |  |  |  |  | 4 Consecutive Failing Scores |  |  |  |  |  |  |  | 3 Consecutive Failing Scores |  |  |  |  |  | 
 |  |  |  |  |  | 2 Consecutive Failing Scores |  |  |  |  |  |  |  | 1 Failing Score |  |  |  |  |  | 

## Slide 10: Analysis of November 2008 Resource Plan Performance Metrics for Non-Wind Only QSEs
CI – Coral Power LLC
  First time failing “Resource Low Sustainable Limit as a Percentage of High Sustainable Limit Measure”.
IO – Westar (SQ1)
  This is their Fourth consecutive failing score of “Adjustment Period Zonal Schedule Measure”. Westar has been issued a possible violation notice of ERCOT Protocols 4.10.2 “Scoring Review” and 4.10.6 “Adjustment Period Zonal Schedule Measure”.
TRE Compliance Report
February 2009

## Slide 11: Analysis of November 2008 Resource Plan Performance Metrics for Non-Wind Only QSEs (cont.)
DF – Constellation Energy Commodities Group Inc
  First time failing “Total Up AS Schedule Obligation Measure”. Constellation was informed by email about their score and did provide a response contesting the failing score. Further analysis of Constellation submitted data will be needed and may change their score.
TRE Compliance Report
February 2009

## Slide 12: November 2008 Resource Plan Performance Metrics for Wind Only QSEs
TRE Compliance Report
February 2009
Resource Plan Performance Metric | ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | JG | BT | HJ | JM | JL | GR | GS | HS | BF | BE | FX | JH | JI | JN | JJ | JC | HE | CY | JQ | JP | JK | JE | IV
DA Zonal Schedule | 100 | 86 | 100 | 100 | 99 | 100 | 100 | 96 | 99 | 100 | 100 | 100 | 100 | 100 | 100 | 99 | 100 | 100 | 100 | 100 | 96 | 100 | 100
AP Zonal Schedule | 100 | 82 | 100 | 100 | 99 | 100 | 100 | 99 | 99 | 100 | 99 | 100 | 99 | 87 | 100 | 100 | - | - | 38 | 100 | 100 | 100 | 100
Down Bid & Obligation | 100 | 83 | 100 | 99 | 100 | 100 | 100 | 100 | 99 | 100 | 100 | 100 | 99 | 100 | 100 | 100 | - | - | 100 | 100 | 100 | 100 | 94
 |  |  |  |  |  |  |  | 4 Consecutive Failing Scores |  |  |  |  |  |  |  | 3 Consecutive Failing Scores |  |  |  |  |  | 
 |  |  |  |  |  |  |  | 2 Consecutive Failing Scores |  |  |  |  |  |  |  | 1 Failing Score |  |  |  |  |  | 
Note: Wind only QSE do not have Resource Status, LSL as a percentage of HSL and Total Aup AS Schedules scores. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 13: Analysis of November 2008 Resource Plan Performance Metrics for Wind Only QSEs
BT – American Electric Power Service Corp (AEP)
  First time failing all three scores.
JN – Invenergy Macadoo (SQ4)
  First time failing the “Adjustment Period Zonal Schedule Measure”. Invenergy reported that their operators cut and pasted the values into their spread sheet and did not notice that the data was off by an hour. They have since corrected their procedure for data submittal.
TRE Compliance Report
February 2009

## Slide 14: Analysis of November 2008 Resource Plan Performance Metrics for Wind Only QSEs (cont.)
JQ – NRG Texas Wind (SQ1)
  First time failing the “Adjustment Period Zonal Schedule Measure”. NRG provided a response on their failing score and reported that the problem has been corrected.
  This is the first month that NRG Texas Wind has been scored.
TRE Compliance Report
February 2009

## Slide 15: December Compliance Progress
Issued 2 NERC Preliminary Notices of Alleged Violation
4 SPS events occurred during the month of December (2 events happened on December 30th)
  Each of these events are being analyzed to determine if mis- operation has occurred
3 pre-December SPS Event Analyses are still pending
  Texas RE will conduct Spot Checks
TRE Compliance Report
February 2009

## Slide 16: December Compliance Progress (cont.)
Loss of large amount of Generation on December 16, 2008
  Analysis of this event is underway by Texas RE. Reports are pending from ERCOT ISO and other entities involved.
2 Multiple loss of Elements
  ERCOT ISO is currently investigating and has not yet reported their findings.
All pre-June 18, 2007 Mitigation Plans have been completed
Six entities are in settlement discussions representing 18 violations
TRE Compliance Report
February 2009

## Slide 17: 2 – Operator Training Seminar
25th Annual ERCOT Operations Training Seminar
Target Audience - qualified scheduling entity (QSE) and transmission/distribution service provider (TDSP) operators and those who provide management, supervision and support for the operators. The seminar is also open to power marketers, retail electric providers and others associated with the bulk electric system.
COST: $299 until March 1 then $349
Location: Wyndham Garden Hotel – Austin
Texas RE ROS Presentation February 2009

## Slide 18: Seminar Schedule
SEMINAR SCHEDULE:
Seminar Date Deadline
Session 1 Mar. 9 - 12, 2009 Feb. 19, 2009
Session 2 Mar. 16 - 19, 2009 Feb. 26, 2009
Session 3 Mar. 23 - 26, 2009 Mar. 5, 2009
Session 4 Mar. 30 – Apr. 2, 2009 Mar. 12, 2009
Session 5 Apr. 6 - 9, 2009 Mar. 19, 2009
Session 6 Apr. 13 - 16, 2009 Mar. 26, 2009
Texas RE ROS Presentation February 2009

## Slide 19: 3 – CIP Self Certification
Registered Entities have been sent the CIP Self Certification Request (required twice a year by CMEP)
Submittal will be via the Texas RE Portal
https://portal.texasre.org
Portal training sessions are posted at http://www.ercot.com
Due date for Self Certification is January 31, 2009
Possible penalties for failing to submit on time
Talk to your Compliance Staff / Master Account Administrator to ensure compliance
Texas RE ROS Presentation February 2009

## Slide 20: 4 – Nodal Plan Request
Public Utility Commission of Texas and Texas RE requested an update from the stakeholder community on the plan and progress for developing Nodal Protocols and Operating Guides monitoring programs and metrics
Letter sent to TAC Chair
Requested response by February 2, 2009
Texas RE ROS Presentation February 2009

## Slide 21: 5 - Load Serving Entity (LSE) Update
NERC Regional Reliability Standards Working Group Meeting was held in Austin in January with other Regional Entities, NERC and FERC
FERC recommended an alternative approach than that being taken by Texas RE and the ERCOT region (registration by requirement)
Recommendation conflicts with previous NERC direction
Texas RE reevaluating our approach
Texas RE ROS Presentation February 2009