## Slide 1: Back-cast of 2008 Shortage Intervals to estimate PRR 776 & 791 Impact
Larry Gurley
PRR 776 Discussion Group
TAC Meeting March 5, 2009
Notes: <number>

## Slide 2: Analysis Objectives
Determine the number of intervals in 2008 where there was shortage as indicated by Up Balancing Energy Service (UBES) offer stack depletion
Estimate the impact in these intervals if PRR 776 had been in place
Estimate the impact of PRR 791 in addition to PRR 776
<number>
Notes: <number>

## Slide 3: Analysis Results
The IMM determined that there 103 shortage intervals in 2008.
Of the 103 intervals, PRR 776 would have eliminated 90.
Of the 90 intervals eliminated, 13 intervals would have likely had lower prices.
Shortage would have persisted for 13 intervals (different 13) and would be impacted by PRR 791.
<number>
Notes: <number>

## Slide 4: Estimated Economic Impact
For the 13 intervals where shortage was eliminated under PRR776
  Assume quick start offer in BES at $600 and MCPE is at $600
Cost to the wholesale market would have been approximately $162 million or $0.52/MWh lower
For the 13 intervals where shortage persisted under PRR 776 if PRR 791 were applied
  Assume 80 MW priced from $500 to $2250
Cost to the market would have been approximately $203 million or $0.65 higher
<number>
Notes: <number>

## Slide 5: 2008 Shortage Intervals
The IMM determined that there were 103 intervals in 2008 where there was shortage due to Up Balancing Energy Service (UBES) offer stack depletion
  Individual QSE ramp rate constraints were violated to honor system balance constraint, or
  System balance not achieved
<number>
Notes: <number>

## Slide 6: More Statistics on 2008 Shortage
Shortage occurred during on-peak hours 78 of the 103 intervals.
Of the 78 shortage intervals during on-peak, ERCOT had procured NSRS during 76. (Remember the 2 difference)
Of the 76 on-peak shortage intervals where NSRS was procured, NSRS was deployed in 16 intervals.
Of the 16 intervals where NSRS was deployed, it was fully deployed in 9 intervals
Of the 7 intervals where NSRS was partially deployed, there were 2 intervals where the remaining was insufficient.
<number>
Notes: <number>

## Slide 7
<number>
Notes: <number>

## Slide 8: Assumptions on PRR 776 Impact on 2008 History
The effect of PRR 776 is to add the quick start capacity to the UBES stack when NSRS is procured.
Quick start capacity is assumed to be approximately 1000 MW
If NSRS were not procured, the quick start capacity is assumed to have already been in UBES.
<number>
Notes: <number>

## Slide 9: More Assumptions
If NSRS were procured and not fully deployed during shortage intervals, PRR 776 would relieve that shortage if the shortage amount were less than undeployed quick start NSRS.
<number>
Notes: <number>

## Slide 10: Shortage Where No NSRS Procured or Procured and Deployed
<number>
Time | NSRS Scheduled | NSRS Deployed | Shortfall (MW) | Shortage after 776 | Original MCPE | Recalculated MCPE
2/26/08 19:15 | 1354 | 820 | 185 | 5 | $299.00 | $609.38
5/19/08 17:15 | 1354 | 585 | 25 | 0 | $2,250.00 | 
6/9/08 10:00 | 0 | 0 | 65 | 65 | $400.6 | $1,921.88
6/9/08 13:45 | 1354 | 272 | 7 | 0 | $389.00 | 
6/9/08 14:15 | 1354 | 1354 | 185 | 185 | $253.01 | $2,250.00
6/9/08 16:15 | 1354 | 1354 | 44 | 44 | $253.01 | $1,462.50
6/9/08 16:30 | 1354 | 1354 | 54 | 54 | $253.01 | $1,681.25
6/18/08 15:30 | 1354 | 1354 | 69 | 69 | $295.00 | $2,000.65
6/18/08 15:45 | 1354 | 1354 | 71 | 71 | $400.60 | $2,044.48
10/2/08 7:15 | 0 | 0 | 21 | 21 | $668.00 | $959.38
10/2/08 17:30 | 1354 | 763 | 7 | 0 | $668.00 | 
10/2/08 17:45 | 1354 | 763 | 132 | 0 | $668.00 | 
12/1/08 18:30 | 1143 | 709 | 321 | 30 | $283.69 | $1,156.25
12/6/08 8:45 | 1143 | 1143 | 135 | 135 | $282.94 | $2,250.00
12/6/08 9:15 | 1143 | 1143 | 69 | 69 | $278.88 | $2,009.38
12/10/08 18:15 | 1143 | 549 | 101 | 0 | $259.06 | 
12/10/08 18:30 | 1143 | 1143 | 944 | 944 | $259.06 | $2,250.00
12/10/08 19:00 | 1143 | 1143 | 13 | 13 | $259.06 | $784.38
Notes: <number>

## Slide 11: 2008 Shortage Intervals Impacted by PRR 791
NSRS procured and fully deployed 9 shortage intervals
NSRS procured and partially deployed such that amount of quick start not available in 4 intervals
PRR 791 shortage pricing would have triggered on 13 shortage intervals in 2008.
For the 13 intervals PRR 791 would have increased the cost to the market $203 million or $0.65/MWh.
<number>
Notes: <number>

## Slide 12: 2008 Shortage intervals mitigated by PRR 776 and not triggering 791
<number>
Time | NSRS Scheduled | NSRS Dep | Shortfall (MW) | Original MCPE
1/10/08 18:00 | 1354 | 0 | 13 | $1,499.67
1/11/08 7:30 | 1354 | 0 | 182 | $1,499.98
1/11/08 7:45 | 1354 | 0 | 222 | $1,499.98
3/3/08 18:45 | 1354 | 0 | 285 | $2,250.00
3/3/08 19:00 | 1354 | 0 | 390 | $2,250.00
4/21/08 15:00 | 1354 | 0 | 87 | $2,250.00
4/23/08 18:30 | 1354 | 0 | 52 | $2,250.00
5/19/08 17:15 | 1354 | 585 | 25 | $2,250.00
8/7/08 18:15 | 1354 | 0 | 871 | $1,999.00
10/2/08 17:30 | 1354 | 763 | 7 | $668.00
10/2/08 17:45 | 1354 | 763 | 132 | $668.00
10/13/08 14:45 | 1354 | 0 | 29 | $1,999.00
12/2/08 7:00 | 1143 | 0 | 327 | $1,643.91
Assuming PRR 776 offers for quick start capacity will be at or below $600, 13 intervals would have likely had lower prices. Had all been $600, annual average would have been $162 million or $0.52/MWh lower.
Notes: <number>