## Slide 1
Retail Market Subcommittee
Visibility into OGRR219

## Slide 2: OGRR 219 Time Error Correction
RMS
March 11, 2009
Revision Description - This Operating Guide Revision Request (OGRR) removes the requirement that ERCOT perform time error corrections for accumulated time errors exceeding five (5) seconds.
Overall Market Benefit - This OGRR reduces the number of times error corrections performed and provides data to North American Electric Reliability Corporation (NERC) to possibly eliminate time error correction as a Reliability Standard.
Consumer Impact - No impact is anticipated. However, data gathered from this field trial is needed to determine that the end consumer is not affected by removing the time error correction and to prove that system reliability is not compromised.
http://www.ercot.com/mktrules/issues/ogrr/200-224/219/index

## Slide 3: Time Error Accumulation
 | Accumulated Time Error (TE) at the End of Month | 
Month (2008) | TE with Time Correction (seconds) | TE with No Time Correction (cumulative seconds)
January | 0.928 (5 corrections) | 7.6850
February | 1.078 (3 corrections) | 12.958
March | 0.038 (7 corrections) | 32.616
April | 0.322 (8 corrections) | 61.879
May | -0.120 (10 corrections) | 94.953
June | 2.537 (7 corrections) | 121.329
RMS
March 11, 2009
The table below compares the actual Time Error at the end of each
month and the results from a study of the amount of Time Error
Which excludes the periods of correction.
This shows that without Time Error Correction for the first four months in 2008,
ERCOT system would have a Time Error of 62 seconds at the end of April.

## Slide 4: OGRR219 - Visibility, Visibility, Visibility
RMS
March 11, 2009
Anticipated time drift for devices with time keeping synchronized to the system frequency
  ERCOT accumulated Time Error will continue to increase greater than +/- 5 seconds as shown in previous slide .
  From preliminary studies it is not uncommon to see up to 30 seconds of accumulated time error a month if not corrected
Anticipated dates for the NERC field trial test
  Start date is not set, but planning for May 2008
  Field trial can end at ERCOT’s discretion, but would like a minimum of a year with the caveat to extend.

## Slide 5: OGRR219 - Visibility, Visibility, Visibility
RMS
March 11, 2009
Anticipated Operations during NERC field trial test
  Time correction using the system frequency will not be performed unless a reliability or consumer issue is identified.
  The Field Trial can be stopped at any time
Anticipated Operations before/after NERC field trial
  Time correction using the system frequency will continue as it is currently performed while the Field Trial is not in effect.
  ERCOT Operations will still perform correction at 5 seconds.

## Slide 6: OGRR219 - Visibility, Visibility, Visibility
RMS
March 11, 2009
Reliability Operations Subcommittee
  Unanimous recommendation for approval
Retail Market Subcommittee
  Raise awareness and discuss
  Looking for feedback
    impacts
    concerns
NERC field trial test
  Looking for more feedback before commencing
  Market notice will be sent out prior to start

## Slide 7: Questions or Feedback
RMS
March 11, 2009
Ken McIntyre
  512-248-3969
  kmcintyre@ercot.com