## Slide 1: 2010 CSC & Zone Selection Scenario -1a
August 19, 2009

## Slide 2: Scenario 1a: 2009 CSCs
  2009 CSC has the following CSCs with 4 zones
    W_N & N_W : Sweetwater – Long Creek / Abilene Mulberry Creek – Long Creek 345 kV DCKT
    N_S & S_N : Lake Creek – Temple / Trading house – Temple Pecan Creek 345kV DCKT
    N_H : Singleton – Obrien / Singleton – TH Wharton 345kV DCKT
  Operational experience demonstrates that the stability limit can be controlled effectively as a CRE

## Slide 3: Benefits of Scenario 1a
W_N congestion experienced in 2009 was dominated by stability; the same expected for 2010
Highly effective in terms of managing congestion if stability interface is a CRE
  Highest generation shift-factors from ERCOT Operation studies
  W_N SF = 41.15%, N_W SF =40.35%
Other scenarios have lower generation shift factors

## Slide 4: Additional Considerations
Delta West to North CSC Shift Factors for West to North power transfer
  Scenario Delta W-N SF Selected CSC
  1a 0.39 2009 W-N CSC
  WN2-4Z 0.82 Stability Limit lines
  WN3-SN0-4Z 0.36 ERCOT Rec.
Choosing the stability limit lines for the W-N CSC has a PTDF double that of the other scenarios
WN2-4Z (Stability Limit lines) appears to require twice as many TCRs for hedging

## Slide 5: Additional Considerations (Cont.)
Historical TCRs auctioned (avg. for Jan – Sept)
2009 (same as scenario 1a)
  W-N TCRs N-W TCRs
  730 761
2008 (similar to ERCOT 2010 Recommendation)
  W-N TCRs N-W TCRs
  575 356
Significant difference in the number of TCRs offered in the auctions
WN3-SN0-4Z (ERCOT) could have a much lower number of TCRs offered for auction than 1a

## Slide 6: Summary
  Scenario 1a can control the stability limit effectively
  Scenario 1a has enough Operation History to manage congestion
  Scenario 1a provides sufficient opportunity to Hedge
  Other Scenarios create more uncertainty for 2010
  Other Scenarios may reduce the TCRs available for Hedging