- Capacity threshold of installed DG that triggers action

  - Zonal

    - Expect limited deployment of DG before Nodal go live

    - If come up with an automatic trigger for nodal it can also be applied to zonal

  - MW Threshold Trigger

    - Still trying to establish the MW threshold that will be applied to Nodal Load Zones?

      - Any Load Zone hits threshold - triggers Market Action

    - DG included in the threshold trigger will be limited to sites/units that are:

      - Not registered with ERCOT and therefore not settled as resources

      - Exporting energy into the TDSP Distribution System where out-flow energy is metered by the TDSP

  - Reporting needs to support determination if the threshold trigger has been hit

    - Competitive Areas

      - TDSPs currently report on non-IDR DRG Load Profile assignments

      - Utilize the information being reported by the TDSPs as required in section 7.14.2 of the Retail Market Guide

        - Modified this section to include TDSP reporting for ESI IDs that have Advanced Meters and include all DG

      - Can a report to support determining the threshold trigger be generated from ERCOT Systems based on information currently being reported?

    - NOIE Areas - Open Item to finalize

      - Data points currently identified for NOIE areas to provide

        - Technology

        - Fuel

        - Capacity

        - Load Zone

        - Annual kWh’s exported into the grid

- Change in the data submittal and registration threshold – Open item to discuss – Darryl, Eric and Ken to work on this.  Next meeting will be scheduled first week of November.

  - Automatically implement?

    - change threshold to?

    - timeline for new threshold to take effect?

  - Reconvene Task Force to evaluate

- Updates to Load Profiling Guides required

- Establish framework for the NPRR -  Not discussed at this meeting

Meeting attendees:

| Attendance on location | Company | Attendance by web-ex | Company |
| --- | --- | --- | --- |
| Don Tucker | ERCOT | Darryl Nelson | Oncor |
| Kathy Scott | CNP Energy | Michael Matthews | BTU |
| Calvin Opheim | ERCOT | Lori Williams | BTU |
| Jim Lee | Direct Energy | Jack Brown | Garland |
| Ken Riordon | LCRA | Harika Basaran | Austin Energy |
| Johnny Robertson | TXU Energy | Eddie Marx |  |
| Frank Wilson | Nueces Electric Retail Division | Mike Troell | STEC |
| Eric Goff | Reliant | Lee Star | BTU |
| Martin Lozano | Austin Energy |  |  |
| Kyle Minnix | Brazos Elec. Co-op |  |  |
| Adrianne Brandt | Austin Energy |  |  |
| Rob Bevil | Green Mountain |  |  |