## Slide 1
PWG Update Report
By
Ernie Podraza
of Direct Energy
ERCOT PWG Chair
for
COPS Meeting
November 10, 2009

## Slide 2
The PWG invites the COPS to join the PWG in wishing all the best to
Ron Hernandez and Diana Ott
on their new ERCOT assignments and recognition of many years of service and many significant contributions to the ERCOT Market as members of the ERCOT Load Profiling Department.
A job well done!!!

## Slide 4
Annual Validation 2009 Schedule
2009 AV on schedule no issues

## Slide 5
  Distribution Loss Factors in Relation to UFE?
    Quantification of UFE by cause is problematic if not impossible.
    During AMS deployment, trending analysis of UFE can be performed to determine if expected results are confirmed, i.e. a decrease of UFE due to elimination of profile modeling error, some aggregation issues, and some theft problems that are components of UFE.
    AMS meters should reduce profile modeling error, settlement daily allocation and some theft portions of UFE leaving perhaps error in distribution losses as the main remaining driver of UFE.
    UFE is +- 1.0% for the majority intervals in 2008 even with the Hurricanes so how close is close enough.
    Some Market Participants see 1% variance significant in market cost.
    A consistent bias is preferred over unpredictable variation.
    Is MCPE a good estimator of UFE cost?
PWG Goal 17

## Slide 6
  Distribution Loss Factors in Relation to UFE?
    TDSPs are encouraged in ERCOT protocols to perform and refresh loss load studies that support the ERCOT loss coefficient methodology.
    In some cases, TDSPs refresh loss studies during tariff filings where accuracy of the study has oversight from the PUCT and Interveners.
    Drivers of distribution losses change very little over time.
    ERCOT Staff could perform regression analysis to develop the coefficients for TDSP loss studies by computing loss amounts at several different load levels ranging from lowest to highest loads and to apply the study results to develop the coefficients specified in the protocols.
    The current three coefficients method is significantly better than the original straight line method in Protocols. The three coefficient method more accurately describes the loss factor over various load levels.
    Distribution Losses by TDSP may be preferred over one statewide method.
PWG Goal 17 (continued)

## Slide 7
  Distribution Loss Factors in Relation to UFE?
    Preference for Engineering Professional at the TDSP performing TDSP loss calculations vs. system-wide regression analysis on ERCOT load and generation values which could include influence from other factors such as theft as opposed isolating just losses.
    Some parts of a TDSP loss study are time consuming and costly to perform.
    PWG Recommendion is to revisit after Nodal resource constraints are lifted or AMS installation is completed.
    Goal Complete.
PWG Goal 17 (continued)

## Slide 8
  Draft in progress for Annual Validation suspension per AMS has been discussed and shall be on the next PWG agenda.
  LPGRR shall be in order for changes per the NOIE DRG TF when the TF is complete.
LPGRR and PRR Status

## Slide 9
Questions?
PWG 2009 meeting dates;
Conference Calls on November 12 and December 10