## Slide 1: Wind Cost Allocation Task Force
Update to WMS
December 16, 2009

## Slide 2: December 14 Meeting
Highlights –
  Reviewed allocation proposal submitted by Reliant
  Re-iterate this is a “how to” and not a “should we” and this task force is not making any statements about whether allocating Ancillary Costs to wind is fair

## Slide 3: Reliant Allocation Proposal
Assign an obligation to provide Regulation Up, Regulation Down, Responsive Reserves, and Non-Spinning Reserves to all QSEs representing WGRs and/or Load Serving Entities
Assign a portion of the cost of RPRS to all QSEs representing WGRs and/or Load Serving Entities

## Slide 4: Wind Plus Load Ratio Share (WPLRS)
Assign obligation based on QSE’s wind plus load ratio share
For example:
  500 MWh of wind from two QSEs
    QSE A has 300 MWh
    QSE B has 200 MWh
  1000 MWh of load
    QSE C has 600 MWh
    QSE D has 400 MWh

## Slide 5: Example, continued
Total wind plus load = 1500 MWh
WPLRS:
  QSE A = 300/1500 = 20%
  QSE B = 200/1500 = 13.3%
  QSE C = 600/1500 = 40%
  QSE D = 400/1500 = 26.7%

## Slide 6: Reliability Credits
WGRs can qualify for Reliability Credits to reduce total ancillary service obligations
For example, a WGR that provides primary frequency response may have their obligation reduced by 10%
  10% is for example purposes only, actual credit may be different
May be several credits, such as primary frequency response, voltage ride through, voltage support, etc.

## Slide 7: WPLRS + Reliability Credits
Previously, unadjusted WPLRS was:
  QSE A = 300/1500 = 20% (WGRs)
  QSE B = 200/1500 = 13.3% (WGRs)
  QSE C = 600/1500 = 40% (load)
  QSE D = 400/1500 = 26.7%
Assume that the WGRs in QSE A can provide primary frequency response, voltage ride through, and voltage support. QSE B’s WGRs cannot.

## Slide 8: WPLRS + Reliability Credits
QSE A received a 30% reduction for its reliability credits, so its adjusted with output is 300 MWh* ( 1-0.3) or 210 MWh
New total MWh is 1410, therefore:
  QSE A = 210/1410 = 14.9%
  QSE B = 200/1410 = 14.2%
  QSE C = 600/1410 = 42.6%
  QSE D = 400/1410 = 28.3%
Because QSE A is contributes more to reliability, it receives a smaller ancillary service obligation

## Slide 9: What AS Should be Included?
Considerable debate on whether to include all types of AS or just a portion
  Questions over whether it was appropriate to include RPRS and Responsive Reserve
  Suggestion made that allocation should limited to the incremental amounts of Reg Up, Reg Down and NSRS that ERCOT purchases due to wind
  Luminant going to bring proposal to next meeting on how this could be accomplished

## Slide 10: Reliability Credits
Market Participants and ERCOT would need to work together to develop a complete list of qualifying services and how to assign a reduction value to each
Debated whether there should be Reliability Credits or whether allocation should take a “binary” approach
  If a WGR cannot provide ALL of the services, then it will not be given any credits for any services that it can provide

## Slide 11: Possible Exemptions
Suggested that Distributed Generation be exempted from this allocation
  Need to determine how to distinguish those that should be exempted
  Allocation could be limited those large enough to require ERCOT registration
Also suggested that WGRs in certain geographic locations could be exempted or treated differently
  For example, WGRs in South Texas

## Slide 12: Other Discussion
Despite the charter and goals, several attendees (including PUCT Staff) voiced concerned over the fairness of allocating AS to WGRs only
Also debated whether a proposal to do nothing counted as a “how to” proposal

## Slide 13: Suggested Next Steps
Continue working through the details of Reliant proposal
Review additional any additional proposals including one from Luminant re: assigning incremental AS only
WMS could consider providing WCATF on the following issues:
  Reliability Credits vs. Binary Approach
  Exemptions for Distributed Generation