## Slide 1: Wind Cost Allocation Task Force
Update to WMS
January 20, 2009

## Slide 2: January 8 Meeting
Highlights –
  Reviewed four potential Reliability Credits
  Began discussions on Incremental Allocation Proposal
  Reached consensus that post-Nodal solution the most likely result due to impacts on ERCOT resources

## Slide 3: Primary Frequency Response – 30%
Required by Protocols
  Details pending outcome of PRR733, Primary Frequency Response Requirement from Existing WGRs
Metric needed to determine if the service is actually being provided by the WGR
  Was the response from controls or just an uptick in wind?

## Slide 4: Voltage Support – 20%
Must meet Protocol requirements as recently clarified by PRR 830, Reactive Power Capabilities Requirement
  Appeals of PRR 830 have been filed with the PUCT
    If the outcome of the appeals change the nature of voltage support, then credit will reflect the change

## Slide 5: Inertia – 30%
Increase in wind will require additional spinning mass to resist frequency oscillations
PDCWG or ERCOT would need to determine what/how much inertia the grid needs and how it can be provided by WGRs

## Slide 6: Forecast Error – 20%
Forecast error causes increase in Ancillary Service procurements
Metric would need to be created to determine eligibility for forecast error credit
Considerable controversy over moving away from centralized forecast from ERCOT as currently prescribed by Nodal

## Slide 7: AS Obligations, not Cost Allocation
ERCOT would create obligations for WGRs (and potentially other Intermittent Resources)
Obligations could be hedged, which could lead to more counterparties in the market
RPRS is the exception – no obligation to provide RPRS, merely a cost uplift to load and Intermittent Resources

## Slide 8: Incremental Allocation Proposal
Up & Down Regulation Service -
  ERCOT calculates the increased amount of wind penetration each month and uses tables provided by GE in their final report to ERCOT in the calculation of Regulation Service requirements
  The tables clearly indicate the incremental MW of Up Reg and Down Reg that are required per 1000 MW of wind generation capacity
  The GE tables could easily be adapted to allocate ancillary services requirements to wind generators based upon installed MW

## Slide 9: Incremental Allocation Proposal
Non Spinning Reserve Service –
  Today, ERCOT uses the 95th percentile of Net Load Uncertainty to determine the base amount of NSRS it should require
    Net Load Uncertainty = Forecasted Net Load - Actual Net Load
    Net Load = Load - Wind Generation
  The incremental amount of NSRS relative to wind generation could be determined by comparing the 95th percentile of Net Load Uncertainty to the 95th percentile of Load Uncertainty for the same data set
  The obligation for the incremental amount of NSRS relative to wind generation could then be allocated to wind generators based on installed MW

## Slide 10: Incremental Allocation Proposal
Reliability Credits -
  Proposal does not currently include any reliability credits but they could be added on

## Slide 11: Next Steps
Finalize Reliability Credits
Review example calculations for Incremental Allocation Methodology
Bring proposals for vote at February WMS – hopefully 