## Slide 1: Proxy Offer Curve – RUC Effect REVISED Settlement and Billing - Market Analysis
January, 15 2010
VCWG
Pamela Shaw

## Slide 2: Background Information
Protocol Section 6.4.2 Output Schedule
(1) A QSE that represents a Resource, other than an RMR Unit, must submit and maintain either an Energy Offer Curve or an Output Schedule for the Resource for all times when the Resource is On-Line.
(3) The entry of an Energy Offer Curve for a Resource automatically nullifies the Output Schedule for that Resource and prohibits entry of future Output Schedules for that Resource for the time during which the Energy Offer Curve is in effect.
(4) For a Resource for which an Energy Offer Curve has not been submitted, the SCED process uses the Output Schedule submitted for that Resource as desired Dispatch levels for the Resource.
ERCOT system shall construct a proxy offer curve when Energy Offer Curve is not submitted by the QSE as described in 6.5.7.3(3).
ERCOT system shall construct a proxy offer curve when an Energy Offer Curve is withdrawn during certain period of the operation day( MMS SCED and Real Time MMS Process requirement v3.01 )

## Slide 4: TWOS Proxy Offer Curve Example
MW | Price (per MWh)
160 | 2250
81 | 2249.99
80 | -$249.99
15 | -$250.00
Inputs
Outcome
    For Interval 14
    TWOS=80 MWs
    HSL= 160 MW
    LSL=15 MW
    For that Operation day
    SWCAP=2250
    RTMG for that interval
    RTMG=24
    RTMG*4=96
MW | Price (per MWh)
HSL | SWCAP
Output Schedule MW plus 1 MW | SWCAP minus $0.01
Output Schedule MW | -$249.99
LSL | -$250.00

## Slide 5: Proxy Offer Curve and Negative AIECAREA - REVISED
Results
RTAIEC = -$183

## Slide 6: Negative AIEC’s impact to RUC revenues
Maximum of 0 or sum of all RUC intervals
RTSPP * Maximum of 0 or {Real-Time Metered Gen – (1/4 of LSL)}
Real-Time AIEC * Maximum of 0 or {Real-Time Metered Gen – (1/4 of LSL)}
-
RUCEXRR =
RUCEXRQC =
Maximum of 0 or sum of all QCLAW intevals
(RTSPP * Real-Time Metered Gen )
Real-Time AIEC * Maximum of 0 or {Real-Time Metered Gen – (1/4 of LSL)}
-
RUCMWAMT = (-1) * Max (0, RUCG – RUCMEREV – RUCEXRR – RUCEXRQC) / RUCHR
May potentially increase the revenue subtracted from the RUC Guarantee and decrease your Make Whole payment or subject you to Clawback charge