Effect of Certain Market Participant Actions on Real Time Market Results

1.	Scope

This document is written to increase awareness of the effects of certain Market Participant (MP) actions on Real Time Market (RTM) results and thereby encourage MPs to manage these actions to get meaningful RTM results during Market Trials (MT). The approach taken is to first explain the RTM results under normal condition and then describe how the results change under different Market Participant (MP) actions. The document will function as a check list for MPs to analyze their data, before contacting ERCOT with questions that can be explained by self analysis. This document also lists the possible issues with Market Design.

2.

Understanding SCED Results

This section describes the RTM results under normal condition.

2.1.	SCED Results Characteristics

The following is the characteristic of an optimal SCED result.

1.	Resource dispatched at High Dispatch Limit (HDL) - LMP is higher than offer price at Base Point [HDL]

2.	Resource dispatched between HDL and LDL - LMP is equal to offered price at Base Point.

3.	Resource dispatched at Low Dispatch Limit (LDL) - LMP is lower than offer price at Base Point [LDL]

4.	Shadow Price is zero for a Transmission Constraint which is not binding

5.	Shadow Price is greater than or equal to zero for a Transmission Constraint which is binding

6.	Base Points are between HDL and LDL [If HDL and LDL are equal, SCED Base Point will also be equal to HDL/LDL until more dispatch range is provided to SCED.]

The following figure (Fig. 1) shows the relationship between Base Points, LMPs and Operating Limits. The subscripts correspond to the bullet numbers in the list above.

BP1

HDL

LMP1

LMP3

LMP2

BP3

LDL

BP2

$/MWh

MW

BP1

HDL

LMP1

LMP3

LMP2

BP3

LDL

BP2

$/MWh

MW

Fig. 1 – Optimal SCED Result

2.2.	Resources Not Setting LMP

Resource will not set the LMP when Emergency Base Points are deployed or when Resources are ramp limited.

2.2.1.	Emergency Base Points are Deployed

Emergency Base Points are typically used when SCED fails.  A SCED failure occurs when the SCED application crashes or Software issue in MMS prevents SCED application from running or failure of connection between EMS and MMS prevents RTM results from being sent to MPs. ERCOT System Operator determines the extra energy needed to meet the load change from the time Base Points were previously deployed. Emergency Base Points are then calculated by allocating this extra energy to all Resources proportional to the remaining capacity available on the Generation Resources. The LMPs used for settlement when Emergency Base Points are deployed, will be the LMPs from the last successful SCED run prior to the issuance of Emergency Base Points. Hence the LMP could be inconsistent with the price from the Resource’s Energy Offer Curve corresponding to the dispatch. However, the QSE may be compensated for any lost revenue based on Protocol 6.6.9.1

2.2.2.	Resources are Ramp Limited.

SCED can not violate the HDL or LDL of Resources. Resources limited by HDL will not be ramped up higher than the HDL even if its offer price is lower than the LMP. Similarly, Resources limited by LDL will not be ramped down lower than the LDL even if its offer price is higher than the LMP. Even if the Resource has normal ramp capabilities that are not being used, the Resource’s calculated HDL or LDL might be limited. The following is the list of most common reasons why HDL or LDL may limit Base Points from SCED.

.

·	Telemetry inconsistency issues

o	HDL is set to calculated LDL  or current telemetered MW  since ERCOT will not be able to identify which value is correct

·	Resource is starting up

o	HDL and LDL are set to telemetered MW if MW < 0.9 * LSL since the Resources is not dispatchable by SCED while it is ramping to LSL

·	After an Ancillary Service deployment is recalled and Resource is dispatched near HASL

o	HDL is set to LDL if calculated LDL >HASL to ramp the Resource down to restore un-deployed Ancillary Service Capacity.

·	Ramp capacity being reserved for Resource Regulation Responsibility

o	HDL = MW when Normal Ramp Rate less than or equal to  Up Regulation Responsibility divided by 5; This causes SURAMP=0

o	LDL = MW when Normal Ramp Rate less than or equal to  Down Regulation Responsibility divided by 5; This causes SDRAMP=0

·	ERCOT system operators have overridden the Resource’s calculated HDL or LDL as provided by protocol

2.3.	Prices Greater than System Wide Offer Cap or Lower than System Wide Offer Floor

The LMPs calculated by SCED is affected by the Power Balance Penalty and transmission constraint Shadow Price (SP) values and hence can be significantly higher than the System Wide Offer Cap or lower than System Wide Offer Floor.

For the SCED to be more robust in finding a solution,  we need to model Power Balance and Transmission Constraints as soft constraints by having penalty cost for relaxing these constraints. ERCOT uses a cost penalty curve to control the amount by which any constraint may be relaxed. The relative value of these penalties will determine the order and the relative amount by which theses constraints will be relaxed if needed.

Also, in Nodal, instead of using a Shift Factor cutoff, ERCOT sets a relatively low maximum Shadow Price to ensure that the Resources with low Shift Factor (SF) will be selected if they are more economical in resolving the constraint than Resources with high SF. Effectively the SF cutoff is (Cost/Max SP). Shadow Price is the reduction in production costs if a constraint were relaxed by 1 MW. The maximum Shadow Price is the maximum $/MWh SCED will allow to resolve 1 MW of the binding constraint.

CMWG proposed an initial set of values for maximum Shadow Price for Transmission Constraints and Power Balance penalty curve based on discussion between Market Participants, IMM & ERCOT. It is anticipated that experience gained from using these values during Market Trial will allow for evaluation of the potential for general (i.e., for a voltage class) or specific (i.e., for a specific constraint) modifications. The initial proposed values are as follows:

o	Power Balance Penalty Curve

| Over Generation Penalty ($/MWh) | -3,001 | -5,000 |
| --- | --- | --- |
| MW Cap Segment (MW) | 10,000 | 100,000 |
| Under Generation Penalty ($/MWh) | 3,001 | 5,000 |
| MW Floor Segment (MW) | 10,000 | 100,000 |

i.e. 3001 $/MWh for the violated MW from 0MW to 9999.999MW, and 5000$/MWh for the violated MW from 10000MW to 99999.999MW

This Power Balance penalty curve provides the means for relaxing the Power Balance constraint. It acts as extra capacity available to meet Power Balance. Based on the current values, during under generation the curve gives 9999.999 MWs at $3001 to ramp up to meet Power Balance and thereby set the LMP at 3001 and during over generation the curve gives 9999.999 MWs at -$3001 to ramp down to meet power balance and thereby set the LMP at -$3001.

o	Maximum Shadow Price for Transmission Constraints

·	Base Case constraint:  $5,000/MW

·	Post Contingency constraint based on monitored element kV level

o	345 kV:  $4,500/MW

o	138 kV:  $3,500/MW

o	69 kV:  $2,800/MW

2.4.	Special Cases – ONRR / ONTEST

There is special logic implemented for handling Resources with ONRR and ONTEST Resource Status. SCED dispatches the Resources with ONRR Resource Status to current telemetry MW if Responsive Reserve is deployed and to zero otherwise. Similarly, SCED dispatches the Resources to current telemetry MW if the telemetry Resource Status is ONTEST.

3.

Effects of Certain Market Participant Actions

3.1.	Inconsistent Telemetry

SCED uses from SCADA telemetry HSL, LSL, Ancillary Service Resource Responsibility, Ancillary Service Schedule, MW, Resource Status, Combined Cycle configuration number and DSR Output Schedule to determine the Base Point for the Resources. If these telemetered values are inconsistent among themselves (for example some are based on gross some on net generation) then ERCOT will not be able to identify which value is correct. If telemetry inconsistencies are identified then ERCOT sets the HDL & LDL according to the following such that the inconsistencies minimally impact the Real Time market.

o	Resource Status =OFF, OUT, OFFNS, EMR and telemetered net MW>0 MW

·	Resource is considered online

·	HDL & LDL are set to (net MW – SCED Down Ramp Rate * 5)

o	Resource Status = ON and telemetered net MW<0

·	HDL, LDL & MW are set to 0

o	Resource Status telemetry quality is bad

·	Resource Status is set to last good value

·	HDL, LDL, HASL, LASL are set to net MW

o	Resource Status telemetry quality is good, but the value is not a valid Resource Status Code

·	Resource is considered online

·	HDL, LDL, HASL, LASL are set to MW

o	Telemetered Resource telemetry quality is Suspect for any of the following HSL, LSL, Ancillary Service Resource Responsibility, Ancillary Service Schedule, net MW

·	 Last good value is used

o	Telemetered Resource Responsibility or Schedule <0 for any Ancillary Service

·	Resource Responsibility or Schedule which is less than 0 is set to 0

o	Calculated LDL >HASL

·	HDL is set to calculated LDL – Resource is gradually ramped down

o	Calculated HDL<LASL

·	LDL is set to calculated HDL – Resource is gradually ramped up

HDL, LDL, HSL, LSL, HASL and LASL are set to telemetered MW for the following issues

o	HSL<LSL,

o	HSL <=0

o	LSL <0

o	HSL <= Reg-Up Resource Responsibility + Responsive Resource Responsibility + Non-Spin Resource Responsibility

o	(HSL-LSL) < SUM (AS Responsibilities)

o	Invalid Combined Cycle Plant configuration

o	MW < 0.9 *LSL

3.1.1.	Effect on Real Time Market

These inconsistencies have the following effect on Real Time Market

o	Under Generation

During periods when the capacity available for SCED is already-low, the situation becomes compounded by Resource telemetry inconsistency.  Any Resource telemetry inconsistency which would force ERCOT to set HDL to the calculated LDL would further reduce the capacity available for SCED and could cause under-generation situation in SCED forcing the power balance penalty function to activate.

This can happen under the following conditions

·	Incorrectly telemetered Resource Status–QSE incorrectly telemeters a Resource Status as OFF, OUT, OFFNS or EMR for online Resources

·	Incorrectly telemetered Ancillary Service Schedule - If the Resource is dispatched near its HASL and QSE telemeters an incorrect Ancillary Service Schedule, which is drastically higher than the previous value, causing its MW to be higher than the calculated HASL

·	Change in Ancillary Service Resource Responsibility - If the Resource is dispatched near its HASL and at the beginning of the hour its Ancillary Service Responsibility and hence Ancillary Service Schedule increased drastically causing its MW to be higher than the calculated HASL

·	Ancillary Service recall - If large amount of Ancillary Service is recalled from a Resource when the Resource is dispatched near its HASL, causing its MW to be higher than the calculated HASL

o	Higher LMP and Price Fluctuation

When telemetry inconsistency occurs and Resources are fixed or moved down, the dispatch and LMP of other Resources are affected. If a lower cost Resource with high Shift Factor relative to a constraint is fixed or backed down due to inconsistency errors then the price to resolve the constraint may increase. Similarly if a marginal Resource is dispatched down due to telemetry inconsistency errors then the balance of the remaining marginal Resources will be moved up and the LMPs will increase even if nothing else changes.

Price Fluctuation can occur when the telemetry inconsistency happens intermittently causing fluctuation in marginal Resource dispatch.

3.2.	Significant Capacity on Output Schedule

If majority of the Resources use Output Schedule then, due to the proxy offer curve creation, most of the capacity available for SCED will only be available at System Wide Offer Cap and hence the LMPs will be at System Wide Offer Cap with small increase in load.  The Proxy Offer Curve created by SCED for Resources with Output Schedule is shown in the figure below (Fig. 2).

Fig. 2 - Proxy Offer Curve for Resources with Output Schedule

3.3.	Lack of Energy Offer Curves for Wind Resources

If a Wind Resource does not submit Energy Offer Curve then ERCOT will create a Proxy Offer Curve (Fig. 3) with effectively all the Resource’s capacity at -$250. If a constraint becomes active due to considerable Wind Resource Production and other Generation Resources cannot resolve the constraint, then all the Wind Resources will be dispatched down, prorated based on the Shift Factors, setting the LMPs negative at -$250. Even if only a small amount of generation is reduced from the Wind Resources, the prices will be at -$250 which may encourage Resources to shutdown. If many Resources disconnect from the network in Real Time at the same time, then it could affect system frequency and cause LMP fluctuation.

Fig. 3 - Proxy Offer Curve for Wind Resources with no Energy Offer Curve

4.

Effects of ERCOT action

4.1.	SCED Failure

When SCED fails the following action will be taken

o	Emergency is declared

o	Emergency Base Point will be deployed

SCED fails when the application crashes or there is a software issue in MMS that prevents the SCED application from running or if there is a failure of the connection between EMS and MMS that prevents SCED results from being sent to MPs via ICCP. When SCED fails, the ERCOT System Operator determines the change in energy needed to meet the load change from the time Base Points were previously deployed from SCED. Emergency Base Points are then calculated by allocating this extra energy to all Resources, proportional to the remaining capacity available on the Resources. The LMPs for the duration of the SCED Failure will be the LMPs from the last successful SCED run prior to the issuance of Emergency Base Points. Hence, the LMPs could be inconsistent with the prices from the Resource’s Energy Offer Curve corresponding to its dispatch. However, the QSE may be compensated for any lost revenue based on Protocol 6.6.9.1

4.2.	Deploying EILS during EEA

Before EILS is deployed, SCED is near a capacity short situation and hence the prices will be high. When EILS is deployed, generation energy to serve load must be reduced to rebalance the system.  Thus more capacity is made available to SCED and hence the prices may drop.

4.3.	ICCP Failure or Data Base Loading

During ICCP Failure or Data Base loading, all ICCP points become suspect and hence Resource Limit Calculator sets HDL and LDL to current telemetered MW. This could result in under generation and high prices. To resolve this, ERCOT aborts SCED and triggers it after 2 minutes if sum (HDL) = sum (LDL) condition is detected. This continues until the total telemetry failure is resolved. Once the issues are resolved SCED will execute and produce Base Points and LMPs.

5.

Market Design Issues

·	Ramp Rate needed for providing Regulation Resource Responsibility is reserved when SCED Up Ramp Rate is calculated. This makes part of available physical capacity un-available to SCED. QSEs must be vigilant in establishing the amount of Reg-Up or Reg-Down provided to assure that the SURAMP and SDRAMP always remain positive and allow for movements of Base Points

·	Output Schedule is not adjusted for RRS deployment. Hence RRS energy from Resources on Output Schedule is not deployed as part of Base Points from SCED, unless the LMP is at System Wide Offer Cap. I.e. RRS energy from Resources on Output Schedules can only be deployed at the System Wide Offer Cap.

·	The artificial drop in price when EILS is deployed during EEA prevents scarcity prices from being communicated consistently to Market Participants

·	SCED Base Points lags behind Load Forecast and uses up regulation since SCED considers current generation as demand instead of 5 minutes look ahead forecast load. Current implementation has extra terms in the “generation to be dispatched” calculation to consider short term load forecast, non-confirming load changes and frequency deviation.

6.	Operational Issues Summary

·	Inconsistent telemetry causes under-generation or price fluctuation

·	Wind Resources may cause negative prices which may in turn result in QSEs switching of too many Resources detrimentally affecting frequency.

·	Wind might be backed down in HRUC to resolve issues

·	Significant capacity on Output Schedule causes high prices due to available capacity being at System Wide Offer Cap.

7.	Appendix

7.1.	 Range of values

HSL

HASL

HDL

MW

LDL

LASL

LSL

HASL

LASL

HDL

LDL

BP

HSL

HASL

HDL

MW

LDL

LASL

LSL

HASL

LASL

HDL

LDL

BP

7.2.	 Calculations

LASL = Min {HSL, LSLTELEM + RDSTELEM}

HASL = Max (LASL, (HSLTELEM – (RRSTELEM + RUSTELEM

+ NSRSTELEM)))

SURAMP = RAMPRATE – (RUSTELEM / 5)

SDRAMP = NORMRAMP – (RDSTELEM / 5)

HDL = Min (POWERTELEM + (SURAMP * 5), HASL)

LDL = Min {Max (POWERTELEM - (SDRAMP * 5), LASL),

HSL}