## Slide 1
Nodal Verifiable Costs for RMR Resources
Ino Gonzalez
WMS
February 17, 2010
<number>

## Slide 2
Issue
RMR Three–Part Supply Offers (3PO) based on RMR contract
O&M costs not included in RMR contract  O&M costs not part of 3PO
RMR 3PO do not reflect true cost of Resource
<number>
RMR vs NON-RMR Three Part Supply Offers

## Slide 3: RMR vs NON-RMR Three Part Supply Offers
<number>
Protocol Language
4.4.8 RMR Offers
ERCOT shall decide, in its sole discretion, when to make a Reliability Must-Run (RMR) Unit available for commitment in DRUC, HRUC, or DAM, considering relevant factors such as whether it is likely to be needed in Real-Time for reliability reasons, whether Security-Constrained Economic Dispatch (SCED) will solve operating constraints, contractual constraints on the Resource, and any other adverse effects on the RMR Unit that may occur as the result of the dispatch of the RMR Resource.
(a) By 1000 in the Day-Ahead, ERCOT shall submit, in ERCOT’s sole discretion, Three-Part Supply Offers based on RMR Agreement rates and any other relevant information as provided under contract on behalf of RMR Units for any RMR Units to be considered in the DAM, DRUC, or HRUC.
(b) ERCOT may submit Energy Offer Curves based on RMR Agreement rates and any other relevant information as provided under contract on behalf of RMR Units committed in the DAM, DRUC, or HRUC.
Notes: <number>

## Slide 4
Verifiable Costs Caps: Non-RMR Units
a. Startup Offer Cap = Fuel Rates x Fuel Price + O&M(a)
b. Min Energy Offer Cap = Fuel Ratem x Fuel Price + O&M(a)
c. Mitigated Offer Cap = IHR x Fuel Price + O&M(a)
where,
s: Startup Fuel ; m: Min Energy Fuel
a: Includes emissions
IHR: Incremental Heat Rate
<number>
RMR vs NON-RMR Cost Methodology

## Slide 5
Verifiable Costs Caps (Offer): RMR Units
a. Startup Offer = Fuel Rates x [Fuel Price + FA(1)]
b. Min Energy Offer = Fuel Ratem x [Fuel Price + FA(1)]
c. Energy Offer Cap = IHR x [Fuel Price + FA(1)]
where,
s: Startup Fuel ; m: Min Energy Fuel
(1): Fuel Adjustment
IHR: Incremental Heat Rate
RMR vs NON-RMR Cost Methodology

## Slide 6: RMR vs NON-RMR Cost Methodology
<number>
Startup Cost Example
Notes: <number>

## Slide 7
Concerns
a. RMR units 3PO understated by actual O&M values paid in settlement
b. RMR units compete in DAM based on understated cost and energy price
<number>
RMR vs NON-RMR Cost Methodology

## Slide 8
Options for Mitigating Problem
a. Do nothing
b. Not Offer RMR Resource into DAM
Requires Protocol change
c. Estimate O&M cost
Requires a MMS system change
Continue…..
<number>
RMR vs NON-RMR Cost Methodology

## Slide 9
Options for Mitigating Problem
d. Estimate O&M - Change Fuel adder to reflect additional cost
Difficult to do without a system change
  Fuel adder same for each part of 3PO
e. Estimate O&M - Change Fuel rate to reflect additional cost
Not reflective of value stated in RMR contract
<number>
RMR vs NON-RMR Cost Methodology

## Slide 10
ERCOT’s Proposal
a. Evaluate ways to include O&M costs into 3PO
b. Write a White Paper to detail how ERCOT is going to create 3PO
c. Share White Paper with WMS and post on the ERCOT public web site
<number>
RMR vs NON-RMR Cost Methodology