## Slide 1: Concerns with RUC Capacity Short Charge and Energy Trades

## Slide 2: Background
RUC processes (DRUC & HRUCs) use the following inputs to make capacity commitment decisions:
  Load Forecast, COP, Start Up & Minimum Energy Offers, Transmission constraints, Resource Parameters, and few others (see 5.5.2 (8)).
  Energy Trades not used in RUC process commitment decision.
RUC Capacity Short Charge is a settlement function used to allocate RUC costs.
  Energy Trades are used in the RUC Capacity Short Charge methodology.
Nodal trade submission rules:
  Final energy trade submission deadline is 1430 of the day following the operating day.
  Snapshots are taken of submitted trades throughout the day-ahead and real-time RUC processes to assess “shortness” for RUC Capacity Short Charge (i.e. snapshot taken at each DRUC and HRUC process).

## Slide 3: Concerns with RUC Capacity Short Charge
Issue 1) Bilateral agreements do not consider RUC process trade submission deadlines; Protocols offer a choice
  Bilateral trade agreement language references submission of trades (i.e. scheduling) “in accordance with ERCOT Protocols” or is silent. Final ERCOT Protocol deadline is 1430 day after. There is no obligation established in bilateral agreements to submit trades before RUC processes.
  Counterparties must agree to voluntarily submit trades before RUC deadlines in order for them to be included in “shortness” assessment.
  Not feasible to change every bilateral agreement in ERCOT.
  It is reasonable for bilateral agreements to not consider RUC deadlines. See Issue #4.

## Slide 4: Concerns with RUC Capacity Short Charge
Issue 2) Conflicting incentives for long and short counterparties regarding trade submission
  No enforcement mechanism for submission based on Protocol requirement or bilateral agreement which requires both counterparties to submit trades before RUC process deadlines.
  Buying counterparty incented to submit trades early at RUC process deadlines – purchases cover any short position for RUC.
  Selling counterparty incented to submit trades at trade submission deadline (1430 day-after) – no short position in system for RUC.
Issue 3) Bilateral trade counterparty settlement reconciliation
  No enforcement mechanism for reconciliation based on Protocol requirement which requires both counterparties to submit trades before RUC process deadlines.
    Submitting trades after RUC process deadlines but before final trade submission deadline still compliant with ERCOT Protocols and bilateral agreement.
  For perspective, counterparty reconciliation of scheduling mismatches in the current zonal market is facilitated by ERCOT Protocol submission requirements along with corresponding settlement data that accommodate the bilateral market.

## Slide 5: Concerns with RUC Capacity Short Charge
Issue 4) RUC process trade submission deadlines undermine bilateral flexibility
  Conflicting economic decisions accompany multiple trade submission deadlines.
    Submitting trades early undermines value of real-time flexibility in bilateral agreements.
    Submitting trades later may create exposure to RUC when the party may not be short.
  Trade submission at DRUC process deadline would reduce liquidity or eliminate the bal-day (balance of day) bilateral market. This removes a real-time hedging tool.

## Slide 6: Concerns with RUC Capacity Short Charge
The Nodal Protocols are clear, but don’t think the intended design will work without significant disruption to the bilateral market.
The Results? Confusion upon nodal go-live especially when ERCOT settlement statements and invoices show up, excessive counterparty reconciliation and disputes, potential litigation, reaction in the bilateral market.
Potential Solution: Remove energy trade snapshot mechanism in RUC Capacity Short Charge. Assess “shortness” based on final energy trade submissions received by 1430 of day following operating day. No change to COP or Capacity Trade snapshots. Preserves original cost allocation concept.
  Be conscious of nodal implementation timeline. Simplify implementation.
  WMS Discussion: What are the consequences of this change?

## Slide 7: Appendix
Nodal Protocol References

## Slide 8: Nodal Protocols Section 4.4.2
4.4.2 Energy Trades
(1) An Energy Trade is the information for a QSE-to-QSE transaction that transfers financial responsibility for energy at a Settlement Point between a buyer and a seller.
(2) An Energy Trade for hours in the Operating Day that is reported to ERCOT before 1430 in the Day-Ahead creates a capacity supply or obligation in the DRUC process. Energy Trades submitted after 1430 in the Day-Ahead for the Operating Day create a capacity supply or obligation in any HRUC processes executed after the Energy Trade is reported to ERCOT. Energy Trades submitted after the DRUC snapshot are considered in the Adjustment Period.
(3) An Energy Trade may be submitted for any Settlement Interval within an Operating Day before 1430 of the following day.
(4) As soon as practicable, ERCOT shall notify each QSE through the Messaging System of any of its Energy Trades that are invalid Energy Trades. The QSE may correct and resubmit any invalid Energy Trade within the appropriate market timeline.

## Slide 9: Nodal Protocols Section 5.4
5.4 QSE Security Sequence Responsibilities
During the Security Sequence, each QSE must:
(1) Submit its COP and update its COP as required in Section 3.9, Current Operating Plan (COP);
(2) Submit any Three-Part Supply Offers before:
(a) 1000 in the Day-Ahead for the DAM and DRUC being run in that Day-Ahead, if the QSE wants the offer to be used in those DAM and DRUC processes; and
(b) The end of the Adjustment Period for each HRUC, if the QSE wants the offer to be used in the HRUC process;
(3) Submit any Capacity Trades before 1430 in the Day-Ahead for the DRUC and before the end of the Adjustment Period for each HRUC, if the QSE wants those Capacity Trades included in the calculation of RUC settlement;
(4) Submit any Energy Trades before 1430 in the Day-Ahead for the DRUC and by the end of the Adjustment Period for each HRUC; if the QSE wants those Energy Trades included in the calculation of RUC Settlement;

## Slide 10: Nodal Protocols Section 5.3
5.3 ERCOT Security Sequence Responsibilities
(3) For each RUC process, ERCOT shall:
(a) Execute the Security Sequence described in Section 5.5, Security Sequence, Including RUC, including:
(i) Validating Three-Part Supply Offers, defined in Section 4.4.9.1, Three-Part Supply Offers; and
(ii) Reviewing the Resource commitment recommendations made by the RUC algorithm; and
(b) Post to the MIS Secure Area, the following information related to the RUC:
(i) All active and binding transmission constraints (contingency and overloaded element pair information where available) used as inputs to RUC; and
(ii) All Resources that were committed or decommitted by the RUC process; and
(c) Issue Dispatch Instructions to notify each QSE of its Resource commitments or decommittments.