## Slide 1: Wind Cost Allocation Task Force
Update to WMS
February 17, 2009

## Slide 2: How We Got Here
1-2 Board Members have asked repeatedly about allocating Ancillary Service Costs to Wind Generators
At September 2009 meeting, PRS made a recommendation to TAC that a task force be created to consider how to allocate Ancillary Service Costs to Wind Generators
  Recommendation was tied to a motion to rehear a motion to approve PRR828, Remove QSE SCE Performance Exemption for QSEs with only Uncontrollable Renewable Resources On-line
  PRR828 was ultimately rejected
  AEP volunteered to lead the task force

## Slide 3: WCATF Charter
The Wind Cost Allocation Task Force (WCATF) is a WMS Task Force formed to address the allocation of the cost of Ancillary Services to Wind Generation Resources.
  Approved by WMS on November 18, 2009

## Slide 4: WCATF Goals
Our primary goal is to develop one or more methodologies with supporting rationales for allocating the cost of Ancillary Services to Intermittent Renewable Resources, specifically, Wind Generation Resources.
Our secondary goal is to consider and potentially develop additional methodologies for the allocation of Ancillary Services to other Intermittent Renewable Resources (e.g. solar resources).
Develop and present to WMS a whitepaper that summarizes the discussion and development of proposed methodologies.
Our goals will not include debating the appropriateness of utilizing one or more of the methodologies being considered. Similarly, our goals will not include a full analysis for assigning costs of Ancillary Services to all Market Participants.
APPROVED by WMS on November 18, 2009

## Slide 5: Let’s Be Clear
WCATF was asked to develop potential methodologies for “how” to allocate Ancillary Services
WCATF did not discuss whether Ancillary Services “should” be allocated
WCATF is not endorsing or recommending approval of either of the proposals presented today

## Slide 6: Proposed Methodologies
Two allocation methodologies have been proposed for WMS Consideration
  Wind Plus Load Ratio Share Proposal
  Incremental Allocation Proposal

## Slide 7: Ancillary Service Obligations with Reductions for Upgrades
Wind Plus Load Ratio Share

## Slide 8: What?
Wind generators receive a hedgeable ancillary service obligation for responsive reserves, non-spinning reserves, regulation up, and regulation down
Wind generators can reduce the obligation by qualifying for “reliability credits”

## Slide 9: How?
Obligation based on “Wind Plus Load Ratio Share” not just Load Ratio Share
  QSE’s sum of energy from WGRs and load from LSEs in the numerator
  ERCOT-wide sum of energy from WGRs and load from LSEs in the denominator
Obligation calculations are provided to LSEs and WGRs at the same time
All obligations are hedgeable in the bilateral market

## Slide 10: How?
Each WGR can reduce the energy used in the WPLRS calculation by qualifying for reliability credits
Credits add up to 100% reduction in obligation for qualified generators
Credits reduce the energy contribution to WPLRS (like UFE adjustment factors)

## Slide 11: How? (Reliability Credits)
Proposed Reliability Credits are:
  Primary Frequency Response (or in-service governor) – 30% reduction
  Voltage Support – 20% reduction
  Inertia or an inertial-like response – 30% reduction
    Inertial-like responses could include “black box” electronic control responses that solve the substantively similar issues
  Metered Contribution to ERCOT peak – 20%
    Rewards WGRs with wind resources more coincident with ERCOT peak

## Slide 12: Why?
Because of wind’s variable fuel supply, ERCOT manages wind as “net load” or negative load, making awind plus load ratio share appropriate
ERCOT’s Wind Ancillary Service study stated:
  “Unlike conventional generation, the electrical output of wind generation plants cannot be dispatched, but is inherently variable and imprecisely predictable. Thus, addition of wind generation resources increases the amount of variability and unpredictability that must be addressed in system operations. The integration of increasing amounts of wind generation capacity into the ERCOT system inevitably leads to changing requirements for ancillary services procurement” [1]
At the wind workshop for docket 37339, ERCOT staff declared “Any energy schedule from a wind resource is a forecast with associated uncertainty that must be covered by reserves.”
[1] GE Energy, Executive Summary, “Analysis of Wind Generation Impact on ERCOT Ancillary Services Requirements”, March 28, 2008.

## Slide 13: 2013 High Wind Week
Source: ERCOT’s August 20th presentation in workshop for Project 37339

## Slide 14: Response to Questions
What ancillary services are included?
  Responsive Reserves, Non-Spinning reserves, Regulation Up, & Regulation Down
Is the obligation based on installed capacity or metered energy?
  Metered Energy
Does the proposal include Reliability Credits?
  Yes. Although the specific credits and their values may be determined through the stakeholder process, reliability credits are an essential part of the proposed revision.

## Slide 15: Response to Questions (PUCT Staff)
Describe how the proposal meets the principle of cost causation.
  Cost causation assigns costs to operational characteristics that cause those costs, to create an incentive for those participants to reduce the costs. Because the reliability credits and tradable ancillary service obligations provide these incentives, the proposal is aligned with cost causation.

## Slide 16: Response to Questions (PUCT Staff)
What impact will this have on wind generation development?
  The proposal will create incentives for developers to invest early to qualify for all reliability credits. Existing generators will have the same incentives. These incentives will lead to a more reliable grid and mature wind development efforts in Texas.

## Slide 17: Response to Questions (PUCT Staff)
Are there incentives for meeting reliability concerns?
  Yes. The reliability credits provide these incentives
Is the proposal static or dynamic with relation to additional wind generation?
  Dynamic – the obligations for each generator will vary with:
    The reliability credits the WGR has qualified for
    The WGR’s share of total wind output
    Total ancillary service obligations
Does the proposal recognize geographic diversity?
  WGRs located with better load coincidence are eligible for an obligation reduction.

## Slide 18: Questions?

## Slide 19: Incremental Allocation

## Slide 20: Introduction
Seeks to apply the principles of cost causation to the allocation of ancillary services costs to wind generators by identifying the incremental amount of ancillary services that are required by ERCOT that are directly related to wind generation.
Incremental amounts of ancillary services necessary to accommodate wind generation are specifically identifiable in ERCOT’s methodology for determining the amount of required ancillary services

## Slide 21: Incremental Allocation of Reg Up and Reg Down (URS and DRS):
ERCOT calculates the increased amount of wind penetration each month and utilize tables provided by GE in their final report to ERCOT in the calculation of Regulation Service requirements.
The tables clearly indicate the incremental MW of URS and DRS that are required per 1000 MW of wind generation capacity[1].
The GE tables could easily be adapted to allocate ancillary services requirements to wind generators based upon installed MW.
1] 2010 ERCOT Methodologies for Determining Ancillary Service Requirements pgs 6 -7.

## Slide 22: Incremental Allocation of Non-Spin Reserves Service (NSRS):
Net Load is defined as the ERCOT load less wind generation.
Net Load uncertainty is then defined as the difference between the actual metered Net Load and the forecasted Net Load.
For the purpose of determining the amount of NSRS to purchase for each hour of the day during the upcoming month, ERCOT will determine the 95th percentile of the Net Load uncertainty using data from the 30 days prior to the study and the same month of the previous year

## Slide 23: Incremental Allocation of Non-Spin Reserves Service (NSRS):
ERCOT then requires an amount of NSRS such that the combination of NSRS and Regulation Up Services cover 95% of the calculated uncertainty from the Net Load analysis.
The wind uncertainty could then be determined as a percentage of the total net load uncertainty. To calculate this percentage, ERCOT would determine the load uncertainty as the 95th percentile of the Mid-Term Load Forecast (MTLF).
By subtracting the 95th percentile of the MTLF from the 95th percentile of the Net Load uncertainty, ERCOT would be able to determine the amount of Net Load uncertainty attributable to wind.

## Slide 24: Incremental Allocation of Non-Spin Reserves Service (NSRS):
Then, ERCOT would calculate the wind uncertainty as a percentage of the total Net Load uncertainty at the 95th percentile.
ERCOT would calculate the allocable portion of the 95th percentile amount of NSRS to wind.
ERCOT then allocates this to the wind generators based upon installed MW.
In a similar manner, ERCOT would determine the impact of wind on the net load bias. ERCOT will determine the average Net Load forecast error and subtract the average MTLF error such that the result is the average wind forecast error.

## Slide 25: Incremental Allocation of Non-Spin Reserves Service (NSRS):
Since average wind forecast error is a contributor to the Net Load bias, the percentage allocable to wind will be the average wind forecast error as a percentage of the average net load forecast error.
This percentage will then be multiplied by the amount that the load bias impacts the NSRS requirement.
  (Note that load bias impact on NSRS requirement is often less than the total calculated load bias due to the NSRS maximum requirement cap of 2000 MW.)
Table 1 uses actual values from January 2010 to estimate the wind allocation of NSRS under this methodology.
Table 2 uses actual values from February 2010 to estimate the wind allocation of NSRS under this methodology.

## Slide 26: Incremental Allocation of Responsive Reserves and Replacement Reserves (RRS, RPRS):
None. There is no allocation of these services to wind generation under the Incremental Allocation method because the ERCOT Ancillary Services Methodology does not identify wind generation as a contributor to incremental amounts of these services.

## Slide 27: Table 1: January 2010

## Slide 28: Table 2: February 2010

## Slide 29: Quick Comparison
 | Incremental | Wind Plus Load Ratio Share
Ancillary Services Included | URS, DRS, NSRS | All
Determinant | Installed Wind Capacity (MW) | Wind Production (MWh)
Reliability Credits | Not Proposed but Optional | Included

## Slide 30: Response to Questions (PUCT Staff)
Describe how this meets principles of cost causation.
  The Incremental Allocation methodology meets the principles of cost causation in that it only allocates the incremental amount of ancillary services to wind generators that are specifically identified as being caused by wind in the ERCOT Ancillary Services Methodology.
  ERCOT has increased its requirements for Ancillary Services in order to reliably integrate additional wind generation and has documented in its methodology those amounts incrementally attributable to wind generation.
What impact will this have on wind generation development?
  The impact on wind generation development is likely to be extremely small. The only impact on generation development related to this issue is the uncertainty associated with whether or not such an allocation will be implemented. Resolution of this issue will allow developers to include this cost in their pro-formas.

## Slide 31: Response to Questions (PUCT Staff)
Are there incentives for meeting reliability concerns?
  The incremental approach encourages accurate scheduling of wind generation. If it were possible to forecast and schedule perfectly accurately, there would be absolutely no allocation of any NSRS to wind generators under this methodology. Of course, we all understand that perfect scheduling would be difficult to achieve but the incentive to schedule accurately is still very much a part of this methodology.
  There are no reliability credit-backs currently contemplated in the Incremental Allocation methodology. The Incremental Approach was designed with the understanding that reliability concerns should be addressed through mandates and not through options to comply. Providing credits back to wind generators that are in compliant with mandatory reliability requirements is a false incentive.

## Slide 32: Response to Questions (PUCT Staff)
Is it static or is it dynamic with relation to additional wind generation?
  The Incremental Allocation method is dynamic relative to increased amounts of wind generation for the allocable Ancillary Services (URS, DRS, and NSRS).
Does it recognize geographic diversity?
  The Incremental Allocation methodology recognizes the beneficial aspect of geographic diversity through increased predictability of wind generation output. This increased predictability decreases the allocation of NSRS to wind generators.

## Slide 33: Questions?

## Slide 34: For WMS Consideration
Wind Plus Load Ratio Share Proposal
  Currently includes Reliability Credits
Incremental Allocation Proposal
  Does not currently include Reliability Credits but WMS could choose to include them