## Slide 1: NPRR210 Wind Forecasting Change to P50
Item 8, Technical Advisory Committee Meeting April 8, 2010

## Slide 2: Purpose of the NPRR
The P80 forecast is included in the original Nodal Protocols
  Deliberately under-forecasts wind
  Could cause ERCOT to overcommit during the DARUC process
This NPRR would revise that to the P50
  Should more accurately predict wind output
  Should drive RUC process to better commit resources
Sounds great right?

## Slide 3: Unintended Consequence
The capacity that is allocated to wind resources for RUC coverage is based on whichever forecast is used
DARUC does not modify this charge regardless of wind performance
  So if P50 shows 100MWs for a given farm and actual production is 20MWs, there is no allocation of DARUC if the WGR sold 100MWs of capacity service to the market
By definition the WGR will only provide the reliability service 50% of the time!!!
There are considerable penalties for providing this level of service (or lack thereof) on all other ancillary services
Conventional generators are charged RUC if there capacity is reduced in RT due to unit trips or derates
So while this should be enough to reconsider implementation of the NPRR there are other consequences

## Slide 4: Market Distortions and Uplift
Ideally the incentives would exist to for loads to hedge their risk in the Day Ahead Market and not carry it to real time
This allows for a much more efficient commitment
If this does not occur, ERCOT will be forced to RUC units on line to support local and ERCOT wide shortfalls
Overallocating capacity coverage to wind generators enhances this problem
  WGRs will now be able to sell additional capacity as RUC coverage to loads
  There is no tie between where the capacity is provided and where RUC is needed, so the load is not at risk
  ERCOT is then left to RUC the needed units on line
  At settlement, the load is covered from a RUC standpoint leaving the RUC charge to be uplifted to load as a whole
  When the market reaches “steady state”, to the extent RUC is procured, the WGRs will be collecting an uplift related to that charge

## Slide 5: Example
Capacity needed here
Capacity “supplied” here
Capacity is needed in HLZ
A 500 MW load (1%) opts to cover their HLZ load with WGR capacity instead of DAM purchase
ERCOT strikes 500MWs of capacity in Houston to cover the shortfall (note that RUC likely does not select the most efficient units to start)
Costs are now uplifted marketwide and the 500 MW load only picks up 1% of that cost

## Slide 6: Morgan Stanley Comments
Morgan Stanley’s comments to this NPRR remove the use of the P80 or 50 forecast for DARUC
Original use of the method was an inadequate compromise meted out in the early stages of nodal development (Omni basement TNT days)
The MS changes place WGRs on the same footing as conventional generators
  They can sell what they feel comfortable they will provide in real time
  If the wind isn’t there, they must pay for the RUC capacity they sold (just like a unit trip)
Method does require a fairly simple system change, so wouldn’t be available at go live but could be included with other RUC changes if any were needed

## Slide 7: Recommendation
TAC should in some way incorporate the changes created by the MS comments
  The move to the P50 forecast could also be delayed until implementation of these changes
  ERCOT has committed to using the bias offset method found in the current ancillary services procedures document to curb overcommitment of RUC resources in the mean time