## Slide 1: Methodology for Demand Forecasts for Bandera Electric Cooperative, Inc.
Brian D. Bartos, P.E.
Manager, Engineering
Presented to
ERCOT Reliability & Operations Subcommittee
June 10, 2010

## Slide 2: General Overview of Forecasting at BEC
Forecasts are prepared by BEC staff using the best available information.
  In rare cases, data has to be estimated
These forecasts are provided to both ERCOT and LCRA as required.
  ERCOT utilizes this data in their overall load forecasts and reserve margin calculation
  LCRA utilizes this data in their planning process
The criteria used to determine the validity of each forecast is:
  “Is the forecast reasonable and supportable”.

## Slide 3: Methodology
Review past historical non-coincident data for each substation transformer.
Factor out any load which may have been abnormally configured or step-loads.
Using the past six (6) years of historical data, perform a weighted average least squares linear projection to determine slope (growth rate).
Apply growth rate to previous year peak demand.
If growth calculates negative, hold the load at previous year value.

## Slide 4: Forecast Adjustments
Make adjustments to account for block load additions or other load transfers.
Make adjustments due to past weather conditions.
  Look at Cooling Degree Days / Heating Degree Days
1,969
1,870
1,549
1,572
1,630
37 Year Average: 1,691
1,840
1,890
A Cooling Degree Day is a unit used to relate the day's temperature to the energy demands of air conditioning. Cooling Degree Days are calculated by subtracting 65 from a day's average temperature. Cooling Degree Days can be used to compare the current summer to past summers. It can also be used to compare the heat in one part of the country with another.
Year
Cooling Degree Days (June-Sept)
Source: Boerne NOAA Weather Station
“Hotter Than Normal”
“Cooler Than Normal”
1,623

## Slide 5: Summer & Winter Non-Coincident Peak Demand
Historical
Projected
124,833
136,215
132,421
143,804
178,681
192,094
121,035
115,927
127,497
Winter
Baseline Projected Increase of 6,706 kW of Non-Coincident Demand per Year or 4.2% growth compared to 5.0% a year ago.
Year
Non-Coincident Demand (kW)
Mild Weather, Slower Economy
Severe Weather, Strong Economy
Summer
Baseline Projected Increase of 3,794 kW of Non-Coincident Demand per Year or 3.1% growth compared to 4.9% a year ago.
163,474
158,563
131,388
165,269
120,657

## Slide 6: Verification by Member Class
To help verify the forecasts, BEC determines a forecast for:
  Coincident Peak (summer / winter)
  Member classes
  Total Meters
  Total Energy
The criteria used to determine the validity of each forecast is:
  “Is the forecast reasonable and supportable”

## Slide 7
QUESTIONS