## Slide 1: Expectations for COP Entries
NATF
June 23, 2010

## Slide 2: Principles
ERCOT expects each QSE to submit a COP that describes the Resource Status and resource capabilities based on the QSE’s anticipated or expected operating conditions for each of its Generation Resources and Load Resources in each of the hours covered by the updated COP.
QSEs and WGR owners should provide their best estimate for HSL consistent with expected meteorological, regulatory and physical conditions associated with the WGR for all hours in the COP reporting period.

## Slide 3: Combined Cycle Trains
The following rules should be applied by the QSE when reporting the Resource Status for CCGR configurations in its COP:
  For those COP reporting hours that the QSE expects to commit a CCGR configuration for ERCOT operations, the QSE should show the committed CCGR configuration to be in an appropriate On-Line Resource Status (i.e. ON, ONREG etc). All other CCGRs configurations in the CCT should be shown with a Resource Status of OUT in that hour.
  If the QSE does not intend to commit a CCT in a COP reporting hour, the CCGR configurations that are available should be reported in the COP as OFF and those CCGR configurations that are unavailable should be reported as OUT.
  If a CCGR configuration is RUC committed in a COP reporting hour, the QSE should show the Resource Status for the committed CCGR configuration as ONRUC. All other CCGR configurations should be reported as OUT in a RUC committed hour.

## Slide 4: RUC
For Resources that are committed in specific hours of an Operating Day by a RUC process for the purpose of meeting ERCOT System capacity requirements
  the QSE must report a COP Resource Status of ONRUC in the commitment hours.
  In each RUC commitment hour the Ancillary Service Resource Responsibility Capacity for each Ancillary Service must equal to zero MW. Failure to do so will result in the COP update being rejected.
For Resources that are committed by a RUC process for the purpose of providing a specified Ancillary Service:
  the QSE must report a Resource Status of ONRUC in the commitment hours.
  In each RUC commitment hour the QSE must report in its COP the commitment specified Ancillary Service Resource Responsibility in the amount specified in the ERCOT RUC commitment. Failure to do so will result in the COP update being rejected.
  Resources that receive a RUC instruction to provide an Ancillary Service may not move that AS Responsibility to another Resource or QSE during the RUC commitment period.

## Slide 5: Timing of COP Updates
Except for Forced Outages, QSEs are expected to honor the Generation Resource’s temporal constraints when updating the COP.
For example, the QSE is expected to honor the temporal constraint for start-up time. In other words the status change hour must be sufficiently far in the future such that if ERCOT rejects the de-commitment ----- sufficient time remains to start the Generation Resource if needed by RUC.

## Slide 6: Questions
Provide comments by COB June 30, 2010.
Review comments and revisions at July 9 NATF.