## Slide 1: Nodal Credit
DAM Non-Business Day Treatment of Available Credit Limit (ACL)

## Slide 2: Issue & Time Constraints
DAM was run over non-business days for the first time with credit constraints over the weekend of August 14-16
  A significant amount of credit was consumed, resulting in some CPs being constrained in the Monday DAM. Key drivers include:
    Data impact –very high values used for the 95% price differences between RT and DA applied to Energy Only Offers and Three Part Offers
      Results from market trials
      not expected to be the norm after go live
    Exposure elements –ACL is consumed for Three Part Offers over non-business days when it is not consumed in the DAM on business days
  ERCOT believes it is appropriate for this topic to be reviewed by the market and possibly consider whether a revision to the current methodology is warranted
    Any clarification must be finalized quickly to achieve implementation prior to go live

## Slide 3: Issue & Time Constraints
Proposed review schedule
  Thursday, August 26 - Review with MCWG/CWG
  Monday, August 30 –Review with MCWG/CWG
  Tuesday, August 31 –Potential vote by NATF
  Thursday, September 2 –Review by TAC

## Slide 4: Current Practice
On Non-Business days, MMS reduces the latest ACL by the following each day until a new ACL is received from credit.
  Energy-only offers: ACL is reduced by the product of the cleared quantity of the offer times the 95th percentile of the positive hourly difference of the Real-Time Settlement Point Price and Day-Ahead Settlement Point Price over the previous 30 days for the hour.
  Energy bids: ACL is reduced by the product of the cleared bid quantity multiplied by the cleared bid price.
  Three part energy offers: ACL is reduced by the product of the cleared quantity of the offer times the 95thpercentile of the positive hourly difference of the Real-Time Settlement Point Price and Day-Ahead Settlement Point Price over the previous 30 days for the hour.
  PTP Obligation bids: For each cleared PTP Obligation Bid, the ACL is reduced by the cleared bid quantity multiplied by the sum of the cleared bid price, if positive, plus the 95th percentile of the hourly positive price difference between the source Real-Time Settlement Point Price minus the sink Real-Time Settlement Point Price over the previous 30 days for the hour.
  Procured AS: For procured Ancillary Services, the ACL is reduced by the product of the cleared quantity of Ancillary Service not self-arranged times the hourly MCPC for that Ancillary Service for that hour.

## Slide 5: Recommendation, Pt 1
Activity Type | Current | Recommendation | For go-live?
Three-Part Offers | 95%ile of the positive diff between RT and DA prices | Reduce exposure by qty * price | Yes
Energy Bids | Increase exposure by qty * price | Same | Yes
Energy-only Offers | 95%ile of the positive diff between RT and DA prices | Same spread & reduce exposure by qty * price * e2 | Yes

## Slide 6: Recommendation, Pt 2
Activity Type | Current | Recommendation | For go-live?
PTP Bids | by the cleared bid quantity multiplied by the sum of the cleared bid price, if positive, plus the “u”th percentile of the hourly positive price difference between the source RTSPP minus the sink RTSPP | Same | Yes
CRRs | Ignored | Same | No
Ancillary Services | Cleared qty not self-arranged * price | Same | Yes

## Slide 7: Proposed Motion
“Move that ERCOT reduce ACL for the DAM on non-business days as it does today, except:
ERCOT should reduce exposure from three part offers by the product of price times qty for each cleared transaction
2) No longer increase exposure for three part offers based on the difference between historic DAM and RTM prices
3) Reduce exposure from energy only offers by the product of price, qty, and e2. e2 is set by ERCOT for each counterparty, and only counterparties with favorable pre-DAM treatment qualify this reduction.“