## Slide 1: DAM Performance Issues with CRR Offers
Steve Reedy
Market Design Manager
TAC
2 September 2010
Notes: <number>

## Slide 2: Agenda
Description of issue
How we got here
Possible Immediate and Long-Term Solutions
Going Forward
Technical Advisory Committee
2 September 2010
Notes: <number>
<number>

## Slide 3: Description of issue
  This is NOT a design issue; it is a Performance Issue
  “Theory, experience elsewhere and ERCOT trials suggest the DAM can take hours to solve if PTP Option Bids involve > a hundred (or so) source-sink pairs” (Risk Analysis Report)
DAM performance is degraded when the number of distinct source/sink pairs of CRR offers in combination with the number of contingencies becomes excessive
e.g.> 150 source/sink pairs x 2500 contingencies = 375000
The performance bottleneck occurs in the Power flow and Contingency Analysis module (NSM)
Cause of performance degradation is sheer volume of computations involved in running Contingency Analysis on CRR Offers
Technical Advisory Committee
2 September 2010

## Slide 4: DAM Workflow Process
Read Input Data
Pre-Process Data
NSM
Power Flow, Contingency Analysis
NCUC
Commitment, Dispatch & Prices
Publish Results
Iterative process
DAM process needs to complete in approximately 3 ½ hours: (10:00 AM – 1:30 PM)
-3 ½ hour timeframe includes time for review of results by ERCOT before publishing
-3 ½ hour timeframe includes possibility of rerunning DAM in case of AS insufficiency
        Based on100 distinct source/sink combinations, 2600 contingencies:
Average 6 iterations between NSM & NCUC
Average NSM execution time ≈ 8 minutes per iteration: Total= 48 minutes
Average NCUC execution time ≈ 20 minutes per iteration: Total= 2 hours
VERY TIGHT TIMELINE
Technical Advisory Committee
2 September 2010

## Slide 5: Power Flow and Contingency Analysis
Determines if there are any transmission violations due to the awarded quantities of three-part offers (3PO), DAM energy only offers/bids, PTP obligation bids and CRR offers
  Uses base case with approximately 2500 contingencies
3PO, DAM energy only offers/bids, PTP obligations are such that superposition principles hold so they can be added together
  Computation is the sum of 1 Base Case (larger flow computation) with 2500 Contingency Power (incremental flow computations) per hour per iteration:
    (1 + 2,500)*24 = 60,024 power flows per iteration
However for CRR offers superposition principles do not hold and hence the
  Computation is the product of number of distinct source/sink combinations in all the CRR Offers and number of contingencies +1 Base Case per hour per iteration:
    number of distinct source/sink combinations * (1 + 2500)*24 power flows per iteration
    If the number of distinct source/sink combinations = 150 then the power flows per iteration is approximately 9 million
    If six iterations are needed to solve then, just for CRR Offers, the number of power flows becomes 54 million
Technical Advisory Committee
2 September 2010

## Slide 6: How We Got Here
  System performance issues were identified last year and major changes were implemented to address this
  Presented in 2009 at TPTF/NATF limitations for DAM Energy Only Offers/Bids, PTP Obligations Bids and CRR Offers.
  Limit on CRR Offers = 2000
  Four releases focused to address these performance issues
ERCOT found satisfactory DAM performance based on assumption of CRR Offers only sinking to NOIE load zones
  With only 4 NOIE load zones, performance improvements and the 2000 limit on CRR offers sufficiently limited the number of distinct source/sink combinations across all the CRR Offers in DAM
In Market Trials, there have been no reported issues with DAM performance due to CRR offers.
During risk assessment, realized that CRR offers into the DAM are not restricted to the NOIE load zones (i.e., between any settlement points)
Technical Advisory Committee
2 September 2010

## Slide 7: CRR PTP Offers: ERCOT’s Action Plan
For Go-Live: Immediate Mitigation
MMS – DAM
Potential software based improvements:
  Make changes to the software which could allow the NSM processes to run faster by enabling parallelization
      DAM - Network Analysis Module
      Three to four weeks are required to determine the performance improvement of this option.
      Additional time will be required to fully verify the functional results.
  Utilize newer math libraries in the software that may improve performance
      DAM – Unit Commitment, Dispatch and Pricing
      At least four weeks are required to determine the performance improvement of this option.
      Additional time will be required to fully verify the functional results
Potential hardware based improvements:
  Upgrade to faster processors. This is being tested at ERCOT this week to determine the magnitude of performance improvement
      Six to eight weeks required to migrate the ERCOT production environments to this processor se t if this option is pursued
Post Go-Live: Long Term Solution
DAM - Network Analysis Module
Potential long term software based improvement
  Further enhance parallel computation capability of Network Analysis Module (NSM)
    Design change:
      Allow network analysis for each hour of the study period to be done in parallel
      Introduce new process controller that manages these parallel network analysis modules
      Manage the interface of passing transmission constraints after network analysis for all 24 hours back to the unit commitment engine
    Long term option, not viable before go live
Technical Advisory Committee
2 September 2010

## Slide 8: Completed Actions
Three CRR Offer Stress Test Scenarios Run in Market Trials
  8/30 -126 pairs, 8/31 – 114 pairs, 9/1 – 164 pairs
  NSM run time as expected
  NCUC run time significantly longer than expected
    Causes under investigation
ERCOT performed new estimate on number of CRR paths
  Looked at all Resources associated with NOIE QSEs
  Combined with appropriate Load Zones
  Added in all possible Hub-LZ combinations
  Approximately 200 total paths
First test of faster processor solution run
  ~33% reduction in processing time on test case
  More testing to be done on Market Trials stress test cases
Technical Advisory Committee
2 September 2010

## Slide 9: Going Forward
NOIE allocation eligibility due to ERCOT on September 8, 2010
NOIEs to submit expected CRR offer paths on or before September 8, 2010
ERCOT to analyze expect offer path to current CRR capabilities
  Done (~200)
Follow up meeting with NOIEs during the week of September 13, 2010 to discuss allocation results and possible actions
ERCOT to coordinate CRR Offer stress test scenario in Market Trials
  Done
2 September 2010
Technical Advisory Committee

## Slide 10
Questions ?
2 September 2010
Technical Advisory Committee

## Slide 11
Appendix
2 September 2010
Technical Advisory Committee
Notes: <number>

## Slide 12: Superposition Principle
3PO, DAM energy only offers/bids, PTP obligations can cancel each other out
  100 MW injected at point A and 100 MW withdrawn at point A put 0 MW on the system
  75 MW A to B PTP Obligation and 75MW B to A PTP Obligation put 0 MW on the system
  Can be modeled all at once
PTP Options (CRR Offers) do not cancel each other out
  75 MW A to B CRR Offer and 75 MW B to A CRR Offer put 75 MW on the system each direction.
  Need to be modeled separately
2 September 2010
Technical Advisory Committee