## Slide 1: NPRR 278 EILS Self-Provision Settlement & Other Issues
WMS Sept. 22, 2010
PRS Sept. 23, 2010
Paul Wattles, ERCOT Staff

## Slide 2: Primary Issue Summary
WMS-PRS
Sept. 22-23, 2010
ERCOT Staff and market participants identified inequities in existing settlement equations relating to EILS Self Provision
Current protocols under-value self-provided EILS by calculating obligations of self-providing QSEs as a percentage of the total unadjusted, originally procured EILS capacity
  Should be based on delivered capacity (adjusted for availability and/or performance evaluations)
  This also results in miscalculation of the weighted average price used to credit EILS self-provision
Bottom line: overstates self-providing QSE’s obligation and under-values its self-provided capacity

## Slide 3: Primary Issue Summary (cont’d.)
WMS-PRS
Sept. 22-23, 2010
ERCOT Staff identified additional potential self-provision settlement issues with the existing language:
  Equations do not accurately credit self-provision from more than one QSE self-providing EILS when some self-provide greater than their obligation and others self-provide less than their obligation
  Not a problem yet, but could be in the future
NPRR 278 establishes the concept of a ‘self-provision capacity upper limit’
  Determined for all self-providing QSEs through simultaneous linear equations
  Helps self-providers fine-tune their offers during procurement when less than 1,000 MW is procured
  Ensures equitable settlement for all self-providers

## Slide 4: Other Issues
WMS-PRS
Sept. 22-23, 2010
NPRR 278 is also a vehicle for addressing other issues with EILS:
Current language requires ERCOT to build individual default baseline models for each member of an EILS Load aggregation
  AMI metering could bring much larger aggregations that would burden ERCOT systems without improving baseline accuracy
  Revised language would allow ERCOT the option of summing the members’ interval usage prior to building the baseline model
Conforms Nodal language to current Zonal practice by allowing fractional MW offers (to tenths of a MW) as long as the 1 MW offer minimum, prescribed by Rule, is met
Allows ERCOT to reduce payment for EILS Loads that fail two consecutive Load-shed tests
Establishes QSE EILS portfolio performance requirements

## Slide 5: Other Clarifying Changes
WMS-PRS
Sept. 22-23, 2010
The draft NPRR also makes a number of changes that ERCOT considers to be clarifying in nature
These changes are described in detail in the Revision Description section of the NPRR

## Slide 6: Status and Proposed Timeline
WMS-PRS
Sept. 22-23, 2010
Previewed at WMS on June 16
Draft discussed in detail at DSWG on Sept. 10
Posted on Sept. 16
  CEO Review and Impact Analysis are complete
Seeking WMS endorsement Sept. 22
PRS first consideration Sept. 23
Seeking PRS IA Review and approval on Oct. 21
TAC on Nov. 4
Board on Nov. 16
Effective date of Feb. 1, 2011
  Matches cutover date for all EILS Nodal Protocol sections
  Coincides with Feb.-May 2011 EILS Contract Period
November approval will provide ample time to update EILS Technical Requirements to be consistent with NPRR

## Slide 7: Questions?
WMS-PRS
Sept. 22-23, 2010
ON
OFF