| NPRR Number |  | NPRR Title | Requirement to Post CRR Options and Obligation Quantities Cleared in DAM or Taken to Real Time |
| --- | --- | --- | --- |
| Date Posted |  |
| Nodal Protocol Sections Requiring Revision (Include Section No. and Title) | 4.5.3 Communicating DAM Results |
| Revision Description | Adds language to specify the need for ERCOT to post quantities of Point-to-Point (PTP) Options and PTP Options with Refund which were not cleared in the Day-Ahead Market (DAM) and taken to Real Time for settlement. Also requires posting of the PTP Obligations which were cleared in the DAM. |
| Reason for Revision | The posting of these cleared quantities by hour by settlement point are necessary for Market Participants to adequately evaluate the results of the DAM including the accuracy of the Network Model used for the DAM. |
| Overall Market Benefit | Greater transparency of the DAM calculations will increase DAM participation and market efficiency. |
| Overall Market Impact | Increased confidence in the accuracy of the DAM market which will likely increase participation in the DAM. |
| Consumer Impact | Increased participation in the DAM could lead to lower prices for consumers. |
| Credit Implications (Yes or No, and summary of impact) | None |
| Submitter Justification for Necessity Prior to the Texas Nodal Market Implementation Date | The reporting of these volumes is particularly important during the early implementation of the market as market outcomes need to be verified for accurate Network Modeling parameters and execution of the DAM co-optimization. |
| CEO Determination (To be completed by ERCOT) |  |

| Quantitative Impacts and Benefits |
| --- |
| Assumptions | 1 |  |
|  | 2 |  |
|  | 3 |  |
|  | 4 |  |
| Market Cost |  | Impact Area | Monetary Impact |
|  | 1 |  |  |
|  | 2 |  |  |
|  | 3 |  |  |
|  | 4 |  |  |
| Market Benefit |  | Impact Area | Monetary Impact |
|  | 1 |  |  |
|  | 2 |  |  |
|  | 3 |  |  |
|  | 4 |  |  |
| Additional Qualitative Information | 1 |  |
|  | 2 |  |
|  | 3 |  |
|  | 4 |  |
| Other Comments | 1 |  |
|  | 2 |  |
|  | 3 |  |
|  | 4 |  |

| Sponsor |
| --- |
| Name | Sherry Looney Sherry.looney@luminant.com Luminant Energy Company, LLC 214-875-9278 469-688-7607 Investor-Owned Utility (IOU) |
| E-mail Address |  |
| Company |  |
| Phone Number |  |
| Cell Number |  |
| Market Segment |  |

| Market Rules Staff Contact |
| --- |
| Name |  |
| E-Mail Address |  |
| Phone Number |  |

Congestion experienced in the DAM is a function of all the generation sources and load sinks that are utilizing the transmission system.  The intent of the Nodal Protocols that is embodied in Section 4.5.3 (2) (f & g), has been to provide transparency to the market regarding the Settlement Point specific sources of energy bought and energy sold, without regard to the form that energy was procured in the DAM (e.g., 3-Part Offers that were struck, load zone bids that were filled, PTP Obligation bids that were filled, PTP Options carried to Real Time that were filled, etc.) by no later than 1330 on the MIS Public Area.  Additionally, the intent of the Nodal Protocols contained in Section 7.5.3.1 (2) (a, b, c, & d), has always been to provide transparency following the CRR auction to the source and sink pair total MWs for all PTP Options, PTP Obligations, FGRs, and the identity of account holders who were awarded CRRs both in and before the CRR Auction.  The combination of these two Nodal Protocol references, establish:

- The location of all of the sources and sinks of energy that utilize the available transmission system in the DAM is expected to be publicly disclosed without delay after the DAM

- The holding of CRRs, without regard to whether they are CRR Options or Obligations, is expected to be publicly disclosed without delay after the CRR Auction

If ERCOT does not disclose all of the specific sources of energy bought and energy sold by Settlement Point, without regard to what form that energy was procured in the DAM, it deprives the broader set of market participants from being able to utilize the transparency that was intended in the Nodal Protocols to validate that the DAM is performing as expected, as well as, formulate their price-sensitive bids and offers in the DAM.  Currently, ERCOT is withholding the disclosure of CRR Options being carried to real time in the DAM by the Non-Opt-In Entities  (NOIEs) which has prevented market participants from being able to understand  the vast majority of the congestion that is being observed in the DAM Market Trials that is not occurring in Real Time.  On some days during the Market Trials, there has been in excess of 100 binding constraints in the DAM, with less than 5 or 10 binding constraints shown in Real Time.  The large number of binding constraints in the DAM results in inaccurate pricing signals which erodes market participant confidence in the validity of the results of the DAM execution.

Posting of all of the energy volumes transacted at each Settlement Point fulfills the original intent of the posting requirements envisioned in the Nodal Protocols and will allow more comprehensive evaluation of the DAM results by all market participants.

Proposed Protocol Language Revision

4.5.3          Communicating DAM Results

(1)        As soon as practicable, but no later than 1330 in the Day-Ahead, ERCOT shall notify the parties to each cleared DAM transaction (e.g., the buyer and the seller) of the results of the DAM as follows:

(a)        Awarded Ancillary Service Offers, specifying Resource, MW, Ancillary Service Type, and price, for each hour of the awarded offer;

(b)        Awarded energy offers from Three-Part Supply Offers and from DAM Energy-Only Offers, specifying Resource (except for DAM Energy-Only Offers), MWh, Settlement Point, and Settlement Point Price, for each hour of the awarded offer;

(c)        Awarded DAM Energy Bids, specifying MWh, Settlement Point, and Settlement Point Price for each hour of the awarded bid;

(d)        Awarded CRR Offers (PTP Options and PTP Options with Refund), specifying CRR identifier(s), number of CRRs in MW, source and sink Settlement Points, and price, for each Settlement Interval of the awarded offer; and

(e)        Awarded PTP Obligation Bids, number of PTP Obligations in MW, source and sink Settlement Points, and price for each Settlement Interval of the awarded bid.

(2)        As soon as practicable, but no later than 1330, ERCOT shall post on the MIS Public Area the hourly:

(a)        Day-Ahead MCPC for each type of Ancillary Service for each hour of the Operating Day;(b)            Day-Ahead Settlement Point Prices for each Settlement Point for each hour of the Operating Day;

(c)        Day-Ahead hourly LMPs for each Electrical Bus for each hour of the Operating Day;

(d)        Shadow Prices for every binding constraint for each hour of the Operating Day;

(e)        Quantity of total Ancillary Service Offers received in the DAM, in MW by Ancillary Service type for each hour of the Operating Day;

(f)	ERCOT shall post the energy bought in the DAM consisting of the following:

i)	The total quantity of awarded DAM Energy Bids (in MWh) bought in the DAM at each Settlement Point for each hour of the Operating Day;

ii)	The total quantity of awarded PTP Obligation Bids sink (in MWh) cleared in the DAM at each Settlement Point for each hour of the Operating Day; and

iii)	The total quantity of sink (in MWh) from the PTP Options that were declared before DAM execution by the NOIE to be settled in Real-Time and not cleared in the DAM, at each Settlement Point for each hour of the Operating Day; and

(g) 	ERCOT shall post the energy sold in the DAM consisting of the following:

i)	The total quantity of awarded DAM Energy Offers (in MWh), from Three-Part Supply Offers and DAM Energy Only Offers, bought in the DAM at each Settlement Point for each hour of the Operating Day;

ii)	The total quantity of awarded PTP Obligation Bids source (in MWh) cleared in the DAM at each Settlement Point for each hour of the Operating Day; and

iii)	The total quantity of source (in MWh) from the PTP Options that were declared before DAM execution by the NOIE to be settled in Real-Time and not cleared in the DAM, at each Settlement Point for each hour of the Operating Day; and

(h)	Aggregated Ancillary Service Offer Curve of all Ancillary Service Offers for each type of Ancillary Service for each hour of the Operating Day.