## Slide 1: Real-Time CRR and Energy Settlements
ERCOT Technical Advisory Committee
January 6, 2011
Dan L. Jones
Vice President
Director, ERCOT IMM
Potomac Economics

## Slide 2: Background
LMPs are the locational prices produced in each SCED run
SPPs are the locational prices for each Settlement Interval calculated using LMPs weighted by various energy data depending on the location
If there is no congestion in a SCED run, all LMPs will be identical
If there is no congestion in any SCED run contained in a Settlement Interval, SPPs can vary by location even though the LMPs in each SCED run are identical

## Slide 3: Background
Section 7.1(1): A Congestion Revenue Right (CRR) is a financial instrument that entitles the CRR Owner to be charged or to receive compensation for congestion rents that arise when the ERCOT Transmission Grid is congested in the Day-Ahead Market (DAM) or in Real-Time.
Section 7.9.2
  Real-time CRR settlement formulas are based upon SPPs
  This means that CRR settlement formulas can produce non-zero values in Settlement Intervals when transmission congestion does not exist in any of the SCED runs contained in that Settlement Interval

## Slide 4: Examples
Settlement Interval 10:15 on 12/21/10. There was no transmission congestion in any SCED cycle in this Settlement Interval; therefore the LMPs for all locations were identical in each SCED run. However, the SPPs for this Settlement Interval range from $45.89 to $100.68 per MWh.
Settlement Intervals 05:15 – 21:00 on 12/21/10. There was no transmission congestion in any SCED cycles in this range of Settlement Intervals; therefore the LMPs for all locations were identical in each SCED run. The chart to the right shows the range of SPP differences in each settlement interval.

## Slide 5: Proposed Changes for Consideration
Revise RT CRR settlement formulas in Section 7 to align CRR settlement with LMP differences rather than SPP differences
Revise RT Energy Imbalance formulas in Section 6 to align with energy settlements that would occur if Settlement Intervals were based on SCED intervals
  May be limited in application to Resource Nodes
  ERCOT Staff and IMM have developed some detailed proposed changes for consideration by the appropriate committee