## Slide 1: Option 2 Summary
Wes Woitt
CenterPoint Energy
2010 SSWG Chair

## Slide 2: Option 1 from Transmission Planner Point of View
Planning Ready Case
Topology Processor Case
Ratings / Impedance Same

## Slide 3: Option 2
Using an already created SSWG case as the seed case for MOD to create 2012 Data Set A
Includes an ongoing commitment by TSPs and ERCOT to compare the Topology Processor (TP) case with an SSWG case and resolve or document differences in order to achieve consistency between planning and operations cases. The process of documenting the differences will be developed by the Planning Working Group. The PLWG will develop and document the tolerances for the differences.
Option 2 to continue until SCR759 and SCR760 are fully vetted and implemented as required.
Option 2 to continue until any additional changes to the IMM or TP are fully vetted and implemented as required. Additional changes must be submitted as SCRs by July 1, 2011.
Option 2 to continue until SSWG reviews a TP case and endorses the TP-seed process for producing Planning Cases. This endorsement will move the process to Option 1.
Under this option Planning Go-live is expected to be implemented by August 1, 2011 with the posting of the 12 DSA cases.

## Slide 4: Option 2
TSP
Profiles
Topology from Existing Planning Case
TSP Review
Case complete?
Case Posted
Yes
No
TSPs submit
Change via MOD
NMMS db
ERCOT Topology Processor
(TP)
ERCOT/TSP Network Model update via NOMCR
CRR Top Output
Planning Case Output
ERCOT
Model on Demand
(MOD)
TSP Future PMCR
ERCOT Dispatch
Profile
Spreadsheet Comparison

## Slide 5: Brief Review of ‘Standard’ PMCR
Planning Model Change Request: Method to input changes to the model in the Model On Demand (MOD) software.
‘Standard’ PMCR – reading in data which does not exist in the Topology Processor (TP) output or makes modifications to data in the TP output
‘Standard’ PMCRs are not related to any future projects
‘Standard’ PMCRs are really ‘TP Deficiency’ PMCRs

## Slide 6: Option 2
If SCR760 is approved, ERCOT estimates completion of most items in 2012
Option 2 bridges the gap between now and 2012 (or whenever SCR760 items are fully implemented)
More accurate than Option 1
Significantly less burdensome on TSPs than using Option 1 in 2011 (No Standard PMCRs)

## Slide 7: Planning Go-live
Data Set A and Data Set B cases will be created by SSWG in 2011. The question is what method will be used.
April 1, 2011 Go-live date
  Nothing truly happens on April 1, as opposed to Dec 1 Nodal Go-live
  Basically corresponds to beginning work on Data Set A cases
Using Option 2, ‘Planning Go-Live’ occurs by August 1, 2011 with the posting of the Data Set A cases

## Slide 8: Consistency
Per Nodal Protocols 3.10.2, “ERCOT shall develop models for annual planning purposes that contain, as much as practicable, information consistent with the Network Operations Model.”
With Option 2, the plan to ensure consistency includes:
  Spreadsheet checks
    Ratings
    Impedances
    Topology
  Resolve differences with NOMCRs or PMCRs
  Document remaining differences for market

## Slide 9: Spreadsheet Comparison – Oct 2010 Branch Comparison
Total Number of branches in SSWG base case but not in TP case | 1454
Branches in SSWG case & not in TP case due to TP BC/BO branches | -467
Branches in SSWG case with different IDs that can be matched by IMM ID changes or SSWG ID changes | -277
3 winding transformers with different IDs/ tertiary busses | -251
Branches in SSWG but not in TP due to additional busses in TP case. (Topology is virtually identical) | -240
Branches in SSWG case that can change to match TP (RARF differences) | -160
Topology Differences | 59
Case Comparison between Topology Processor (TP) and 10FAL1 case
Branches in 10FAL1 case without a match in TP case
Observed explanation for the majority of these mismatches
Actual topology differences are 59 (<1% of all branches in ERCOT)

## Slide 10: Branches in SSWG case not matching the TP case due to BC/BO branches. (467 branches)
SSWG Case:
Topology Processor Case:

## Slide 11
Branches in SSWG case not matching the TP case due to BC/BO branches. (467 branches)
SSWG Case:
Topology Processor Case:

## Slide 12: There are 277 branches in the SSWG case that did not match the TP case due to an ID difference. (Does not include BC/BO branches)
SSWG Case:
Topology Processor Case:

## Slide 13
Branches in SSWG case but not in TP case due to additional TP busses. Topology is virtually identical.
(240 branches not matching)
Example:
SSWG Case:
Topology Processor
Case:

## Slide 14: Transformer branches in SSWG Case, “missing” in TP Case. (251 Branches)
SSWG Case:
Topology Processor Case:
Example of 2-winding transformer modeled as a 3-winding in TP case

## Slide 15: Spreadsheet Comparison – Oct 2010 Ratings Differences
From ERCOT Nov ROS presentation
164 ratings differences
  72 GSUs (Data from RARFs, TSP can change SSWG case)
  91 Autos
  1 Transmission line

## Slide 16: Spreadsheet Comparison – Oct 2010 Impedance Differences
From ERCOT Nov ROS presentation
456 impedance differences
  103 GSUs (Data from RARFs, TSP can change SSWG case)
  101 Autos (Possible TP calculation – may have been rectified since)

## Slide 17: Summary
Option 2 is the bridge to get to Option 1 (with the items in SCR760 fully implemented)
Option 2 uses new Model On Demand tool
Option 2 uses Topology Processor, just in a different way than ERCOT envisioned
Option 2 meets Protocol requirements
TSPs were unanimous in their support for Option 2 at Dec 15 meeting