## Slide 1: ERCOT Protocols 11.4.4.2 Gray Box Language
February 08, 2011
NPRR 208 Formula Discussion
Don Tucker
Manager Settlement Metering

## Slide 2: 11.4.4.2 (2) AML for ESI IDs with wind generation shall be adjusted as follows
NOIE DRG Settlements TF update to COPS
February 08, 2011
For ESI IDs with non-IDRs installed, AML shall be reduced for excess generation from ESI IDs with wind generation equal to or lower than the DG registration threshold behind the meter where there is a meter that measures excess energy flow into the ERCOT System in a separate register. Only ESI IDs that have been assigned a wind profile segment as specified in the Load Profiling Guide Appendix D, Profile Decision Tree, shall be eligible for this reduction.
  Intervals beginning 0800 and ending 2000 CPT (spanning (48) 15-minute intervals) shall be reduced by the following amount:
    Wind_adjust = kWh_gen * .65 / (read_days * 48)

## Slide 3: 11.4.4.2 (2) AML for ESI IDs with wind generation shall be adjusted as follows
NOIE DRG Settlements TF update to COPS
February 08, 2011
  All other intervals in the day (the remaining 48 intervals) shall be reduced by the following amount:
    Wind_adjust = kWh_gen * .35 / ((read_days * 48) + DST adjust)
  For days affected by day-light savings time adjustments, 48 in the above equation should be reduced to 44 or increased to 52, as appropriate. (delete this)
    Where :
      wind_adjusti = the Reduction for wind excess generation for interval i in kWh
      kWh_gen = Actual (measured) kWh flowing into the Distribution System (out-flow from the Premise) in kWh
      read_days = Number of days in meter read period in days
      DST adjust = Daylight Savings Time Adjustment: Spring DST = -4; Fall DST = 4
N/A

## Slide 4: Allocated Energy Based on Formulas
NOIE DRG Settlements TF update to COPS
February 08, 2011