## Slide 1: QMWG Update to WMS
March 9, 2011
S. Looney

## Slide 2: Assignment from PRS – Discussion of NPRR308, Deployment Procedures for NSRS
NPRR308 adds requirement for NS deployment to respect minimum online and offline requirements from RARF
Current 30 minute NS product allows for Resource to remain online to honor minimum run time.
NS responsibility for zero to LSL will be relieved
QSE’s responsibility to provide the NS responsibility during the minimum offline period for the Resource
QMWG Recommendation – Do not support NPRR308 as written. This revision requires a philosophical change to the NS product which would require additional proposed Protocol revision language.

## Slide 3: Update on MISUG, NPRR329 and Dashboards for ERCOT MIS Public
NPRR329 changes security classification for Extracts/Reports to be available on public site
Urgency passed. To PRS in March.
Presentation by M. Mereness regarding dashboard specifications for public site.
Provide feedback to MISUG at March 31 meeting to expedite design. Dashboards could be available early to mid summer, 2011.

## Slide 4: Implementation of WGR Curtailment Flag
Market Notice planned for April 15, implementation on May 18.
Flag via ICCP, set HSL to equal current WGR output when not curtailed. Set HSL equal to WGRPP when curtailed and AGC to follow Base Point.
No plan for closed loop testing with QSEs
Will also implement Base Point Deviation changes to settlements systems.

## Slide 5: Information on HDL/LSL Manual Overrides and Offsets
Presentation by ERCOT posted
Reasons for overrides:
  To prevent continuous operation of SPSs
  To prepare for a significant outage
  For QSGRs
  For telemetry issues to prevent SCED failure
  Should not be used for W-N Congestion Management
Offsets being used for wind ramping, load ramping, DC Tie schedules
ERCOT Operator should call QSE to inform of Manual overrides. Report every 5 minutes informs QSE if override still in effect.
Consider adding notification of overrides to Daily Operation Report, continue report to QMWG from ERCOT.

## Slide 6: Update on SCRs
NPRR307 will require additional NPRR to make system modifications to check temporal constraints.
SCR for trades cancellation to be presented at April WMS
ERCOT working on SCR for COP validation of AS
ERCOT to submit NPRR for Startup and Shutdown RST to include NSRS ICCP notification.
Notification to all QSEs when NSRS deployed, pending

## Slide 7: GREDP and AS Performance Metrics
ERCOT presentation on GREDP scores for December- February
Discussion of possible revisions to metrics calculations for GREDP and NSRS performance metric for outlying data points
Recommend more holistic approach to evaluation of GREDP measures to increase reliability through PDCWG as more operating data is available