## Slide 1: ERCOT CRR Update
WMS 3-9-2011
Steve Reedy
Manager, CRR

## Slide 2: Problem Statement
CRR Calendar Changes
Capacity Factor Calculation for NOIEs
Multi-month Modeling Assumptions

## Slide 3: CRR Calendar Changes
Posting Dates now represent last possible day to post results
Invoice dates (you must pay by/we must pay by) removed from calendar
  Dependant on actual posting date
  Impossible to forecast
Balance of Year is JULY-DECEMBER
  JUNE-DECEMBER won’t work
    Can’t fit all the needed activity between latest possible posting of May and June 1st
  Most activity is sequential

## Slide 4: Capacity Factor Calculation
Nodal Protocols 7.4.2 (e) (ii) Capacity option – The eligible NOIE may nominate up to 100% of the lesser of the net unit capacity or contractual amount for those Resources at a capacity factor no greater than 40% over each calendar year. ERCOT shall allocate PCRRs in accordance with the NOIE nominations subject to the SFT.
Calculated as sum of MWhrs nominated for Capacity type PCRRs/Sum of Capability in months where unit was nominated for Capacity type PCRRs

## Slide 5: ERCOT CRR Use of Planning Model Data
Steve Reedy, CRR Manager
(Originally presented at ROS on 2/18/2011)

## Slide 6: Protocol 7.5.1 (2)
“The CRR Network Model must be based on, but is not the same as, the Network Operations Model. The CRR Network Model must, to the extent practicable, include the same topology, contingencies, and operating procedures as used in the Network Operations Model as reasonably expected to be in place for each month. The expected network topology used in the CRR Network Model for any month must include all Outages from the Outage Scheduler and identified by ERCOT as expected to have a significant impact upon transfer capability during the month. These Outages included in the CRR Network Model shall be posted on the Market Information System (MIS) Secure Area consistent with model posting requirements by ERCOT with accompanying cause and duration information, as indicated in the Outage Scheduler. Transmission system upgrades and changes must be accounted for in the CRR Network Model for CRR Auctions held after the month in which the element is placed into service. “

## Slide 7: “as reasonably expected”
ERCOT CRR interprets “as reasonably expected” as NOMCRs.
ERCOT CRR does not plan to include PMCRs in the balance of year or annual auction models.
ERCOT does not plan to use SSWG cases for CRR auctions.

## Slide 8: Why all the fuss about planning data for CRRs, then?
CRR uses certain planning data
  Connectivity node groups (planning buses)
  Circuit IDs
It is important that that data be accurate in the Network Operations Model upon which the CRR model is based for good/reasonable CRR topology