## Slide 1: Quick Start Task Force Update to WMS
March 9, 2011
Austin, Texas

## Slide 2: February 17 QSTF Meeting
Using SCED to produce LMP Projections
Details on NYISO’s Real Time processes
Real-Time Co-optimization
Power Augmentation

## Slide 3: GTBD Forecasting
Presented by Floyd Trefny
Program SCED to issue “Forecast GTBD”:
  Sample Ramp Rate over last 15 minutes
  Real-Time SCED GTBD + (Ramp Rate * 15)
  Only relevant when approaching aggregate supply stack inflection point
Non-binding indicative price forecast
Allows QSE to make unit commitment decision

## Slide 4: Details on NYISO
Real Time Commitment (RTC)
Real Time Dispatch (RTD)
  Corrective Action Mode (RTD-CAM)
Additional information:
  NYISO Manual 12: Transmission and Dispatching Operation Manual
  QSTF webpage

## Slide 5: RTC Operational Details
Looks forward 2 hours and 15 minutes
Runs every 15 minutes
Issues
  Binding decisions 15 & 30 minutes into future
  Advisory guidance beyond 30 minutes
  De-commitment decisions 15 minutes out
  Advisory RT Ancillary Service prices
Resources must be synchronized and running at LSL in :15 or :30
Notes: Manual 12
5.1.1 Real-Time Commitment Process
5.1.3 (5) Real-Time Commitment Information Posting

## Slide 6: RTC Operational Details
Fast Start Management
  Requires NYISO staff to approve Start-Up and Shut-down of Quick Start Units
RTC Assumptions
  1-hour minimum run time
  Start-Up Cost added to energy offer
  Only Energy Offer used to set LMP
  Hybrid pricing
    LMP set first; Base Point then issued to HSL
    Re-dispatch other Resources
Notes: 5.7.2 Interaction with Fast Start Management
5.7.6 Supplemental Resource Evaluation Procedures

## Slide 7: Real Time Dispatch
Runs every 5 minutes, issues LMPs
  Similar to SCED
Looks forward 60 minutes
Issues
  Base Points
  Energy and A/S prices for first RTD increment
  Advisory prices for remaining 45 minutes
Does not make UC decisions
Notes: Manual 12
2.5.4
6.1.1 Real-Time Dispatch Process

## Slide 8: RTD Corrective Action Mode
Used during unanticipated system conditions
5 modes, issuing unit commitments 5 or 10 minutes in future
  Reserve Pickup
  Maximum Generation Pickup
  Base Points ASAP – No Commitments
  Base Points ASAP – Commit as Needed
  Re-sequencing

## Slide 9: Short versus Long Term Proposals
Short Term (GTBD) | Long Term (NYISO)
15-minute forecast | Full ~2 hour Look-Ahead with advisory prices, Base Points and commitments
Short, low cost implementation | Involved implementation, based on NYISO’s Real Time Scheduling
Non-binding price signal | Binding unit commitment decision Advisory AS prices and Base Points
No Make-Whole | Make-Whole if RT prices fall below Energy Offer
Resource Parameters managed by QSE | Respects minimum run time, Start-Up costs, minimum down time, etc.

## Slide 10: Real Time Co-optimization
To be discussed at next QSTF
Supporting materials available at 2/17 QSTF webpage, including:
  Patton Direction Testimony, PUC Docket 31540
  Final Order, PUC Docket 31540
  2006 Co-optimization Task Force material

## Slide 11: Guidance from WMS
Investigate
  Short Term (GTBD) Proposal; and/or
  Long Term (NYISO) Proposal?
To do:
  Real Time Co-optimization
  Augmentation Technologies
Next meeting: Monday, March 28