## Slide 1: Observed impacts of Real-Time Settlement Point Prices NPRR326
http://nodal.ercot.com <number>
PRS
March 24, 2011

## Slide 2: PRS NPRR326 Discussion
Reminder/definition of the issue being resolved with NPRR326
Evidence of the issue becoming a larger problem over time
Conclusion
Appendix of detailed example from CMWG in January

## Slide 3: Reminder of the issue being addressed in NPRR326
Real-Time Settlement Point prices are influenced by energy weighting
This has caused RT-SPPs to separate even when there is no congestion (example)
NPRR326 would remove MW weighting and make time-weighted average SPP = $50 for both

## Slide 4: Issue Escalating
Evidence of this problem
  Theoretical concerns have materialized
Most observable pattern is price separation within station in real-time
QSEs increasing bids into DAM to secure PtPObligation Bids where there is no congestion
  DAM procures PtPObligation at low cost or free $0 (no DAM price separation)
  QSE paid/charged holding the PtP for the price separation in real-time
    Example from previous page
ERCOT Concerns
  DAM performance
    Oversubscribed/unreasonable activity within stations
      bids within station in excess of 10x output of entire site
    DAM solution diverging and was at risk in early March, but ERCOT mitigating risk
  Revenue neutrality impacts of paying congestion rents

## Slide 5: Conclusion
If nothing is done, energy weighting of RTSPPs will continue to create price separation in real-time
QSE positions (PtPObligations) can be purchased at little or no cost
  Within a station, or
  Between any 2 settlement points where the energy weighting contributes to price movement/separation of a resource node
  Observed where this can be $10,000 at single station in a single day
Currently there are winners and losers at this point, but issue could become more predictable (over time and coming into summer peak)
Recommend market-focus and timely consideration of NPRR326 to address this design issue.

## Slide 6
APPENDIX- Detailed example from January CMWG
http://nodal.ercot.com <number>

## Slide 7
http://nodal.ercot.com <number>
Real-Time LMP and SPP FAQ

## Slide 8
http://nodal.ercot.com <number>
Real-Time LMP and SPP FAQ

## Slide 9: Current Settlement Point Prices
This is appropriate for settling energy produced in Real-Time where there was no obligation to produce.

## Slide 10: The current method works for Energy payment if no DAM award
RTLMPa | Start time | End Time | BP | Energy "Production" | Energy Long (+)/ Energy Short (-) | per SCED Energy imbalance charge
$ 1,000.00 | 1/1/2011 0:00:00 | 1/1/2011 0:00:22 | 100 | 0.611111111 | 0.611111111 | $ (611.11)
$ 500.00 | 1/1/2011 0:00:22 | 1/1/2011 0:05:21 | 110 | 9.136111111 | 9.136111111 | $ (4,568.06)
$ 100.00 | 1/1/2011 0:05:21 | 1/1/2011 0:10:20 | 90 | 7.475 | 7.475 | $ (747.50)
$ 50.00 | 1/1/2011 0:10:20 | 1/1/2011 0:15:00 | 100 | 7.777777778 | 7.777777778 | $ (388.89)
 |  |  |  | 25 |  | 
 |  |  | SPP (energy weighted) | $252.62 |  | 
Current method = RT SPP * ENERGY LONG = $252.62 * (25 )= ($6,315.56)
Settle every SCED interval = ΣENERGY LONG*SCED LMP = (611.11) + (4,568.06)
+ (747.50) +(388.89) = ($6,315.56) = The same

## Slide 11: Current settlement wrong for PTP OBL
Settlement point price based on energy weighting
Can cause SPP prices to diverge even when there is no congestion (slides 3 & 4).
Causes payouts to PTP OPT and OBL holders even when there is no congestion.
These payouts are not supported by Congestion Rent and may lead to RT Neutrality Uplift.

## Slide 12
http://nodal.ercot.com <number>
10 MW CRR from 3 to 4 would pay holder $1,241.60 (= {564.06-67.42} * 10 * 0.25)
for that 15 minute interval.

## Slide 13: Settle PTP OBL on Time Weighted SPP
Mathematically equivalent to settling each SCED interval
Get the right answer without the significant system change needed to settle per SCED interval

## Slide 14
RTLMPa | Start time | End Time | BP | RTLMPb | BP | Value of CRR evaluated over SCED interval
$ 1,000.00 | 1/1/2011 0:00:00 | 1/1/2011 0:00:22 | 0.001 | $ 1,000.00 | 20 | $ -
$ 500.00 | 1/1/2011 0:00:22 | 1/1/2011 0:05:21 | 0.001 | $ 500.00 | 10 | $ -
$ 100.00 | 1/1/2011 0:05:21 | 1/1/2011 0:10:20 | 10 | $ 100.00 | 0.001 | $ -
$ 50.00 | 1/1/2011 0:10:20 | 1/1/2011 0:15:00 | 20 | $ 50.00 | 0.001 | $ -
 |  | $ 67.42 | $ 239.33 | $ 564.06 | $ 239.33 | $ -
 |  | SPPa | Time Weighted SPPa | SPPb | Time Weighted SPPb | Total PTP OBL value if evaluated over each SCED interval
Payment to PTP OBL Holder | Method of calculation
$ - | evaluated over each SCED then summed (ideal)
$ 1,241.59 | evaluated based on energy weighted SPP (current)
$ - | evaluated based on time weighted SPP (proposed)

## Slide 15: Current Settlement not ideal for Real-Time Imbalance
Not Ideal = Compliant with protocols, but not matching “per SCED run” ideal
Propose settling DAM award/schedule based on time weighted SPP but Real Time generation/load based on energy weighted SPP.
Mathematically equivalent to settling each SCED interval
Get the right answer without the significant system change needed to settle per SCED interval

## Slide 16: Proposed method matches per SCED
Current method = RT SPP * ENERGY LONG = $252.62 * (25-25 )= ($0.00)
Settle every SCED interval = ΣENERGY LONG*SCED LMP = (0) + (415.28) + 83.06+ 0 = ($332.22)
Settle DAM award on time weighted SPP and Energy production on energy weighted SPP
= 25 * $239.33 – 25 * $252.62 = ($332.22)
RTLMPa | Start time | End Time | BP | Energy Obligation | Energy "Production" | Energy Long (+)/ Energy Short (-) | per SCED Energy imbalance charge
$ 1,000.00 | 1/1/2011 0:00:00 | 1/1/2011 0:00:22 | 100 | 0.611111111 | 0.611111111 | 0 | $ -
$ 500.00 | 1/1/2011 0:00:22 | 1/1/2011 0:05:21 | 110 | 8.305555556 | 9.136111111 | 0.830555556 | $ (415.28)
$ 100.00 | 1/1/2011 0:05:21 | 1/1/2011 0:10:20 | 90 | 8.305555556 | 7.475 | -0.830555556 | $ 83.06
$ 50.00 | 1/1/2011 0:10:20 | 1/1/2011 0:15:00 | 100 | 7.777777778 | 7.777777778 | 0 | $ -
 |  |  |  | 25 | 25 |  | 
 | Time Weighted SPP | $239.33 |  | Energy Weighted SPP | $252.62 |  |