## Slide 1: Valley Import Constraint
John Dumas

## Slide 2: Objective
Establish an appropriate Shadow Price for the Valley Import limit
  Consistent with the methodology established in the Board Approved ERCOT Business Practice “Setting the Shadow Price Caps and Power Balance Penalties in Security Constrained Economic Dispatch”

## Slide 3: Current Methodology
  3.4 Methodology Outline
The methodology for determination of maximal Shadow Prices for transmission constraints could be based on the following setting:
  Determine Shift Factor efficiency threshold (default x%)
  All generators in the valley have a shift factor of 0.95 or greater
  (b) Determine maximal LMP congestion component (default $y/MWh)
  Non-competitive constraint therefore offer is limited to mitigated offer in the valley
  (c) Calculate maximal Shadow Price for transmission constraints:
  SP(max) = highest offer/lowest shift factor threshold
  (d) Determine Shift Factor cutoff threshold (default z%)
  not applicable due to all generation in the valley having a very high shift factor impact on the import constraint
  (e) Evaluate settings on variety of SCED save cases.

## Slide 4: Current Methodology
For the network transmission constraints, the Shadow Price Cap may vary for each constraint, or may be a unique value applicable to all constraints, or may be values unique to subsets of the full constraint set.
Generating units with small Shift Factors (i.e. below Shift Factor threshold) will not be as effective in resolving constraints as will generators with higher shift factors on the constraint. If there is no efficient generating units then Shadow Price must be increased to get enough contribution from inefficient units. Therefore, high Shadow Prices indicate inefficient congestion management. - All generators in the Valley have a very high shift factor impact on the Valley constraint therefore increasing the shadow price does not result in additional generation (i.e. all generators are at maximum output)

## Slide 5: Valley Import Constraint
Range of SFs
  -0.95 to -0.97 in valley area
  0.03 to 0.045 outside valley area
Not a competitive constraint and hence the Resources are moved based on offers capped by higher of Reference LMP & Mitigated Offer Cap curve
Base Case constraint are assigned the system-wide value of $5,000 per MWh for the Max Shadow Price

## Slide 6: Price Related Factors
Highest Shadow Price when observed when the Valley Import constraint is binding but not violated is less than $100/MWh (more than 16 hr in the first 4 months)
  Constraint cannot be resolved many times even with all the generation available
South LZ SPP when the constraint is violated ranges from $1500/MWh to $1850/MWh (more than 7 hr in the first 4 months)
  Demand response in majority of that load zone with the high price has no impact on resolving the constraint violation.
Constraint is managed by Operator action after it has been violated for more than an hour in SCED (roughly 43 hrs in the first 4 months)

## Slide 7: Current Planning Process
Ensures that all parts of the system are reliable based on the planning criteria
Planning has reviewed the area and they are proposing solutions that will ensure that the valley area will be secure under the outage of a single element and a generator
Preliminary planning studies with the TDSP show that there is possibility of increasing the limit on the interface in the short term, which should reduce the extent of dependence on the regional generator to meet the valley load.
The planning process ensures that the area is secure for the next 5 years even without any import from the DC ties and considering the estimated load growth, planned generator outages for more than 6 months and other system changes
The valley constraint will be overloaded in RT only outside the planning criteria. i.e. if the load is considerably higher and if there are multiple generator or line outages.

## Slide 8: Hours of Binding/Violation
 | December | January | February | March | sum | violated hrs
Hours active in SCED | 2.8 | 21.5 | 26.9 | 9.3 | 60.5 | 
Hours binding in SCED | 1.3 | 6.0 | 6.8 | 2.1 | 16.3 | 
Hours violated in SCED | 0.0 | 2.1 | 5.2 | 0.0 | 7.3 | 
Hours with Violated & overridden | 0.1 | 3.9 | 39.3 | 0.0 | 43.3 | 50.5
Active in SCED – Constraint is passed to SCED
Binding in SCED – Constraint is resolved by SCED – Flow = Limit
Violated in SCED – Constraint was not resolved by SCED – Flow > Limit
Violated & Overrriden – LDL was overriden and Flow > Limit
Congestion Cost = (Flow MW * Shadow Price * 1/12) per 5 min

## Slide 9: Congestion Cost
 | December | January | February | March | sum | violated hrs
Hours active in SCED | 2.8 | 21.5 | 26.9 | 9.3 | 60.5 | 
Hours binding in SCED | 1.3 | 6.0 | 6.8 | 2.1 | 16.3 | 
Hours violated in SCED | 0.0 | 2.1 | 5.2 | 0.0 | 7.3 | 
Hours with Violated & overridden | 0.1 | 3.9 | 39.3 | 0.0 | 43.3 | 50.5
SP*MW Flow | December | January | February | March | Sum | Sum in SCED
VALIMP binding in SCED | $3,089.05 | $56,224.85 | $33,959.97 | $2,011.26 | ($95,285.14 | 
VALIMP violated in SCED @SP5000 | $0.00 | $11,831,250.00 | $34,809,583.33 | $0.00 | + $46,640,833.33) | = $46,736,118.47
Violated & overridden @ SP5000 | $469,121.70 | $17,241,771.70 | $281,173,247.58 | $0.00 | $298,884,140.98 | 
Violated & overridden @ SP3000 | $281,473.02 | $10,345,063.02 | $168,703,948.55 | $0.00 | $179,330,484.59 | 
Violated & overridden @ SP2000 | $187,648.68 | $6,896,708.68 | $112,469,299.03 | $0.00 | $119,553,656.39 | 
Violated & overridden @ SP1000 | $93,824.34 | $3,448,354.34 | $56,234,649.52 | $0.00 | $59,776,828.20 | 
Violated & overridden @ SP500 | $46,912.17 | $1,724,177.17 | $28,117,324.76 | $0.00 | $29,888,414.10 | 
Violated & overridden @ SP350 | $32,838.52 | $1,206,924.02 | $19,682,127.33 | $0.00 | $20,921,889.87 | 
Violated & overridden with 2 step limits $200 & $2000 MSP | $18,764.87 | $1,465,179.63 | $97,588,665.34 | $0.00 | $99,072,609.83 | 
Violated & overridden with 2 step limits $200 & $2000 MSP – One constraint at limit + margin with Max Shadow Price at $200 and another at limit with Max Shadow Price at $200 0

## Slide 10: South Load Zone Extra Payment
  Average $/MW for hours when constraint was violated in SCED
  = (7.3 + 43.3)*(1806.83-63.68)=50.6*1743.15
  = $88,203.4
STLPNT_NAME | AVG(LMP) | Average Load
LZ_SOUTH | $1,806.83 | 6316
LZ_HOUSTON | $58.00 | 11943
LZ_NORTH | $65.44 | 20763
LZ_WEST | $66.68 | 3102
Avg N H W | $63.37 | 11936

## Slide 11: ERCOT Proposed Max Shadow Price - $350/MWh
Determine the highest Shadow Price cap necessary to fully utilize existing and potential new valley generation to relieve the overload
The highest offer from a new resource with no verifiable cost that could be moved is
  14.5 heat rate* $10 FIP/ lowest SF = 14.5 *10 /0.95 ~ 150/MWh
The highest offer from a new resource with verifiable cost that could be moved is
  (high Heat Rate * $10 FIP + corresponding high O&M) * highest multiplier/ lowest SF
  (14 .5*10 + 75 )*1.5/0.95 ~ $350/MWh

## Slide 12: Conclusion
Current Business Practice
  Establishes shadow price caps that can vary per constraint in order to dispatch generation efficiently
  Gives latitude to increase the Shadow Price Caps if doing so would dispatch less efficient generation to help solve the constraint
Current Planning Process
  Ensures that enough transmission is built in order to maintains system security under the loss of one line and one generator scenario
The recent real-time limit violations were due to multiple outages (outside the planning criteria)
Demand response in the South Zone that is physically north of the constraint will not help resolve a Valley import limit