| PGRR Number |  | PGRR Title | Dynamics Working Group Guidelines |
| --- | --- | --- | --- |
| Date Posted |  |

| Planning Guide Section(s) Requiring Revision (Include Section No. and Title) |  |
| --- | --- |
| Protocol Section(s) Requiring Revision, if any |  |
| Requested Resolution (Normal or Urgent, and justification for Urgent status) |  |
| Revision Description | This Planning Guide Revision Request (PGRR) adds new Section _ Dynamic Working Group Guidelines. |
| Reason for Revision | This PGRR brings parts of the current DWG Procedures into the Planning Guide deemed to be appropriate for addition to the Planning Guide. The Planning Guide is being developed as requested by the Reliability and Operations Subcommittee (ROS) and the Technical Advisory Committee (TAC). |
| Overall Market Benefit |  |
| Overall Market Impact |  |
| Consumer Impact |  |

Quantitative Impacts and Benefits

Instructions:  To allow for comprehensive PGRR consideration and development of the Cost Benefit Analysis (CBA), please fill out each block below completely and provide as much detailed information as possible.  Wherever possible, please include reasons, explanations, and cost/benefit analyses pertaining to this PGRR.

| Assumptions | 1 | e.g.: Key assumptions used in estimating market cost and/or benefit |
| --- | --- | --- |
|  | 2 | Dependencies on other projects or other timing requirements |
|  | 3 |  |
|  | 4 |  |
| Market Cost |  | Impact Area | Monetary Impact |
|  | 1 | e.g.: Cost per MP to implement | e.g.: $10,000 each for 50 QSEs |
|  | 2 | Add’l staff required per MP | 1.5 FTE each for 6 TDSPs @ $65/hour |
|  | 3 |  |  |
|  | 4 |  |  |
| Market Benefit |  | Impact Area | Monetary Impact |
|  | 1 | e.g.: Reduced MP costs | e.g.: 2 FTE reduction for 25 CRs @ $65/hour |
|  | 2 | Enhanced MP efficiency | 2 hour savings per day for 50 generators @$65 |
|  | 3 | Reduced congestion cost | 0.5% reduction in total congestion cost |
|  | 4 |  |  |
| Additional Qualitative Information | 1 | e.g.: Benefits that are difficult to quantify |
|  | 2 | Benefits that are not certain but relatively likely |
|  | 3 | Customer service impacts, cash flow impacts, transaction speed, etc. |
|  | 4 |  |
| Other Comments | 1 | e.g.: Thoughts on ERCOT systems impacts |
|  | 2 | Potential manual workarounds or delivery options |
|  | 3 | Other comments of value to PRS, TAC and the Board of Directors |
|  | 4 |  |

| Sponsor |
| --- |
| Name | Charles DeWitt |
| E-mail Address | cdewitt@lcra.org |
| Company | LCRA TSC |
| Phone Number | 512-369-4199 |
| Cell Number |  |
| Market Segment |  |

| Market Rules Staff Contact |
| --- |
| Name |  |
| E-Mail Address |  |
| Phone Number |  |

Proposed Guide Language Revision

6.2   Dynamics Model Development

(1)	To adequately simulate dynamic and transient events in the ERCOT System it is necessary to establish and maintain dynamics data and simulation-ready study cases representing the dynamic capability and frequency characteristics of machines and equipment connected to the ERCOT System.

(2)	Dynamics data is the network data and mathematical models required in accordance with the Reliability and Operations Subcommittee (ROS)-approved Dynamics Working Group (DWG) Procedure Manual for simulation of dynamic and transient events in the ERCOT System.

(3)	For Resource Entities, Dynamics data includes the data needed to represent the dynamic and transient response of Resource Entity owned devices and/or loads including but not limited to generating units, plants, and other equipment when connected to the ERCOT System including the data for any privately owned transmission system or collection system used to connect the Resource to the ERCOT System.

(4)	For TSPs, Dynamics data includes data needed to represent the dynamic and transient capability of TSP owned devices including but not limited to load shedding relays, protective relays, FACTS devices (e.g., DVARS, SVC, STATCOM, SMES), DC ties, variable-frequency transformers, automatically switched shunts, and transformers with automatic load tap changers.

(5)	All dynamics data must be compatible with the current version of the planning model software as described in the DWG Procedure Manual.

(6)	The Facility owner shall provide appropriate dynamics data to ERCOT, including the data for a planned Facility.

(7)	Dynamics data for a planned Facility will be updated by the Facility owner upon completion of the design for the Facility.

(8)	Updated Dynamics data for an existing Facility shall be provided to ERCOT when field tests, inspections, or other information demonstrates that the dynamics data should be changed to accurately represent the dynamic characteristics of the Facility.

(9)	Dynamics Data is considered confidential under the ERCOT Protocols, and shall be held confidential under ERCOT Transmission Provider code-of-conduct rules.

(10)	Dynamics Data shall be provided with the legal authority to provide the information to all TSPs.  If any of the information is considered Protected Information, the Facility owner shall indicate as such.

6.2.1   Dynamics Data Requirements for Resources

(1)	A Resource Entity shall submit new or updated Dynamics data in accordance with Section 5, Generation Resource Interconnection or Change Request.  The Resource Entity shall provide all dynamics data as described in the DWG Procedure Manual.  The Resource Entity shall provide an accurate and appropriate model and model parameters. Resource Entities are encouraged to use standard models to represent the Resource’s dynamic and transient capability and response.  If no appropriate standard model is available, the Resource Entity shall submit a model, model documentation, and the associated model parameters to ERCOT for inclusion in simulation-ready study cases as described in the DWG Procedure Manual.

(2)	A Resource Entity is responsible for tuning and validating the parameters that go into their models to ensure that the models produce an accurate representation of a device’s capability and response.  If ERCOT, the interconnecting TSP, or the DWG identifies inappropriate or incomplete dynamics data, ERCOT shall take action to resolve discrepancies with the Resource Entity.

6.2.2   Dynamics Data Requirements for Load Resources

(1)	ERCOT shall provide the updated Load Resource relay models.

(2)	Load Resource relay models shall be updated as describe in the DWG Procedure Manual.

6.2.3   Dynamics Data Requirements for Load Serving Entities (LSEs) and Transmission and/or Distribution Service Providers (TDSPs)

(1)	The owner of UFLS equipment shall provide necessary data to model under frequency Load shedding relays for their portion of the ERCOT System as described in the DWG Procedure Manual.

(2)	The owner of UVLS equipment shall provide necessary data to model under voltage load shedding relays for their portion of the ERCOT System as described in the DWG Procedure Manual.

(3)	When requested by ERCOT or a TDSP, the owner of protective relays, control systems, and special protection schemes shall provide dynamics data needed to simulate their action.

(4)	The DWG shall document appropriate load model data as described in the DWG Procedure Manual for use in dynamic simulations.

(5)	The owner of a dynamic element connected to the transmission system shall provide the dynamic data needed to simulate the action of the device in dynamic simulations to ERCOT and the TSP to which the element is connected. Examples of dynamic elements include, but are not limited to, static-var compensators, Direct Current Ties (DC Ties), variable frequency transformers, switched shunt devices, and transformers with automatic tap changers.

6.2.4 Dynamics Data Screening and Maintenance

(1)	In order to maintain simulation-ready base cases and associated dynamics data files for use in dynamic simulations, the DWG, in consultation with ERCOT, shall perform dynamic simulations, called flat-start simulations, as described in the DWG Procedure Manual.

(2)	The schedule for producing the flat start simulations will be reviewed annually and submitted to the ROS.

(3)	Transmission owners shall review the completeness and applicability of dynamics data used in the flat start simulation for equipment connected to their system.  The model should be appropriate for the equipment and the data shall be appropriate for the model.

(4)	ERCOT shall contact the appropriate TSP or Resource Entity to resolve any dynamics data problems, incomplete or missing data, encountered while preparing the flat start simulation.

(5)	Upon completion of each flat start simulation, ERCOT shall distribute to the members of the DWG an electronic copy of all files necessary to repeat the flat start simulation as described in the DWG Procedure Manual.

(6)	ERCOT and members of the DWG shall document assumptions made, data created, and data changed during the creation of a flat start simulation.

(7)	ERCOT shall be responsible for storing all of the dynamics data.  It shall maintain a repository of dynamics data with tuned parameters and will maintain the submitted revisions.  All dynamics data received by ERCOT shall be forwarded to the TSP to which the dynamics device is connected within 30 days of receipt.

6.2.5 Dynamics Data Recorder

(1)       ERCOT, in consultation with the other members of the DWG, shall prepare a list of locations, based on criteria contained in the DWG Procedure Manual, which require the installation of devices capable of recording ERCOT Transmission Grid events with sufficient resolution to serve as a benchmark for dynamic simulations.

# Comments

Need Section number.

Is this referring to PUNs?

It may be more. The Nodal Protocols generally refer to a system used to serve load that is netted with generation. In this case we want the data for a transmission system is owned by a Generating Entity as a means of connecting multiple generators to a single point of interconnection.

From ONCOR TSP and LCRA TSC: Dyre preparations by non-equipment owners is a courtesy and equipment owners still maintain the responsibility for providing the dyre data. The provision of dyre records should be addressed in the DWG Procedures.

From ERCOT: Note to PLWG. It is recognized that equipment data needs to come from owners but the dyre records need to come from TSPs.

From ONCOR TSP and LCRA TSC: Dyre preparations by non-equipment owners is a courtesy and equipment owners still maintain the responsibility for providing the dyre data. The provision of dyre records should be addressed in the DWG Procedures.

ERCOT believes that “in consultation with ERCOT” is redundant in that they are a member of DWG.

The issue seems to arise from a  lack of definition in the Planning Guides of the composition of DWG and its hierarchy.

Has this moved to SPWG?