## Slide 1: Appeal to the Technical Advisory Committee NPRRs 351 and NPRR 378
Chaparral Steel, Nucor Steel, and CMC Steel
Floyd J. Trefny
August 4, 2011

## Slide 2: Topics
NPRR 351 Review
NPRR 378 Review
NPRR History
Summary

## Slide 3: NPRR 351 Review
In the existing SCED, the software uses the total amount of current generation needed in Real Time to dispatch generation base points
To calculate projected prices, execute the same SCED algorithm, but instead of current generation needed, use a forecast of the total generation for 15 minutes from now
  Forecast generation could be higher or lower than the current requirement
Use same energy offer curves, Resource limits and status that were available to SCED for the actual dispatch
  For the projected prices, adjust HDL and LDL calculations to ramp over 15 minutes instead of 5 minutes as is done for RT
Assume that the same transmission constraints that are active in real time SCED are also active in the forecast
Post, the projected LMP’s generated for:
  Resource Nodes
  Hubs
  Load Zones (LMPZ)
Projected prices posted every 5 minutes for 15 minutes ahead
Generation
Load
HUB
SUPER
HUB
HUB
HUB
HUB

## Slide 4: NPRR 378 Review
Written to incorporate ERCOT comments originally made on NPRR 351
Adds to Ancillary Services Capacity Monitor additional Reserve postings for:
  For Real Time
    Up Reserve between sum HDL and actual generation
    Down Reserve between actual generation and sum of LDL
    Posts Short Term Load Forecast used to calculate Sum of Base Points
  For 15 Minute Projection
    After adjusting for longer term ramping of generation, calculates the same HDL and LDL reserves above
    Posts expected Short Term Load Forecast expected to be used 15 minutes from current dispatch

## Slide 5: NPRR History
NPRR 351
  Provides non-binding projections of LMPs, a rolling 15-minute look ahead
  Concepts/Drafts reached consensus at:
      Quick Start Task Force
      Demand Side Working Group
      Wholesale Market Sub-committee voted to sponsor the NPRR, 4/8/2011
      ERCOT Stated at PUC Workshop on Resource Adequacy that this project is “medium to small” undertaking
NPRR 378
  Written to capture ERCOT comments on NPRR 351
  Provides postings of more reserves from SCED
PRS on June 23, 2011 rejected both NPRRs for “Cost Benefit Study”

## Slide 6: Summary
Non-Binding projected prices can be very useful tool, allowing the load to respond to prices – reinforcing the interaction between supply and demand
    Using price projections is the simplest means of explaining what to do and when to do it for entities “not in the market”
    ERCOT may need indications of near future prices to understand the effects of Non-Spin deployment
PRS’s rejection of NPRRs 351 and 378 should be reversed by TAC and TAC should approve both NPRRs for an Impact Analysis
ERCOT should perform impact analyses on the two NPRRs, on an expedited basis
TAC can reconsider the appropriateness of adopting these NPRRs in light of the impact analyses