## Slide 1: PRS Response to Steel Companies’ Appeal of NPRR’s 351 and 378
Tom Payton on behalf of PRS
August 4, 2011
Disclaimer: This response attempts to capture concerns leading to rejection of NPRR’s 351 and 378 at the June 23, 2011 PRS meeting. Individual votes at PRS may have been for any or all of the following reasons or for other reasons not discussed herein.

## Slide 2
The PRS vote to reject NPRR’s 351 and 378 was appropriate based on the procedural, policy, technical and market flaws therewith.
The PRS voted over 2-to-1 to reject - i.e., the package of NPRR’s 351 and 378 did not fail on a motion to approve, rather, the package was rejected by approval of a motion to reject.
Representatives of the Steel Companies objected to an individual vote on each NPRR and also objected to tabling the NPRR’s for one month to investigate the concerns about policy, technical and market flaws.
Except for the Steel Companies’ representative, the entire consumer segment voted against the package of NPRR’s 351 and 378.

## Slide 3: Short Descriptions
NPRR 351 - requires ERCOT to provide “non-binding”
ex-ante prices to market
NPRR 378 - requires ERCOT to provide additional
situational information to market, but not
ex-ante prices

## Slide 4: NPRR 378
Unaware of anyone with particular objections to NPRR 378, however, the Steel Companies’ representative strenuously objected to it being voted on by itself.
NPRR 378 might have been approved, but for the insistence that it be packaged with NPRR 351.

## Slide 5: NPR 351
NPRR 351 as presented has significant problems that properly led to its rejection by PRS.
These problems mainly revolved around ex-ante pricing and the following:
  reduced reliability and/or higher ancillary service requirements
  increased real-time market volatility
  improper shifting of costs from certain loads to other loads

## Slide 6
NPRR 351 is not about efficiently and economically integrating demand response into the ERCOT market.
It is about a subset of loads seeking an ex-ante price to arbitrage against.

## Slide 7: Fundamental Market Reality
By bidding an “up to” price in the DAM (through their REP/QSE) and then not operating for hours not awarded, loads may already avoid operating at price levels they consider undesirable.
Any load which does not arrange its supply in the DAM (through their REP/QSE) has, by definition, requested ERCOT to arrange supply for them in real-time.
Advocates for NPRR 351 are asking to be able to decline to take the real-time power in an interval after ERCOT has already acquired it on their behalf.
The cost impact of power not taken by certain loads in that interval is then improperly shifted to other loads.

## Slide 8: Impact of Ex-Ante Pricing
Certain loads are particularly suited to arbitrage ex-ante prices. These loads have the following characteristics;
  relatively continuous intermittent operation
  virtually instantaneous ramp rate
  designed for frequent on/off cycles
This arbitrage will have the following negative impacts:
  reduced grid reliability and/or increased ancillary service requirements
  increased real-time market volatility
  improper shifting of costs to other loads

## Slide 9: Conceptual Arc Furnace Operation - I
Arc furnace operation on/off
Arc furnace operation off/on

## Slide 10: Conceptual Arc Furnace Operation - II
5 arc furnaces operating
5 arc furnaces operating
with ex-ante price
without ex-ante price

## Slide 11
40 40 40 40 1,000 20 1,000 20 1,000 20 1,000
ERCOT Load Forecast
NPRR 351 Arbitrage Example – Market Upset in Interval 4
LMP - $/MWh

## Slide 12: Cost Shifting Example
Market upset (such as a large generator tripping) occurs in Interval 4. SCED dispatches additional generation to meet load in Interval 5 at $1,000/Mwh.
Arc furnaces shut off to avoid $1,000/MWH LMP in interval 5.
However, SCED has already acquired generation to serve arc furnace load in Interval 5.
Therefore, approximately 250 MW of Regulation Down is dispatched in Interval 5 to offset arc furnace response to ex-ante price.
Regulation Down providers now have a 250 Mw generation imbalance in Interval 5 that ERCOT charges them for at $1,000/MWH.
Regulation Down providers could have made the energy themselves for $40/MWH, therefore they lose $960/MWH on 250 MW.
In the next Interval, SCED sees the load cuts and acquires less generation at a much lower LMP. The arc furnaces now all restart to take advantage of the $20/MWH LMP in Interval 6.
However, SCED has already cut back generation for interval 6 to offset the previously missing arc furnace load.
Therefore, approximately 250 MW of Regulation Up is dispatched to offset arc furnace response to ex-ante price in Interval 6.
Regulation Up providers now have a 250-MW generation imbalance that ERCOT pays them for at only $20/MWH.
Regulation Up providers cost to make this energy is $40/MWH, therefore losing $20/MWH. Etc. Etc.
Regulation service providers are systematically short-changed by arbitrage of the ex-ante price. They then raise their bids to offset these systematic losses, thereby shifting arbitrage costs to all loads.

## Slide 13: Points of Note from Example
Ex-ante pricing can increase real-time volatility
Ex-ante pricing can increase peak load
Ex-ante pricing can incent swings larger than available Regulation
Diversion of Regulation to offset arbitrage of ex-ante pricing can result in Regulation being unavailable for its intended reliability purpose
With ex-ante pricing, arc furnace load comes off or returns after SCED has already acquired generation for the next interval - too late to cause more efficient dispatch
Ex-ante pricing can result in less efficient market dispatch and less efficient market outcomes

## Slide 14
Other Issues

## Slide 15: Some Assertions by Proponents of NPRR 351 at PRS
Assertion
Look-ahead SCED will issue binding ex-ante LMP’s, therefore NPRR 351 is just a transition to that future state.
All other markets provide, at a minimum, non-binding ex-ante LMP’s. For example, the NYISO provides ex-ante LMP’s 5-minutes before the start of any interval
Lack of an ex-ante price from ERCOT would require a single steel mill to train about 50 people in plant operation on how the ERCOT electric market works.
PRS can ask ERCOT to perform Cost Benefit Analysis and then decide later if they want to approve the NPRR, therefore no harm in sending it to ERCOT for Cost Benefit Analysis at this time.
Comment
Not true. Look-ahead SCED does not issue binding ex-ante LMP’s.
Not true. For example, the NYISO does not provide ex-ante LMP’s before the start of an interval. It generally provides pricing 1-1/2 to 2 minutes after the start of an interval (just like ERCOT).
Not true. Where price forecast comes from does not change who does or does not need to be trained in plant.
Generally not consistent with Protocols. For an NPRR not sponsored by ERCOT, the NPRR should not be sent for an Impact Analysis unless it has first been approved by PRS. See Nodal Protocols Section 21.4.5.

## Slide 16: Recommendation
For the foregoing reasons, reject the appeal of PRS action on NPRR 351 and 378

## Slide 17
Q: So what is the solution to further integrate demand response into the real time market?
The general consensus seemed to be that a properly designed Loads in SCED is the answer.
Is this already being worked on?
A. Yes, it is working its way through the stakeholder process.
One Other Thought

## Slide 18
Thank you