## Slide 1
RELIABILITY AND OPERATIONS SUBCOMMITTEE Report to TAC Austin, TX September 1, 2011
Kenneth A. Donohoo, P.E.
Chairperson
Oncor Electric Delivery Company LLC

## Slide 2: TAC Voting Items
NOGRR069, Relay Misoperation Reporting Changes for Consistency with ERO-RAPA Proposal – URGENT
NOGRR070, Synchronization with NPRR356, EEA Changes Related to Dispatch Instructions and BLTs
NOGRR071, Synchronization with NPRR362, Changes to PRC Calculation
NOGRR073, Entity Responsible for Load Shed During EEA Level 3
NOGRR074, Clarified Responsible Entities for Reporting Sabotage Information to NERC
Notice of ROS Rejection of NOGRR075, Synchronization with NPRR363, Revision to EEA Level 2B ERCOT Requirements During the EILS VDI

## Slide 3: ESTIMATED CONGESTION COSTS Top Ten Binding Each Month
DEC 2010 | JAN 2011 | FEB 2011 | MAR 2011 | APR 2011 | MAY 2011 | JUN 2011
21,805,811 | 31,295,778 | 122,383,944 | 19,252,807 | 39,629,295 | 39,629,295 | 50,733,613
Subtotal Top Ten $324,730,543
TOTAL 2011 Congestion $459,045,570 (as of 07/31/2011)
Source: Monthly ERCOT System Planning Report to ROS
Estimated Congestion Cost (Shadow Price X Limit)
Does not include some Congestion Costs during EEA Events

## Slide 4: ESTIMATED CONGESTION COSTS Top Ten Jan-Jul 2011
Source: Monthly ERCOT System Planning Report to ROS
Estimated Congestion Cost (Shadow Price X Limit)
Does not include some Congestion Costs during EEA Events
Binding Element | Congestion Cost $ | Transmission Project
West to North Stability Limit | 74,382,777 | CREZ
Valley Import | 41,457,339 | RPG Project Under Review
Lon Hill - North Edinburg 345kV | 31,689,757 | RPG Project Under Review
West Denton - Jim Cristal 138kV | 22,404,765 | 5YTP [2010-R12]
Carrollton Northwest - Lakepointe 138kV | 14,243,808 | Upgrade NW Carrollton - Lakepointe (TNMP) 138 kV line [14TPIT0014]
Marion 345/138kV Autotransformer | 13,826,062 | 
Nicole - Oak Creek 138kV | 10,705,811 | CREZ
Garrott - Midtown 138kV | 10,158,439 | Upgrade 138 kV underground Ckt. 90 Garrott to Midtown to Polk
Ackerly Lyntegar - Sparenburg 69kV | 10,092,284 | Lamesa - Ackerly Vealmoor 69 kV line rebuild
West Levee Switch 345/138kV AT2 | 9,073,730 | 5YTP [2009-R21]

## Slide 5: PLWG/CMWG Effort
PGRR011 is part of Holistic Solution with Status update to ERCOT Board due in October
Meetings
  Friday, Sept 26
  Wednesday, August 31
  Wednesday, September 7
Many constructive comments and stakeholder interaction
Need ERCOT Operating and Planning Staff Input at Sept 7 Meeting
Coordinating NOGRR and NPRR Filing
Submission to ROS September 8
Will be considered at September 15 ROS Meeting

## Slide 6: SCR760 Status
SCR Sub Part | SCR Description | Status
SCR760-1 | Upgrade to PSS/E v32 | Submitted
SCR760-2 | Distribution Capacitor banks | Planning
SCR760-3 | Zero Impedance Line Ratings | Planning
SCR760-4 | Associate Loads and Capacitor banks with the correct CNG | Planning
SCR760-5 | Additional Transformer Data for Planning | Planning
SCR760-6 | FACTS Devices | Submitted
SCR760-7 | Assign valid PSSE IDs to Breakers/ Switches/ Series Devices | Planning
SCR760-8 | Phase shift of Autos for short circuit studies | Planning
SCR760-9 | Multisection Line Grouping | Planning
Table 1: In the following table:
Red will be used to show status of Not Submitted, meaning that the SCR sub part has not been submitted to Siemens as a Service Request.
Yellow will indicate that the SCR sub part has been submitted. The color will remain yellow and the status will change in order to Submitted, Planning (Requirements, SOW, Code Writing), Release (Siemens produces first code to test), and Testing (code has completed internal test and is moving through release management).
Green will indicate that the code has been tested and installed on the machines that ERCOT uses to produce Topology Processor output for Planning and CRR.

## Slide 7: SCR760 Status
Status update on SCR760, Changes Needed for Information Model Manager and Topology Processor for Planning Models, which was approved by the ERCOT Board in March 2011.
  Bundle 1 (Items 3, 7 and 8): Statement of Work (SOW) completed. Sample output for all three items approved by ERCOT. Initial release and updated documentation due August 15.
  Bundle 2 (Items 2, 4, 9): Item 5 removed from Bundle 2 to continue requirements definition without delaying remaining items 2, 4, and 9. ERCOT completed requirements with TSP review and is waiting on Siemens to update cost estimates due week of August 1.
  Item 5: Additional requirements review completed by ERCOT and sent to Siemens to verify implementation. Will send to TSPs for review upon completion. Item 5 may rejoin Bundle 2 at code release, otherwise will continue separately.
  Bundle 3 (Items 1 and 6): Asked Siemens to update document previously sent in December 2010 to determine differences between version 32 and version 30 of RAWD format. Update will determine differences through version 33 of RAWD.

## Slide 8: ROS Next Meetings
Thursday, Sept 15, 9:30 AM at ERCOT Austin