## Slide 1: Approval of Important Station Voltages for State Estimator Reporting Review of SE and Telemetry Standards
Alex Sills
Advanced Network Applications
10/13/11

## Slide 2: Objective
Approval of Important Buses as defined by the TAC-approved State Estimator Standards
  “On 20 most important station voltages designated by ERCOT and approved by ROS each October; the telemetered voltage minus State Estimator voltage shall be within 2% of the telemetered voltage measurement involved for at least 95% of samples measured during a 1 month period.”

## Slide 3: Important Station Voltages
Defines key stations to be monitored to ensure State Estimator accuracy
Reviewed and endorsed by the Network Data Support Working Group on 9/28/11

## Slide 4: Determination of Critical Buses
Major criteria for inclusion in important station voltage list:
  Nuclear plant buses
  Black Start synchronization point-related buses
  IROL associated buses
  Zonal CSC/CRE related buses
  345KV buses with large power transfers

## Slide 5: Station List
STATION_ID | VOLTAGE_LEVEL
BI | 345
ALNSW | 345
AUSTRO | 345
BNBSW | 345
CALAVERS | 345
CBY | 345
CPSES | 345
JEWET | 345
LON_HILL | 345
MGSES | 345
NEDIN | 345
NORSW | 345
RIOHONDO | 345
RNKSW | 345
SSPSW | 345
STP | 345
TMPSW | 345
VENSW | 345
WLVEE | 345
ZORN | 345

## Slide 6: Nodal Protocol 3.10.7.5 (1) – Telemetry Criteria
“The appropriate TAC subcommittee shall establish a task force that is open to Market Participants, comprised of technical experts, to develop a set of Telemetry Criteria consistent with the minimum requirements of the Protocols. TAC shall approve a set of telemetry criteria and the appropriate TAC subcommittee shall update the telemetry criteria annually each October or more often on a periodic basis as deemed necessary.”

## Slide 7: Nodal Protocol 3.10.9 (1) – State Estimator Standard
“The appropriate TAC subcommittee shall establish a task force that is open to Market Participants, comprised of technical experts to develop a State Estimator Performance Standard consistent with the minimum requirements of the Protocols. TAC shall approve the State Estimator Performance Standards, and the appropriate TAC subcommittee shall update the State Estimator Performance Standards annually each October or more often on a periodic basis as deemed necessary.”

## Slide 8: Conclusion
ERCOT SE report will monitor the telemetry vs. SE bus KV and document violations for the approved buses
SE and Telemetry Standards documents available in “Other Binding Documents” section of ERCOT Market Rules webpage. No changes have been proposed by ERCOT or any working groups for this year.
Seeking approval of 20 station voltages and existing SE and Tel Standards documents