## Slide 1: Congestion Cost Example
Jeff Billo, ERCOT Mid-Term Planning
ROS, November 2011

## Slide 2: ERCOT Economic Planning
Current ERCOT economic planning criteria uses a reduction in production costs or a reduction in energy revenue to justify transmission improvements
Ideally, when observing past congestion we would measure the production cost or energy revenue impact due to each transmission constraint
However, this is not practical using existing tools

## Slide 3
~
~
100 MW
Rating = 80 MW
$40/MW
$10/MW
LMP A = $10/MWh
LMP B = $40/MWh
Load Charge = $40 X 100 MW = $4000
Generator A Payment = $10 X 80 MW = $800
Generator B Payment = $40 X 20 MW = $800
Total Congestion Cost = $4000 -$800 -$800 = $2400
Shadow Price = $40 - $10 = $30
Congestion cost = Shadow price X Rating = $30 X 80 = $2400
Production cost = $800 + $800 = $1600
A
B
Example
Q: Where does the $2400 go?
A: In an ideal market, it goes back to load

## Slide 4
~
~
100 MW
Rating = 80 MW
$40/MW
$10/MW
LMP A = $10/MWh
LMP B = $10/MWh (the constraint is not binding)
Load Charge = $10 X 100 MW = $1000
Generator A Payment = $10 X 100 MW = $1000
Generator B Payment = $10 X 0 MW = $0
Total Congestion Cost = $1000 -$1000 -$0 = $0
Shadow Price = $0
Congestion cost = Shadow price X Rating = $0 X 200 = $0
Production cost = $1000 + $0 = $1000
Production cost savings = $1600 - $1000 = $600
A
B
What is the value of upgrading the line?
Rating = 200 MW

## Slide 5: Conclusions
Congestion cost is not the same as potential production cost savings or energy revenue savings
Congestion cost (rent) is a good metric for measuring where there is congestion, and hence inefficiencies on the system
  And can give a sense of magnitude of congestion
Questions?