## Slide 1: South Texas Electric Cooperative
Eagle Ford Shale Load
ERCOT RGP
11/11/11

## Slide 2: STEC MEMBER COOPS
Karnes Electric Cooperative (KEC)
Wharton Electric Cooperative (WCEC)
Jackson Electric Cooperative (JEC)
Victoria Electric Cooperative (VEC)
San Patricio Electric Cooperative (SPEC)
Nueces Electric Cooperative (NEC)
Medina Electric Cooperative (MEC)
Magic Valley Electric Cooperative (MVEC)

## Slide 3: STEC Transmission
69 kV transmission: approximately 1430 miles
138 kV transmission: approximately 495 miles
345 kV transmission: approximately 72 miles
Total STEC transmission: approximately 2000 miles
Note: mileage data from ERCOT 2011 summer peak case updated in February, 2011.

## Slide 4: STEC Transmission System

## Slide 5: STEC Member Load
Total Load: 1205 MW ( 2010 NC PEAK)
MVEC: 581 MW
MEC: 165 MW
VEC: 115 MW
NEC: 100 MW
KEC: 85 MW
JEC: 64 MW
WCEC: 47 MW
SPEC: 48 MW

## Slide 6: Eagle Ford Shale
Oil reserves estimated at 3 billion barrels and the discovery may also contain trillions of cubic feet of natural gas.
May be the sixth largest oil field discovered in the US and the largest discovery in the past 40 years.

## Slide 7: Well Activity in the Eagle Ford Shale
As of April 29, 2011:
1,698 Wells Permitted
111 on schedule – oil
220 on schedule - gas

## Slide 8: STEC Coops with Eagle Ford Shale Activity
Jackson Electric Coop
Karnes Electric Coop
Medina Electric Coop

## Slide 9: Load Forecast with Eagle Ford Shale
Non-coincident peak load
 | 2010 (MW) Actual | 2011 (MW) | 2012 (MW) | 2013 (MW) | 2014 (MW) | 2015 (MW) | 2016 (MW)
KEC | 85 | 107 | 213 | 220 | 232 | 242 | 250
JEC | 64 | 67 | 97 | 163 | 168 | 172 | 176
MEC | 165 | 195 | 248 | 267 | 279 | 294 | 305
Total | 314 | 369 | 558 | 650 | 679 | 708 | 731

## Slide 10: Jackson Transmission Project (Vanderbilt to El Campo Rebuild)
Submitted to RPG on 10/07/11
Under ERCOT independent review as of 11/01/11

## Slide 11: Karnes & Medina Transmission Projects
Under Study

## Slide 12: Planning Considerations
69 kV system is rated at 40-45 MVA and has limited thermal capacity to support new load
69 kV system is voltage limited
Reactive support critical to support load levels expected by 2012 summer peak.
Timing of new loads requires transmission solutions that can be quickly implemented.
Double circuit 138/69 kV transmission reduces/defers substation conversion costs.

## Slide 13: Questions?