## Slide 1: IMM alternate framework for Look-Ahead SCED
November 21, 2011

## Slide 2: Objectives
Rationally commit Generation and Load Resources that can come online or curtail within 15 to 30 minutes.
  Restore one of the few good features of the zonal market that was lost with the implementation of nodal (i.e., the quick-start deployment mechanism that included reasonable notice and minimum run-times.)
  Do so without otherwise disrupting the benefits of the 5-minute SCED dispatch based on current, actual system conditions.
Provide indicative pricing for future intervals.

## Slide 3: Outputs
Indicative prices for the next two 5-minute periods and two subsequent 15-minute periods
Startup Instruction for Generation Resources that can startup in the intervals being optimized. Offline Resources that are awarded are the ones issued Startup Instructions.
Curtailment Instructions for Load Resources that need advance notification and that can be curtailed in the intervals being optimized. The criteria for Load Resources to be issued Curtailment Instructions to be discussed (may need new COP status).

## Slide 5: Two 15-minute Interval Optimization (1 of 5)
Application runs every quarter hour.
Time period under consideration starts 15 minutes into the future and spans two consecutive 15 minute settlement intervals for a total time period of optimization of 30 minutes.
  Open Question about whether the two 15 minutes intervals are considered sequentially or are jointly optimized.
This application only considers an Energy Offer Curve from Generation and Load Resources (One Part offer)
  Submitting flat curves will minimize partial deployments.
If Resource follows Startup/Curtailment Instructions, deployed MWs are guaranteed to be settled to at least their Offer price for 15 minutes. Offer price may be mitigated.
  Details to be determined

## Slide 6: Two 15-minute Interval Optimization (2 of 5)
Startup of Generation Resources and Curtailment of Load Resources need to be consistent with past and future statuses (telemetry in the past and COP in the future).
For the 15-minute interval in the same hour as current, telemetry status is used. If a 15-minute interval is in the next hour, as compared to current telemetry, then COP status is used.

## Slide 7: Two 15-minute Interval Optimization (3 of 5)
Startup and Curtailment Instructions for first 15 minute interval of time period of optimization is BINDING.
Startup and Curtailment decisions for second 15 minute interval of time period of optimization is BINDING (becomes Instructions) only if the Resource characteristics (startup time, etc.) do not allow the Startup and Curtailment decisions to be delayed for the next run of this application.
Startup and Curtailment Instructions (binding only) from previous run of application will be respected in the current run.

## Slide 8: Two 15-minute Interval Optimization (4 of 5)
Temporal constraints will be preprocessed. A list of eligible Resources for Startup/Curtailment will be determined by a preprocessing step using submitted temporal data.
Offer from Resources will be treated as continuous variables between 0 and HSL(Gen) or 0 and MPC (Load) and if the award is greater than some percentage of LSL (Gen) or LPC (Load) a start-up/deploy instruction will be issued.

## Slide 9: Two 15-minute Interval Optimization (5 of 5)
The dispatch for the two 15-minute intervals will have the following :
  Ramp Rate constraints are explicitly modeled (i.e. no LDL,HDL limits) if the two 15-periods are jointly optimized.
    ramp rates from curve or telemetry?
  Implement Mitigation as in ‘ Real’ SCED (Run Step 1-competitive constraints & Step 2-all constraints)
The initial conditions for resources at the start of the time period to be optimized (15 minutes in the future)
  Use current SCED sequentially for two additional 5- minute intervals, feeding the Base Points from last sequential SCED run as starting point for next SCED run in the sequence

## Slide 10: Future Indicative Prices
Sequential SCED is run every 5 minutes. Sequential SCED starts after Current SCED has completed.
Sequential SCED is run for 2 future intervals using the Base Points of the most recent binding SCED run as the initial condition. Then for time intervals 15-30 minutes and 30-45 minutes into the future, the indicative prices will be output from the two interval optimization run.
For future intervals :
  Use short term load forecast (may be modified by current GTBD and GTBD trend for the past ‘x’ 5-minute intervals)
  For WGR, the value of HSL will be a combination of STWPF (hourly value) with adjustments from telemetered HSL (to capture trends).
  Telemetered DSR output schedule and telemetered DSR load will be kept persistent for all the 5-minute intervals under consideration by sequential SCED. If the DSR resources submit future 5-minute Output Schedules then these values will be used.

## Slide 11: Other Changes
Need a complementary SCED run to determine pricing for LSL energy and make-whole for marginal units that may be backed down to accommodate LSL energy from Resources committed by Look-Ahead.

## Slide 12: Other Changes – Quick Start and Non-Spin
Current practice of QSGR participating in SCED will be eliminated.
Resources providing NSRS are obligated to submit offers in the Look-Ahead.
Provision of NSRS from online Resources will be eliminated.

## Slide 13: Other Changes - Loads
Settlement point for Load Resources to participate in Real-Time Energy Market (only?)
Model Load Resources with Offers in SCED.
Add Load Resource Awards from previous interval to GTBD.