## Slide 1: NPRR 418 Reporting of Forced Outages
Improved Situational Awareness
More efficient event reconstruction
More accurate forecasting of Outage rates

## Slide 2
When a Unit is Forced Out . . .
There are five potential communication paths between the Resource and ERCOT for reporting Forced Outage data – each has it own unique challenges
Outage Scheduler
Telephone
COP data
Telemetry
Protocols require Resources to only enter Forced Outages in the Outage Scheduler that last more than 2 hours resulting in incomplete set of data.
Protocols do not require Resource Operators to call ERCOT and report Forced Outages
Resources can report a status in COP but cannot update COP until approximately 2 hours after event
Resources telemeter their status in real-time. Status is correctly telemetered only 80% of time
RFI
Resources can provide accurate accounting of status, but process is lengthy and burdensome for ERCOT and QSEs
Only current source for complete Outage Information
Only Tool for Outage
Forecasting (SARA) even though FO data incomplete
Only current source for information in Real Time
Forced Outage Detector
(Only as good as telemetered status)
Forecasting
Situational Awareness
Event Reconstruction

## Slide 3
After NPRR418
Outage Scheduler
Telephone
COP data
Telemetry
All Resource Forced Outages entered in Outage Scheduler resulting in a complete and up-to-date dataset.
Reduced need for verbal confirmation
RFI
Need for RFIs will be reduced
With Complete dataset,
Best tool for Event Reporting
With Complete dataset,
Best Tool for Outage Rate Forecasting (SARA)
Improved Situational Awareness in Real Time
Forced Outage Detector
Improvement in Telemetered Status by cross check with OS entry
Forecasting
Situational Awareness
Event Reconstruction