## Slide 1
Reliability Deployment Task Force (RDTF Meeting)
December 20th 2011
December 20, 2011

## Slide 2: Impact of New Power Balance Penalty Curve on PNM
December 20, 2011
PB Violation MW | Current | Original CPS Proposal | New CPS Proposal | IMM Proposal
0 | 200 | 200 | 200 | 200
1 | 200 | 200 | 200 | 200
1 | 250 | 250 | 250 | 250
5 | 250 | 250 | 250 | 250
5 | 300 | 300 | 300 | 300
10 | 300 | 300 | 300 | 300
10 | 400 | 500 | 350 | 400
20 | 400 | 500 | 350 | 400
20 | 500 | 750 | 400 | 500
30 | 500 | 750 | 400 | 500
30 | 1000 | 1000 | 500 | 1000
40 | 1000 | 1000 | 500 | 1000
40 | 2250 | 2250 | 1000 | 2250
50 | 2250 | 2250 | 1000 | 2250
50 | 3001 | 3001 | 2000 | 4000
75 | 3001 | 3001 | 2000 | 4000
75 | 3001 | 3400 | 3400 | 4000
150 | 3001 | 3400 | 3400 | 4000
150 | 3001 | 3600 | 3600 | 4000
250 | 3001 | 3600 | 3600 | 4000
250 | 3001 | 3800 | 3800 | 4000
400 | 3001 | 3800 | 3800 | 4000
400 | 3001 | 4000 | 4000 | 4000
500 | 3001 | 4000 | 4000 | 4000
500 | 3001 | 4000 | 4000 | 4000

## Slide 3: Impact of New Power Balance Penalty Curve on PNM
December 20, 2011
Original CPS Proposal (Submitted to RTDF) : Same as existing curve between 1-10 MW and 30-75. Penalty cost higher between 10-30 and above 75 MW under-generation.
New CPS Proposal (Submitted to PUCT) : Same as existing curve between 1-10 MW. Lower penalty between 10-75 MW, while finishing higher for 75 MW and up.
IMM Proposal : Same as existing curve except for after 50 MW under-generation, the penalty increase from existing $3001/MWh to $4000/MWh
All at $3001
PNM addition is calculated as the sum of time weighted difference between new penalty and old penalty for each level of Power Balance violation. For the first 3 cases, the assumption is that Power Balance Violation amount is not changing when the curve changed. For the last one since the new penalty is above SWCAP, all offers will be used before violating Power Balance and hence only intervals were the rampable room in SCED offered below SWCAP is less than Power Balance violation were considered. i.e. the effect of increase in prices when the rampable room in SCED offered below SWCAP is greater than Power Balance violation due to clearing more from the offer stack was not considered.
Proposed Curve | PNM change | Excluding intervals GTBD >66,195 MW
Original CPS | 14,427 | 11,339
New CPS | 8,082 | 6,032
IMM | 22,474 | 17,740
All at 3001 | 14,700 | 12,830