## Slide 1
Reliability Deployment Task Force (RDTF Meeting)
December 20th 2011
December 20, 2011

## Slide 2: NPRR
6.4.3.1 Energy Offer Curve for RUC-Committed Resources
(1) Prior to the end of the Adjustment Period for an Operating Hour during which a Generation Resource has been committed by ERCOT as part of a Reliability Unit Commitment (RUC) process, the QSE shall ensure that an Energy Offer Curve that prices all energy from LSL to HSL at or above $XXX/MWh for the Operating Hours in the RUC commitment period, has been submitted and accepted by ERCOT.
(2) If the QSE receives a RUC Dispatch Instruction from ERCOT for its Generation Resource during the Operating Period that includes a RUC-Committed Hour, then the QSE shall be exempt from the submission timeline requirement specified in paragraph (1) above and shall instead submit the required Energy Offer Curve as soon as reasonably practicable after receipt of the RUC Dispatch Instruction.
(3) The requirement in paragraph (1) above is not applicable for Weekly Reliability Unit Commitment (WRUC)-instructed hours during which the Resource was Day-Ahead Market (DAM)-committed or QSE self-committed.
December 20, 2011

## Slide 3: RUC Committed Resources Dispatched for Capacity (12/01/2010 to 10/31/2011)
  8640 Effective RUC Unit Hours
  1787 hrs (20.7%) were dispatched above LSL for capacity (LMP<=System Lambda and BP>=LSL+2)
    1560 hrs(18.1%) with prices below $100
    71 hrs(0.8%) with prices between $100 and $200
    33 hrs(0.38%) with prices between $200 and $300
    16 hrs(0.19%) with prices between $300 and $400
    8 hrs (0.09%) with prices between $400 and $500
    38hrs (0.4%) with prices between $500 and $3000
    61hrs (0.7%) with prices greater than or equal to $3000
‘Effective RUC Unit Hours’ considers multiple units committed for the same hour as different unit hours while ‘Effective RUC hours’ considers it as single hour.
December 20, 2011

## Slide 4: RUC Committed Resources Dispatched for Capacity (12/01/2010 to 10/31/2011)
  8640 Effective RUC Unit Hours
  LMP<=System Lambda+2 and BP>=LSL+2 to determine dispatch for capacity
    2107 hrs (24.4%) were dispatched above LSL for capacity
      2008 hrs (23.2%) with prices below $500
      38 hrs (0.4%) with prices between $500 and $3000
      61 hrs (0.7%) with prices greater than or equal to $3000
December 20, 2011
Notes: RN LMP = System lambda & BP> LSL => Resource is moved up for capacity since there is no congestion
RN LMP > System lambda & BP> LSL => Resource can contribute to reducigng congestion and hence could be moved up for transmission.
<number>

## Slide 5: RUC Committed Resources (12/01/2010 to 10/31/2011)
December 20, 2011

## Slide 6: RUC Committed Resources (12/01/2010 to 10/31/2011)
December 20, 2011

## Slide 7: 0 to LSL Energy from ONRUC
8640 Effective RUC Unit Hours
    Average ONRUC LSL is 82 MW , BP is 99.6 MW, HSL is 207 MW
  5741 hrs (66.4%) are at or below LSL (BP-LSL<2MW)
    Average ONRUC LSL is 85MW
  2899 intervals (33.6%) are above LSL for transmission or capacity
    Average ONRUC LSL is 75.5MW
3071 Effective Hours with at least one resource on ONRUC status
    Average system total ONRUC capacity
      LSL is 230.5 MW;
      HSL is 581.8MW;
      BP is 279.9MW
Effective RUC Unit Hours’ is SCED duration, summed up to hour level, for each RUC committed resource when it was online. ‘Effective RUC Unit Hours’ considers multiple units committed for the same hour as different unit hours while ‘Effective RUC hours’ considers it as single hour.
December 20, 2011

## Slide 8: RUC Committed Resources (12/01/2010 to 10/31/2011)
December 20, 2011
Notes: Offer floor could increase the system lambda for all intervals with Capacity Headroom <=0
<number>

## Slide 9: RUC Committed Resources (12/01/2010 to 10/31/2011)
December 20, 2011

## Slide 10: RUC Committed Resources (12/01/2010 to 10/31/2011)
December 20, 2011

## Slide 11: RUC Committed Resources (12/01/2010 to 10/31/2011)
December 20, 2011

## Slide 12: RUC Committed Resources
December 20, 2011