## Slide 1: Draft NPRR Discussion Emergency Response Service (ERS)
Paul Wattles
ERCOT Staff
March 8, 2012
Update to ROS

## Slide 2: Overview
Rule: PUC Project 39948 to amend Subst. Rule §25.507
  PUC Staff confirmed that proposal for adoption will be posted for consideration at March 22 PUC Open Meeting
Accompanying NPRR schedule:
  Still in draft form, current version will be sent to exploders and will post to meeting pages
    Still tweaking with ERCOT Legal but major provisions are unchanged
  Initial review at COPS, WMS and ROS in February
  Reviewed at PDCWG Feb. 28
  Return visits to WMS and ROS in March
  Filed with number by March 15
  PRS March 22
    ERCOT will offer comments to amend NPRR to be consistent with any changes adopted in the PUC Rule
  TAC and Board in April
  June 1 effective date
Notes: <number>

## Slide 3: Changes since last month
Clarified definition of ERS Generator:
  Either (1) an individual generator contracted to provide ERS which is not a Generation Resource or a source of intermittent renewable generation and which provides ERS by injecting energy to the ERCOT System, or (2) an aggregation of such generators.
ERS Generators come in 2 types:
  ‘Self-serving generators’
    May offer only that capacity above the level serving the native Load
    May not operate above that level except during ERS deployment events (availability requirement)
  ‘Non-self serving generators’
    Normally at zero generation except during testing and ERS deployment events
    Considered available if at zero generation, unless part of a self-test or ERCOT unannounced test

## Slide 4: Discussion at PDCWG
Will ERS Generators be required to provide voltage support and primary frequency response?
  Voltage Support is a requirement for Generation Resources, which are ineligible for ERS
  Primary Frequency Response is required of All-Inclusive Generation Resources, which include Non-Modeled Generators
    If a Non-Modeled Generator provides ERS, it would be subject to Protocols 8.5.1.1 to provide Primary Frequency Response
Will ERS Generators have similar weatherization requirements to Generation Resources?
  PUC Rule 25.53 requires Power Generation Companies to submit: ‘summary of power plant weatherization plans and procedures’
  However, no current language in Rules, Protocols or Guides relating to guidelines for weatherization
  If guidelines or rules are adopted, ERCOT will consider expanding them to include ERS Generators

## Slide 5: Questions?
ON
OFF
pwattles@ercot.com
512/248-6578