| PGRR Number | 020 | PGRR Title | Administrative Changes for the June 1, 2012 Planning Guide |
| --- | --- | --- | --- |
| Date Posted | May 16, 2012 |
| Status | Administrative Change |

| Planning Guide Section Requiring Revision | 8.3.1, Peak Load Estimate |
| --- | --- |
| Protocol Section(s) Requiring Revision, if any | None. |
| Revision Description | This Administrative Planning Guide Revision Request (PGRR) updates the Planning Guide to reflect the changes proposed through Nodal Protocol Revision Request (NPRR) 451, Implementation of New P.U.C. Subst. Rule 25.507, Electric Reliability Council of Texas (ERCOT) Emergency Response Service (ERS), which was approved by the ERCOT Board on April 17, 2012. Changes are limited to updating references of Emergency Interruptible Load Service (EILS) to Emergency Response Service (ERS). |
| Reason for Revision | Administrative change to maintain accurate information as allowed by Section 1.1, Introduction. |

| Sponsor |
| --- |
| Name | Paul Wattles |
| E-mail Address | pwattles@ercot.com |
| Company | ERCOT |
| Phone Number | 512-248-6578 |
| Cell Number |  |
| Market Segment | Not applicable |

| Market Rules Staff Contact |
| --- |
| Name | Yvette M. Landin |
| E-Mail Address | ylandin@ercot.com |
| Phone Number | 512-248-4513 |

Proposed Guide Language Revision

### 8.3.1	Peak Load Estimate

ERCOT shall prepare, at least annually, an estimate of the total peak Load for both summer and winter peak Load periods for the current year and a minimum of ten future years using an econometric forecast, taking into account econometric inputs, weather conditions, demographic data and other variables as deemed appropriate by ERCOT.  The firm peak Load forecast shall be determined by the following equation:

FIRMPKLDs ,i	=	TOTPKLDs, i – LRRRSs, i – LRNSRSs, i – ERSs, i – CLR s, i – ENERGYEFF s, i

The above variables are defined as follows:

| Variable | Unit | Definition |
| --- | --- | --- |
| FIRMPKLDs, i | MW | Firm Peak Load Estimate—The Firm Peak Load Estimate for the Peak Load Season s for the year i. |
| TOTPKLDs, i | MW | Total Peak Load Estimate—The Total Peak Load Estimate for the Peak Load Season s for the year i. |
| LRRRSs, i | MW | Load Resource providing Responsive Reserve (RRS)—The amount of RRS a Load Resource is providing for the Peak Load Season s for the year i. |
| LRNSRSs, i | MW | Load Resource providing Non-Spinning Reserve (Non-Spin)— The amount of Non-Spin a Load Resource is providing for the Peak Load Season s for the year i. |
| ERSs, i | MW | Emergency Interruptible Load Service (ERS)— The amount of ERS for the peak Load Season s for the year i based on: (a) For the winter Peak Load Season of the current year, the amount of ERS procured by ERCOT for the October to January ERS Contract Period using the simple average of two time period procurements (Business Hours and Non-Business Hours); (b) For the summer Peak Load Season of the current year, the amount of ERS procured by ERCOT for the May procurement (Business Hours); and (c) For all subsequent years and Peak Load Seasons, escalate the amount of ERS from the previous Season by 10%. |
| CLRs, i | MW | Amount of Controllable Load Resource—Amount of Controllable Load Resource that is available for Dispatch by ERCOT during the current year i for the Peak Load Season s not already included in LRRRS or LRNSRS. |
| ENERGYEFFs, i | MW | Amount of Energy Efficiency Programs Procured—Amount of energy efficiency programs procured by Transmission and/or Distribution Service Providers (TDSPs) pursuant to P.U.C. Subst. R. 25.181, Energy Efficiency Goal, for the peak Load Season s for the year i. |
| i | None | Year. |
| s | None | Peak Load Season (summer or winter as defined above). |