## Slide 1: Analysis for Potential Changes to the Power Balance Penalty Curve
June 1, 2012
RDTF
John Dumas

## Slide 2: Analysis of Historical Load
The following analysis was done using historical load data from June, July and August of 2011 between noon and 6 PM
  The average change in load over a 10 minute period during this study time was an increase of 216 MW
  For Net-Load, this number changes to 200 MW
RDTF
June 1, 2012

## Slide 3: Analysis of Historical Real-Time Energy Offers
The aggregate energy offer curve seen by step 1 of SCED was analyzed for 3 different SCED executions:
  16:00 on Aug. 24th, 2011 (High load day from Summer 2011)
  7:10 on Jan. 13th, 2012 (High load day from Winter of 2012)
  18:30 on Mar. 9th, 2012 (Spring day in which prices went to 3000 $/MWh)
The reason for looking into these curves is to investigate how the Power Balance Penalty Curve (PBPC) could interact with the energy offers that have been submitted by the Market Participants
The PBPC is included in the aggregate offer curves
RDTF
June 1, 2012

## Slide 4: Analysis of Historical Real-Time Energy Offers
Aug. 24th, 2011
  One of the peak load days from 2011 (~66,500 MW)
  Prices at ~3,000 $/MWh for several intervals
  Went into EEA step 2a at 15:08
RDTF
June 1, 2012
Price ($/MWh) | Percent of Price/MW Pairs Below: | Amount of MWs Offered Below:
200 | 91.9% | 64720
500 | 93.3% | 64785
1,000 | 97.6% | 65239
2,250 | 97.8% | 65249
3,001 | 99.9% | 65455

## Slide 5: Analysis of Historical Real-Time Energy Offers
Jan. 13th, 2012
  Day had one of the higher peak loads of this last Winter (~47,000 MW)
  Prices stayed relatively low and never went above 100 $/MWh
RDTF
June 1, 2012
Price ($/MWh) | Percent of Price/MW Pairs Below: | Amount of MWs Offered Below:
200 | 90.4% | 47577
500 | 96.8% | 48508
1,000 | 97.4% | 48543
2,250 | 98.0% | 48574
3,001 | 99.8% | 48706

## Slide 6: Analysis of Historical Real-Time Energy Offers
Mar. 9th, 2012
  Day had relatively mild peak load (~37,500 MW)
  Prices went to ~3,000 $/MWh around 18:30 for 4 SCED intervals
RDTF
June 1, 2012
Price ($/MWh) | Percent of Price/MW Pairs Below: | Amount of MWs Offered Below:
200 | 87.9% | 36625
500 | 94.9% | 37276
1,000 | 95.4% | 37286
2,250 | 96.3% | 37303
3,001 | 99.8% | 37427