## Slide 1
WMS June 13, 2012

## Slide 2: Problem Statement
If we move to a $4,500/MWh offer cap in August, the PBPC will need to be adjusted.
The current PBPC is, in essence, an energy offer curve for a virtual generation resource, and does not get “deployed” after all available competitive offers are exhausted(as it is sometimes described), but rather is “deployed” as the price for Regulation through SCED any time prices rise above the $200 starting point of the curve.
There is always a risk with a static PBPC that it will be “deployed” even when sufficient generation is available to meet demand.
Currently, the starting point for the PBPC is $200/MWh. As a result, the PBPC intervenes in front of other competitive offers as soon as prices reach $200/MWh.
In RDTF, Luminant advocated for a “dynamic PBPC” that would begin $1 above the last available offer and rise to the offer cap.
Given the complexities of implementing a “dynamic PBPC” by August 2012, Luminant now supports Chairman Nelson’s proposed PBPC as the best alternate solution.

## Slide 3: Ramp Rate Concern
Using data from the first 12 months of nodal operation, the situation where SCED was completely out of available ramp had the potential of occurring in 61 intervals out of a total of over 104,000. In other words, the potential for ramp rate related spikes is .059% or 59/1000ths of one percent.
On the other hand, the potential that the PBPC is used to undercut competitive offers, because of its low starting point and gradual slope, occurs nearly 1 percent of the time.

## Slide 4: Nelson’s Proposed Curve
MW violation | Violation <1 | 1 ≤ Violation < 5 | 5 ≤ Violation < 10 | 10 ≤ Violation < 20 | 20 ≤ Violation < 30 | 30 ≤ Violation < 40 | 40 ≤ Violation < 50 | 50 ≤ Violation < 100000
Price $/MWh | 500 | 500 | 500 | 1000 | 1000 | 3000 | 3000 | 4500
MW violation | Violation <1 | 1 ≤ Violation < 5 | 5 ≤ Violation < 10 | 10 ≤ Violation < 20 | 20 ≤ Violation < 30 | 30 ≤ Violation < 40 | 40 ≤ Violation < 50 | 50 ≤ Violation < 100000
Price $/MWh | 200 | 250 | 300 | 400 | 500 | 1000 | 2250 | 3001
Current PBPC
Nelson’s Proposed PBPC

## Slide 5: Principles
The PBPC should not be allowed to undercut any dispatchable competitive energy offers that are not ramp rate limited.
PBPC should price at SWOC if there are no ramp rate limitations and energy is exhausted. In other words, we should not lean on Regulation for any amount of time at a price less than SWOC if available energy is exhausted.
PBPC should be at a maximum of 50MWs and should be priced at SWOC at that point. If the PBPC is longer, it further diminishes reliability and it can extend the time that ERCOT is experiencing actual scarcity without prices reflected at the SWOC.