## Slide 1: CMWG Update to WMS
7-11-12
Report of CMWG Meeting of 7-10-12
M Wagner
Edison Mission Marketing & Trading

## Slide 2: 2% Shift Factor Cut Off vs. Holistic Solution
Issue: Currently Operations uses a 2% cutoff to limit re-dispatch (along with existing SP Caps). Nodal Protocols created shadow price caps to limit re-dispatch and did not include SF cutoff.
Transmission & Security Op Procedure-- 4.1 Transmission Congestion Management

## Slide 3: Brief History: 2% Shift Factor Cut Off
Developed in Zonal—where
  portfolio deployment
  manually developed constraints
  no Shift Factor cut offs
  Resulted at times in moving large # of MW for remote constraints—which also contributed to stranding Ancillary Service MW
In Nodal—
  unit specific dispatch provides granular control,
  RT Constraint Activity Manger provides real time insight into constraints,
  Shadow Price caps inherently truncate redispatch

## Slide 4: 2% Shift Factor Cut Off vs. Holistic Solution
Eliminate 2% Cutoff | Retain 2% Cutoff
Nodal Protocols designed to create economic dispatch relying on Shadow Price caps to cut off redispatch—SP cap levels based on significant analysis from IMM | Dispatch is working now—urge caution—system is complex
QSEs can move their AS to other units or ERCOT can run SASM to replace AS that are not supplied | Small QSEs cannot move AS
Currently SCED can take ~ 30 active constraints—generally under 10 active at given time Multiple binding constraints (oscillation) is currently managed—no changes to this | What happens if more than 30 constraints With multiple binding constraints, is there a chance units would move around too much (oscillation)?
CMWG Discussion Pro/Con Eliminate 2% Cutoff
WMS direction?

## Slide 5: Over-Mitigation in SCED
Issue: large # of MW of resources at same mitigated offer price. Unintended consequences.
One result is tie breaker logic can send small MW dispatches to offline NonSpin units—if they turn on in response to dispatch, ERCOT gets more MW than needed which lowers RT price due to price taker MW (0-LSL issue) and creates inconsistent results for Quick Starts

## Slide 6: Over-Mitigation in SCED
Issue: large # of MW of resources at same mitigated offer price. Unintended consequences.
One result is tie breaker logic can send small MW dispatches to offline NonSpin units—if they turn on in response to dispatch, ERCOT gets more MW than needed

## Slide 7: Over-Mitigation in SCED: IMM Proposed Solution
Modify Mitigated Offer curves by adding incremental cost to offer curve
Currently
  Capped & Bounded (C&B) offer curve for Resource in SCED Step 2 = Max (MOC, Ref LMP Step1) for each point on the offer curve.
  Proposed change C&B offer curve for Step 2 = Max(MOC, Ref LMP Step1 + MOC * 0.01) [The 0.01 is for discussion--could be different]
Would create differentiation across “clumps” of MW at same price--potentially reducing RT commitment of Quick Starts

## Slide 8: Over-Mitigation in SCED
Discussion
  Would it solve the problem? Could result in same unit within a QSE always being deployed—potential concern for QSE
  Philosophy of ERCOT/IMM to adjust offer curves to resolve “contestability” appears inconsistent with recent arguments on where assertions made that large MW offered at same price were not competitive—this solution was not offered up for those discussions
  Solution would impact RT SCED, LA SCED –delivery could be lengthy or fast depending on prioritization
IMM to report back on diversity of Mitigated Offer Curves