## Slide 1: Anticipated Impacts for FRRS Pilot Program
ERCOT TAC Meeting
September 7, 2012

## Slide 2: Agenda
DNV KEMA Introduction
Review Order 755 and Related ISO Experience
Summary of DNV KEMA PJM Fast Response Study
Criteria for FRRS Assessment
Questions

## Slide 3: Review FERC Order 755
FERC finalized Order 755 last summer and introduces a performance payment to current regulation markets
Performance payment contains two key aspects
Add a regulation market product that rewards regulation resources based on the amount of regulation energy they provide
  Basis is that faster resources travel more “MWs” than slower resources thereby doing more work
  As a result, this portion of Order 755 is referred to as the “MW-mileage” payment
Base MW-mileage payments for any type of regulation provider on performance
  Difficult to separate random generator movements from responses to regulation signals
  Other ISOs have developed 2 and 3 statistical metrics to determine how well a generator followed AGC signals
Every system operator is responding to this order in different ways

## Slide 4: PJM Fast Acting Resources – Project Goals
Establish a platform for these and other long term dynamics / system regulation and frequency response studies of the PJM system and its resources by developing a KERMIT model implementation of the PJM system and calibrating it to observed real time data
Examine the relative performance and impact on system performance of fast versus traditional regulation resources
Simulate and analyze the metric of MW-mileage and response accuracy for resources with different responses to the PJM regulation control signals.

## Slide 5: PJM Fast Acting Resource – Key Findings / Conclusions
Based on the simulations, the addition of faster regulation resources in 5% increments (from 5% to 50% of the regulation requirement), improved the average CPS1 scores for all studied dates, when compared to the base case simulation results and while keeping the same regulation requirements as in present practice.
Over 12 sample days of simulation, fast resources provided 30% more value than conventional

## Slide 6: List of Economic / Operational Impacts
Change in net regulation deployment
  This is the primary metric for ERCOT and where we expect the majority of benefits / costs to be observed
Leads to Potential Reductions in Procured Regulation Capacity
  Use regulation deployments per regulation capacity as metric indicating regulation capacity savings
  Weighted ratio of regulation MW-mileage of conventional resources to fast resources is first order (linear) indication of how much less regulation capacity can be procured and still maintain the same system performance
Avoided reserve deployments
  Difficult to estimate, would need to make assumptions about what would have happened if FRRS Pilot Program was not in place
Change in administrative costs
  Providing two regulation products may increase ERCOT O&M

## Slide 7: List of Long Term Benefits
These are post pilot long term benefits that could be observed
More efficient dispatch
  Measure changes in total MW bid into other ERCOT markets
  Generators that no longer participate in regulation market may increase their participation in the real time market
  FFRS pilot study first step towards estimating market efficiency benefits; simulations using the pilot data next step to quantify system wide effects
Increased system reliability
  Difficult to measure, can track change in average reserve deployments or MW of load lost
  Would need to make assumptions about what would have happened if FRRS Pilot Program was not in place

## Slide 8: Additional Considerations
Need to control results for varying system conditions
  Wind and other sources of variability will change from the base case to when the FRRS pilot program is implemented
  Generation portfolio can change (e.g. increased wind capacity over course of pilot study, generator builds and retirements)
  Market structure and competitiveness of FRRS and Regulation markets
  Weather
  Industrial and commercial production
And need to examine results based on FRRS pilot program implementation details
  FRRS parameters can be examined and modified during the course of the pilot program
  ERCOT can examine how sensitive the results are to FRRS implementation
Results can be controlled and examined either through a statistical analysis or via simulations