## Slide 1: Tab 5: Operations Report (Sep & Oct 2012)
H.B. “Trip” Doggett
President & Chief Executive Officer
Board of Directors Meeting
ERCOT Public
November 13, 2012
Notes: <number>

## Slide 2: Summary – September 2012
September 2012 Operations
  The peak demand of 64,862 MW on September 5th was less than the mid-term forecast peak of 65,492 MW and more than the September 2011 actual peak demand of 63,160 MW. The instantaneous peak load on September 5th was 65,020 MW.
  Day-ahead load forecast error for September was 3.43%
  No Advisories issued for Physical Responsive Capability (PRC) below 3000 MW
  No Watches issued for PRC under 2500 MW
  No Energy Emergency Alert (EEA) events
Planning Activities
  143 active generation interconnection requests totaling over 39,000 MW, including 21,000 MW of wind generation as of September 30, 2012. This is three more requests, and 2,000 MW additional since August 31, 2012
  10,035 MW wind capacity on line September 30, 2012; No change from August 31, 2012
Tab 5
ERCOT Public
Notes: <number>

## Slide 3: Summary – October 2012
October 2012 Operations
  The peak demand of 48,256 MW on October 4th was less than the mid-term forecast peak of 50,447 MW and less than the October 2011 actual peak demand of 49,709 MW. The instantaneous load on October 4th was 48,422 MW.
  Day-ahead load forecast error for October was 3.00%
  No Advisories issued for Physical Responsive Capability (PRC) below 3000 MW
  No Watches issued for PRC under 2500 MW
  No Energy Emergency Alert (EEA) events
Planning Activities
  143 active generation interconnection requests totaling over 40,000 MW, including 21,000 MW of wind generation as of October 29, 2012. This is the same number of requests but 1,000 MW additional total MW since September 30, 2012
  10,035 MW wind capacity on line October 29, 2012; No change from September 30, 2012
Tab 5
ERCOT Public
Notes: <number>

## Slide 4: September 2012 Daily Peak Demand: Hourly Average Actual vs. Forecast, Wind Day-Ahead COPs & On-line Capacity at Peak
Note: All data are hourly averages during the peak load hour obtained from COPs, and EMMS.
Tab 5
ERCOT Public
Notes: <number>

## Slide 5: October 2012 Daily Peak Demand: Hourly Average Actual vs. Forecast, Wind Day-Ahead COPs & On-line Capacity at Peak
Note: All data are hourly averages during the peak load hour obtained from COPs, and EMMS.
Tab 5
ERCOT Public
Notes: <number>

## Slide 6: Market Statistics – September 2012
Market Statistics | Sep 2011 | Sep 2012 | 2011 Average | 2012 YTD Average
Percentage of Real-Time load hedged in Day-Ahead Market | 113.96% | 122.47% | 115.13% | 121.64%
Load-Weighted Average ‘ERCOT Hub Average 345 kV Hub’ Settlement Point Price in Day-Ahead Market ($/MWh) | 38.24 | 30.33 | 55.19 | 30.72
Load-Weighted Average ‘ERCOT Hub Average 345 kV Hub’ Settlement Point Price in Real-Time ($/MWh) | 40.25 | 25.97 | 50.83 | 26.44
Tab 5
ERCOT Public

## Slide 7: Market Statistics – October 2012
Market Statistics | Oct 2011 | Oct 2012 | 2011 Average | 2012 YTD Average
Percentage of Real-Time load hedged in Day-Ahead Market | 121.22% | 126.83% | 115.13% | 122.15%
Load-Weighted Average ‘ERCOT Hub Average 345 kV Hub’ Settlement Point Price in Day-Ahead Market ($/MWh) | 29.80 | 28.90 | 55.19 | 30.57
Load-Weighted Average ‘ERCOT Hub Average 345 kV Hub’ Settlement Point Price in Real-Time ($/MWh) | 28.12 | 28.10 | 50.83 | 26.57
Tab 5
ERCOT Public

## Slide 8: Operational Performance Measures – September 2012
Performance Measure | Target Met | Further Information
Retail Transaction Performance (Target 98%) | Yes | Retail transaction processing performance was at 100%
Settlements Performance (Target 99%) | No | 100% timely statement and invoice posting To note: Data errors for 9/18/12 prompted a Real-Time Resettlement of the Operating Day which posted one day after the Real-Time Initial Settlement. Data errors were the result of a missed step in a non-standard, partial system failover and resulted in settlement using energy trade and DC Tie import quantities that were 4x the actual quantities. In follow-up, failover procedures have been updated and data integration has implemented additional error detection logic.
Tab 5
ERCOT Public

## Slide 9: Operational Performance Measures – October 2012
Performance Measure | Target Met | Further Information
Retail Transaction Performance (Target 98%) | Yes | Retail transaction processing performance was at 100%
Settlements Performance (Target 99%) | Yes | 100% timely statement and invoice posting
Tab 5
ERCOT Public

## Slide 10: Operational Dashboard – September 2012
Metric | Trending as Expected | Further Information
Day-Ahead Schedule | Yes | Normal level of market activity and liquidity Loads appear to have hedged against exposure to Real-Time prices
Day-Ahead Electricity And Ancillary Service Hourly Average Prices | Yes | Hourly average prices correctly reflect the opportunity cost of energy
Day-Ahead vs Real-Time Load Zone Settlement Point Price (Hourly Average) | Yes | Day-Ahead & Real-Time prices for different Load Zones reflect relative transmission congestion
Day-Ahead vs Real-Time Trading Hub Settlement Point Price (Hourly Average) | Yes | The average energy price across the system reflects marginal offers and scarcity pricing impacts Higher average Day-Ahead energy prices during peak hours reflect the risk premium between Day-Ahead & Real-Time
Day-Ahead Reliability Unit (DRUC) Commitment Monthly Summary | Yes | Capacity committed by the DRUC process indicates the level of out of market activity needed Day-Ahead to maintain reliability No resource was committed in DRUC in this month
Tab 5
ERCOT Public

## Slide 11: Operational Dashboard – October 2012
Metric | Trending as Expected | Further Information
Day-Ahead Schedule | Yes | Normal level of market activity and liquidity Loads appear to have hedged against exposure to Real-Time prices
Day-Ahead Electricity And Ancillary Service Hourly Average Prices | Yes | Hourly average prices correctly reflect the opportunity cost of energy
Day-Ahead vs Real-Time Load Zone Settlement Point Price (Hourly Average) | Yes | Day-Ahead & Real-Time prices for different Load Zones reflect relative transmission congestion Day-Ahead & Real-Time prices for Load Zone West were higher than other zones due to planned outages and low wind generation in far west
Day-Ahead vs Real-Time Trading Hub Settlement Point Price (Hourly Average) | Yes | The average energy price across the system reflects marginal offers and scarcity pricing impacts Higher average Day-Ahead energy prices during peak hours reflect the risk premium between Day-Ahead & Real-Time
Day-Ahead Reliability Unit (DRUC) Commitment Monthly Summary | Yes | Capacity committed by the DRUC process indicates the level of out of market activity needed Day-Ahead to maintain reliability Three resources were committed in DRUC in this month to provide voltage support
Tab 5
ERCOT Public

## Slide 12: Operational Dashboard – September 2012
Metric | Trending as Expected | Further Information
Hourly Reliability Unit Commitment (HRUC) Monthly Summary | Yes | Capacity committed by the HRUC process indicates the level of out of market activity needed during the Operating Day to maintain reliability Two resources were committed to resolve congestion and two to provide voltage support in this month
Supplemental Ancillary Service Market Monthly Summary | Yes | Normal trend indicates that deliverability was not a major concern
Non-Spinning Reserve Service Deployment | Yes | Offline Non-Spin was not deployed to solve local congestion
Congestion Revenue Rights Price Convergence | No | The total CRR value was about 1.6 times of the total CRR cost. CRRs were valued much higher in Day Ahead due to combination of outages, low wind and high load.
Tab 5
ERCOT Public

## Slide 13: Operational Dashboard – October 2012
Metric | Trending as Expected | Further Information
Hourly Reliability Unit Commitment (HRUC) Monthly Summary | Yes | Capacity committed by the HRUC process indicates the level of out of market activity needed during the Operating Day to maintain reliability One to provide more capacity, two to provide voltage support and one for both voltage support as well as congestion management in this month
Supplemental Ancillary Service Market Monthly Summary | Yes | Normal trend indicates that deliverability was not a major concern
Non-Spinning Reserve Service Deployment | Yes | Offline Non-Spin was not deployed to solve local congestion
Congestion Revenue Rights Price Convergence | No | The total CRR value was about 2.2 times of the total CRR cost. CRRs were valued much higher in Day Ahead mainly due to combination of outages in west and north area and low wind in west area.
Tab 5
ERCOT Public

## Slide 14: Operational Dashboard – September 2012
Metric | Trending as Expected | Further Information
Retail Transactions | Yes | Seasonal variations in transaction volumes trending as expected
Advanced Metering | Yes | 91% of ERCOT load settled with 15-minute interval data. 5.7M Advanced Metering System (AMS) Electric Service Identifier (ESIID)s included in settlement at month end
Settlement Dollars | Yes | At month end, the daily average settlement dollars collected were $11.39M, which is down from August 2012, but comparable to September 2011.
Revenue Neutrality | Yes | At month end, Revenue Neutrality was a charge of $10.29M. This value is relatively flat compared to the previous month, and is down from the $13.6M charge in September of 2011.
Market-Based Uplift to Load | Yes | At month end, the market-based uplift to load was a $2.36M credit to load, compared to a charge of $3.87M in August 2012 and a charge of $5.95M in September 2011.
Tab 5
ERCOT Public

## Slide 15: Operational Dashboard – October 2012
Metric | Trending as Expected | Further Information
Retail Transactions | Yes | Seasonal variations in transaction volumes trending as expected
Advanced Metering | Yes | 92% of ERCOT load settled with 15-minute interval data. 5.8M Advanced Metering System (AMS) Electric Service Identifier (ESIID)s included in settlement as of 10/24/12*
Settlement Dollars | Yes | As of settlement of Operating Day 10/23/12*, the daily average settlement dollars are trending to be near $9M, which is down from $11.39 September and expected to be slightly higher than October 2011.*
Revenue Neutrality | Yes | As of settlement of Operating Day 10/23/12*, Revenue Neutrality uplift is trending as a charge of nearly $2.7M, which is down substantially from previous months and similar to October 2011.
Market-Based Uplift to Load | Yes | As of settlement of Operating Day 10/23/12*, the market-based uplift to load is trending as a charge of over $2M, which is an increase from September 2012 and comparable to October 2011.
* For full month detail refer to the Monthly Operational Overview.
Tab 5
ERCOT Public

## Slide 16: Market Enhancements Under Consideration
Enhancement | Further Information
Evaluating market design improvement proposals | Ongoing discussions with stakeholders on Hour-Ahead Market Real-Time Commitment and Dispatch Competitive Constraint Test design improvements Over mitigation in Real Time Market Price reversal during ERS deployments
Evaluating Pilot Project Feasibility | Developing a governing document for a Fast-Responding Regulation Service (FRRS) pilot FRRS pilot up for approval at November Board meeting
NPRR 351 (Future Indicative Prices) | Analyzing performance of the future indicative prices that are currently being posted by ERCOT Working with Market Participants to improve the quality of future indicative prices
Tab 5
ERCOT Public

## Slide 17: Major Project Highlights
Project | Trending as Expected | Further Information
SCR760 – Recommended Changes Needed for Information Model Manager and Topology Processor for Planning Models | Yes | Making progress with efforts to deliver final enhancements of SCR760 suite. Currently working with vendor to finalize the estimates and proposal for SCR760-1 and SCR760-6, the final two enhancements. Schedule and budget on track, with a target release to production by end of June 2013.
EMS Upgrade – Upgrade EMS and OTS from ALSTOM EMP 2.3 to EMP 3.0 | Yes | Project progressing as planned with code comparison activities between ALSTOM base product and ERCOT production version. Outage Training Simulator comparison complete, other major network applications at 40% and on track to deliver in January 2013. Comparison results will be used for detailed planning activities scheduled to begin in February 2013.
Oracle 11g Upgrade – Upgrade Oracle databases and related tools that support ERCOT’s application portfolio from Oracle 10g to Oracle 11g. | Yes | Project tracking to schedule and budget with several production upgrades completed in October. The foundational components for monitoring, backups, and data replication have been completed and specific setup scheduled with each upgrade.
NPRR347/400 – Combine the DAM and the Real-Time Market Invoices into a single daily Settlement Invoice; Eliminate Unsecured Credit for CRR Auctions and for Future Credit Exposure (FCE); Eliminate netting of FCE with Current Credit Exposure (CCE) | Yes | Project on schedule for early November go-live; overall budget on track. Currently completing final integration testing, which included testing of credit reports with select Counter Parties.
Settlement System Upgrade – Replace proprietary code, data structures and tools with an ERCOT supported solution | No | Earned value analysis indicates potential cost-overrun attributable to schedule delay, a complex design, and temporary resource assignments to other higher priority projects. Management engaged to review recovery options and implement corrective actions intended to deliver project within existing schedule and budget.
CRR Upgrade – Upgrades the CRR clearing engine and associated components to Linux in order to provide measurable performance improvements in the annual auction | No | Defects discovered in vendor package, along with re-allocation of resources to higher priority annual auction activities, eliminated opportunity to run new functionality in parallel with October’s annual auction and will delay the planned launch. The team is currently working with vendor to confirm patch release dates in order to assess schedule and budget impacts.
ERCOT Public
Tab 5
Notes: <number>

## Slide 18: Projects with Red or Yellow Status
Project | Trending as Expected | Further Information
ERCOT Website Enhancements | No | Development and testing activities have been delayed due to user interface (UI) / functional design clarifications currently in progress. Delay in schedule potentially impacting go-live target in Dec 2012 - Jan 2013; team is investigating schedule options and confirming impacts. Will also require budget increase for additional development and testing resources and in support of anticipated schedule extension.
ITRON Load Forecast | No | Launch pushed from October (R5) to December (R6) release due to delays in schedule. Additional time needed to address requirements and design, which delayed development effort and subsequent go-live date. Schedule also impacted by loss of key team resource, which has not been replaced. No impact to budget.
NPRR322 – Real-Time PTP Option Modeling | No | Development forecast was lower than the actual effort required to deliver code changes, resulting in a budget increase. Schedule remains intact for December (R6) release.
ERCOT Public
Tab 5
Notes: <number>

## Slide 19: Appendix
ERCOT Public
The ERCOT Monthly Operational Overview will be posted to (http://www.ercot.com/committees/board/) on the 15th day of the following month
Tab 5