## Slide 1: SSWG 13DSB Case Preparation Extraordinary Dispatch
ROS Meeting
November 8th, 2012

## Slide 2: SSWG Procedure Manual Excerpt
<number>
4.3.3.1 Extraordinary Dispatch Conditions
On occasion, the total load plus the spinning reserve indicated above in later year cases can exceed the amount of available generation due to load forecasts in later year cases. SSWG base cases typically model load at individual coincident TSP peaks instead of at the ERCOT coincident system peak. When such a condition is encountered in future cases, ERCOT may increase generation resources by taking the indicated action, or adding generation, in the following order:
DC ties dispatched to increase transfers into ERCOT to the full capacity of the DC ties.
Increase NOIE generation with prior NOIE consent
Mothballed units that have not announced their return to service. The methodology for this procedure is detailed below.
Ignore spinning reserve.
Add publicly announced plants without interconnect agreements.
Black start Units
Add generation resources at the sites of retired units.
Notes: <number>

## Slide 3: 13DSB Case Implementation
<number>
13DSB’s 14SUM1, 15SUM1 and 16SUM1 Cases:
  Steps 1 through 4 were employed.
  Varying need for mothballed units.
13DSB 16MIN Case:
  No extraordinary dispatch was required.
13DSB 17SUM1 Case:
  Steps 1 through 4 were employed.
  Mothballed units were fully dispatched.
  One unit with rolling service date amendments was fully dispatched.
13DSB 18SUM1 Case:
Steps 1 through 4 were employed.
Multiple units with rolling service date amendments were dispatched.
*Summarized Implementation from ‘Extraordinary Dispatch’ Document
(Filed on POI Website)
Notes: <number>

## Slide 4: Pending PGRRs (2013 Case-Building)
<number>
PGRR018: Additional Prerequisites for Modeling New Generation:
…
Financial Commitment and Notice to Proceed;
ERCOT Notification of Requisite Air Permits; and
Demonstrated Rights to Sufficient Water
PGRRxxx: SSWG 6-Year Case
Protocol and Planning Guide language is under PLWG review for inclusion of a 6th Year-Out case into SSWG’s DSB cases
14DSB Cases: Will include 2020 Case and Load Forecast
*Both of these PGRRs are anticipated to exacerbate the issue of limited generation availability!
Notes: <number>