Options for recovering actual fuel costs in Resource’s offer caps:

Currently all generators receive an increase in the price of fuel via the Value of X (VOX).  The VOX increases the start-up and minimum energy fuel rate, which is equivalent to increasing the fuel price [Cost = fuel rate * fuel price*(1+VOX)].  Recently, the value of VOX has been fluctuating around 17%, but in the past it has reached as high as 20% or more.  Effectively, this implies that generator’s start-up and min energy costs are been calculated at 17-20% higher than FIP/FOP.  Hence, this increase should help recover differences between spot price of fuel and the index price as well as transportation costs and fees.  However, it appears that for some generators the total fuel costs may surpass the value of the index fuel price plus the VOX.  This is may be true in particularly for solid fuel generators that must transport coal from other states, thus incurring significant transportation costs.  And since the 3PO generator offers must be submitted in terms of FIP or FOP, a coal fire-Resource would submit offers based on gas (around $3/MMBtu) since it’s not able to offer its costs based on the solid fuel price ($1.5/MMBtu).  And although the cost of FIP is almost twice as high as the index price for coal, it appears that transportation costs increase the price of solid fuels much higher than that of natural gas.

The VOX is calculated as $0.5/AVGFIP, and as the average value of the price of fuel (AVGFIP) decreases, the VOX increases.  The VOX currently does not apply to the Mitigated Offer Cap (MOC), although the recently approved NPRR 485 allows for a fuel adder to be incorporated at the MOC for all resources.  However, until there is a system change and an approved proposal for including the fuel adder that is different from VOX and specific to individual Resources for all levels of generation (start-up, Min Energy and MOC), allocating a fuel adder, for non-QSGRs, different from VOX is not possible.

The following are alternatives for creating fuel adder to resource’s costs:

Option 1:  Keep the current VOX methodology

Advantages

- No system change or staff impact

- Currently all Resource’s start-up and min costs include a fuel adder of approximately 17% (VOX) of FIP

- QSGRs may include their actual fuel adder (QSVOX) at the MOC

Disadvantages

- Non-QSGRs do not receive a fuel cost adder (VOX) at their MOC

- Existing VOX values may not be high enough

Option 2:  Change current $0.50 value in VOX to a different number (i.e. $1.00 or $0.25)

Advantages

- Minimal system change and no staff impact

- Could help recover the actual cost of fuel for some generators

Disadvantages

- Increases in VOX may allow Resources to recover higher costs than what they actually paid for fuel

- Updated VOX values may not be high enough for some type of generators (i.e. coal-fired Resources)

- If fuel prices (i.e. AVGFIP) increase, the fuel adder (VOX) may not be sufficient to recover actual costs.

- If fuel prices (i.e. AVGFIP) decrease, the fuel adder (VOX) may over -compensate for actual costs.

- Non-QSGRs do not receive a fuel cost adder (VOX) at their MOC

Option 3:  Change current $0.50 value in VOX with a variable number that would result in a fixed (or nearly fixed) number for VOX.  For example, if market wants to ensure that VOX is, on average, say 20%, then the $0.5 adder would need to change with changes to AVGFIP.

Advantages

- Minimal system change and no staff impact

- Could help recover the actual cost of fuel

Note:  Market would have to agree on the frequency ERCOT would have to change the variable (i.e. $0.5) to keep up with changes in FIP.   One possible solution would be to change the variable adder on a monthly basis based on the AVGFIP value.  This would be easy to implement

Disadvantages

- Increases in VOX may allow Resources to recover higher costs than what they actually paid for fuel

- Updated VOX values may not be high enough or too high

- Market would have to agree on the frequency ERCOT would have to change the variable (i.e. $0.5) to keep up with changes in FIP.

- Non-QSGRs do not receive a fuel cost adder (VOX) at their MOC

Option 4:  Make VOX a fixed number, say 10% - 20% and applicable to all Resources for Start-up and min energy costs.

Advantages

- System change required but no staff impact

- Could help recover the actual cost of fuel

Disadvantages

- Increases in VOX may allow Resources to recover higher costs than what they actually paid for fuel

- Updated VOX values may not be high enough (i.e. coal fired units) or too high, depending on chosen VOX value.

- Non-QSGRs do not receive a fuel cost adder (VOX) at their MOC but could be implemented.

Option 5:  Replace VOX with actual Resource-specific fuel cost adder (VOXR), where the subscript “R” represents individual generators.

Advantages

- Potentially more accurate estimate of actual Resource costs

- Could help reduce overpayment to generators whose costs are higher than current FIP + VOX values, if they are forced to file their actual fuel costs

Disadvantages

- Potentially much higher system impact than other options

- Significant impact to staff to review fuel costs for all generators.

- May require a significant amount of time to review all generator’s fuel costs

- Will require an implementation plan to ensure all fuel costs are reviewed

Option 6:  Same as Option 5, but only applicable to solid fuel Resources such as coal 	 fired units.   Replace VOX with actual Resource-specific fuel cost adder (VOXR), where the subscript “R” represents individual generators.

Advantages

- Allows coal-fired units to recover all of their fuel costs

Disadvantages

- Will have system impact

- Impact to staff to review fuel costs for coal-fired generators.