## Slide 1: Reliability and Operations Subcommittee Report
01/03/2013

## Slide 2: Credible Single Contingency for Transmission Planning
(1) A single facility, comprised of transmission line, auto transformer, or other associated pieces of equipment. This includes multiple equipment Outaged or interrupted during a single fault (SFME).
(2) The Forced Outage of a DCKT in excess of 0.5 miles in length (either without a fault or subsequent to a normally-cleared non-three-phase fault) with all other facilities normal.
(3) Any Generation Resource:
  (a) A combined-cycle facility shall be considered a single Generation Resource; or
  (b) Each unit of a combined-cycle facility will be considered a single Generation Resource if the combustion turbine and the steam turbine can operate separately, as stated in the Resource registration on the Market Information System (MIS) Public Area.

## Slide 3: Credible Single Contingency for Transmission Planning
(4) With any single Generation Resource unavailable, and with any other generation preemptively redispatched, the contingency loss of a single Transmission Facility (either without a fault or subsequent to a normally-cleared non-three-phase fault) with all other facilities normal.
(5) Single contingency conditions defined in North American Electric Reliability Corporation (NERC) Reliability Standards and any subsequent revisions.

## Slide 4: Transmission Facilities
(1) Power lines, substations, and associated facilities, operated at 60 kV or above, including radial lines operated at or above 60 kV;
(2) Substation facilities on the high voltage side of the transformer, in a substation where power is transformed from a voltage higher than 60 kV to a voltage lower than 60 kV (DISTRIBUTION SUBSTATION) or is transformed from a voltage lower than 60 kV to a voltage higher than 60 Kv (GENERATION SWITCHYARD); and
(3) The direct current interconnections between ERCOT and the Southwest Power Pool or Comision Federal de Electricidad (CFE).

## Slide 5: PLWG Directive
Continue efforts to reformat the Transmission Planning Criteria in Section 4 of the Planning Guide:
Credible Single Contingency
  Eliminate the use of Credible Single Contingency for Transmission Planning by explicitly stating system conditions, contingencies and performance requirements in the Planning Guide; or
  Modify the definition to accurately state the contingencies. Consider renaming the defined term from Credible Single Contingency… to Planning Contingencies.
Structure the criteria such that it is clearly understood and can easily be modified to incorporate ROS-directed OPSTF Issues.
Only substantive changes to reflect current practices should be included.

## Slide 6
Unopposed Recommendations for Approval
PGRR024, Clarify Planning Assumptions and Performance Criteria
  Clarifies assumptions allowed for planning studies and planning performance criteria.
  Better reflects current planning practices.
  Simplifies the format to more efficiently incorporate future ERCOT-specific criteria additions.